Secure Content switch

by

Ganesh Godavari

Post Graduation Diploma in MISCA 1999

Bachelor of Science 1997

A thesis submitted to the Faculty of Graduate School of the

University of Colorado at Colorado Springs

in partial fulfillment of the

requirements for the degree of

Master of Science

Department of Computer Science

2002

( Copyright By Ganesh Godavari 2002

All Rights Reserved

This thesis for the Master of Science degree by

Ganesh Godavari

has been approved for the

Department of Computer Science

By

_______________________________________________________

Advisor: C. Edward Chow

_______________________________________________________

Jugal K. Kalita

_______________________________________________________

Charles Shub

Date _____________

Ganesh Kumar Godavari

Secure Content switch

Thesis directed by Professor C. Edward Chow

Content switches examine the content of incoming requests in order to make decisions about routing them to a server among a cluster of servers. Security has become a major concern in today’s networks. This report describes the enhancement of security in a content switch using Transport Layer Security and Secure Socket Layer Protocols. OPENSSL provides extremely secure encryption and decryption capabilities that I am utilizing for handling encrypted HTTP requests. The content switch can route requests based on URL, IP address and text or XML content in application layer payload. Some of the other features of my secure content switch include session reusability for efficient and faster processing of secure HTTP requests.

CONTENTS

INTRODUCTION	1

1.1. Secure Content Switch	2

1.2. Security Approaches For Web Traffic	3

1.3. Tradeoff between Layer 3 and Layer 4 security	5

1.4. Some content switches that support security	6

1.5. Focus of Thesis	7

1.6. Analysis of Layer 4 Protocol (TLS Ver 1)	8

1.6.1. Goals of TLS protocol	8

1.6.2. TLS Sessions and Connections	9

1.6.3. TLS LAYERS	11

1.6.3.1. TLS Handshake Protocol	12

1.6.3.2. TLS Record protocol	15

CHAPTER 2	18

SECURE CONTENT SWITCH	18

2.1. SSL Transactions [  ]	19

2.2.  OpenSSL: The Open Source toolkit for SSL/TLS [ ]	21

2.3. Software architecture of secure content switch	22

2.3.1. Secure Content Switch Child Module.	23

2.4. Dynamic Forking SSL SECURE CONTENT SWITCH	27

2.5. Pre-Forking SSL SECURE CONTENT SWITCH	33

2.6. RuleModule	39-

Performance Results	42

3.1. Performance Test 1	44

Dynamic Forking vs. Pre-forking secure content switch	45

3.2. Performance Test 2	46

3.3. Performance Test 3	48

3.4. Performance Test 4	51

3.5. Performance Test 5	54

3.6. Performance Test 6	56

Remote rule module vs. local rule module	57

3.7. Performance Test 7	57

Chapter 4	60

Conclusion and future work	60

Appendix A	63

A.1. Installing of Linux Application Level Content switch	63

A.1.1.  Install Openssl	63

A.1.2.	Install SSL Proxies for Content switch	63

A.1.3.    Configure secure content switch for content switch	64

A.2.  Configure LCS routing rules	67

A.3. Compile the content switch code	69

APPENDIX B	71

WebBench [ ]	71

FIGURES

Figure 1.1 relative Location of Security Facilities in the TCP/IP Protocol Stack	3

Figure 1.2 operations of the TLS Handshake Protocol	11

Figure 1.3 showing the operations of a TLS Record Protocol	14

Figure 2.1 shows the location of SSL in the OSI model	17

Figure 2.2 illustrates the steps taken during an SSL negotiation	17

Figure 2.3 Architecture of secure content switch	20

Figure 2.4 showing the flow of control in a Dynamic forking secure content switch	26

Figure 2.5 showing the flow of control in a Pre-forking secure content switch	31

Figure 2.6 showing the flow of control in a Rule Module	36

Figure 3.1 showing the block diagram of the secure content switch test bed	38

Figure 3.2 showing the request/sec of different types of secure content switch	43

Figure 3.3 showing the request/sec of different types of secure content switch	45

Figure 3.4 showing the block diagram of the secure content switch test bed	46

Figure 3.5 showing the Request / Second of Dynamic Forking secure content switch	48

Figure 3.6 showing the Request/sec of dynamic forking non-secure content switch	49

Figure 3.7 showing the Request/sec of secure content switch with local rule module	51

Figure 3.8 showing the Request/sec of secure content switch with remote rule module	52

Figure 3.9 showing the Request/sec of secure content switch in local node problem	54

TABLES

Table 3.1 Configuration of machines used in performance tests	39

Table 3.2 showing the request/sec of different types of secure content switch	40

Table 3.3 showing the request/sec of different types of secure content switch	42

Table 3.4 showing the request/sec of different types of secure content switch	44

Table 3.5 showing the request/sec of different types of secure content switch	46

Table 3.6 showing the Request / Second of Dynamic Forking secure content switch	47

Table 3.7 showing the request/sec of dynamic forking non-secure content switch 	49

Table 3.8 showing the Request/sec of secure content switch with local rule module	50

Table 3.9 showing the Request/sec of secure content switch with remote rule module	52

Table 3.10 showing the Request/sec of secure content switch with remote rule module	53

CHAPTER 1

# INTRODUCTION

The explosion of the Internet from a small network of known individuals to a huge, heterogeneous anonymous network has brought several troubles in its wake. Right from the case of a mail account password being sniffed and acquired to credit card numbers and other confidential business data being observed, attacks can occur on transmitted information in many ways. The number of commercial transactions and private data transmission that occur and the ability of malicious elements to observe and manipulate data anonymously has necessitated the growth of security measures to protect Internet users. A need to have standard security protocols that are platform and network type independent and easily implementable, usable and secure was felt.

Along with security another major issue is handling of the large volumes of data present in today’s networks. Many approaches have been devised in order to provide a solution to this problem. One solution to reduce the load is to have a paid subscription to one of the Content Delivery Network (CDN) providers such as Akamai [1], Speedera [2] and Digital Island [3]. Another approach is to distribute the large volume of requests among a group of servers where a master controller, that can be a dedicated host or a process, first receives the requests and delegates it to one of a group of servers for processing. A content switch (CS) [4] is such a load balancing system that distributes load based on the content of the received requests. A Web-switch is a content switch that distributes load based on Web requests.

## 1.1. Secure Content Switch

Consider the case of an e-commerce site with a large amount of traffic. The users who are accessing the site may be performing various functions like browsing, signing in or doing some profitable activity like purchasing. It makes good business sense to provide better and faster access to paying customers rather than casual surfers. One way of doing this is to provide some kind of preferential treatment like routing them to faster servers. This segregation implies that requests are routed to different servers based on their content. This kind of routing based on request content cannot be achieved by traditional layer4 and below switches, which route requests based on request characteristics like portno, or IP address, but not on the content of the request. A better approach in this direction would be to develop a mechanism, which can route request based on content, in other words, a content based switch. Some of the other functions that a content switch can be used for are:

- Load Balancing: As a Load Balancer, a content switch can segregate incoming requests based on the HTTP meta header, URL or even the application layer payload and route them to the back end servers in the server cluster.

- Firewall: As a firewall, a content switch can either allow or reject requests based on their content or their IP address.

- Email Filtering:  a content switch can function as an efficient spam guard or work as an anti virus device by verifying the sender and content of emails.

E-commerce transactions normally involve the transfer of sensitive or private data like personal information or credit card numbers, which are liable to active or passive attacks during transmission.

## 1.2. Security Approaches For Web Traffic [5]

There are several approaches to provide Web security. The approaches are similar in the services they provide and, to some extent, in the mechanisms that they use, but they differ with respect to their scope of applicability and their relative location within the TCP/IP protocol stack.

(a) Layer3/Network Security		   (b) Transport/Layer4 Security

Figure 1.1 Relative Locations of Security Facilities in the TCP/IP Protocol Stack

One way to provide Web security is to use IP Security or IPSEC [6] as it is generally called. Figure 1.1.a shows its location in the TCP/IP protocol stack. The advantage of using IPSec is that it is transparent to end users and applications and provides a general-purpose solution. Further, IPSec includes a filtering capability so that only selected traffic need incur the overhead of IPSec processing.

Another relatively general-purpose solution is to implement security just above TCP. Figure 1.1.b shows its location in the TCP/IP protocol stack. The foremost example of this approach is the Secure Sockets Layer (SSL) [7] and the follow-on Internet standard of SSL known as Transport Layer Security (TLS) [8]. At this level, there are two implementation choices. For full generality, SSL (or TLS) could be provided as part of the underlying protocol suite and therefore be transparent to applications. Alternatively, SSL can be embedded in specific packages. For example, Netscape [9] and Microsoft Explorer [10] browsers come equipped with SSL, and most Web servers have implemented the protocol.

The goal of SSL was to deploy something totally at the user level, without needing to change the operating systems, whereas the goal of IPSec was to deploy something within the operating system and not require changes to the applications. Since everything from TCP down is generally implemented in the operating system, SSL is implemented as a user level process that calls TCP. IPSec is implemented in layer 3, which means it considers everything above layer 3 as data, including the TCP header. The philosophy behind IPSec is that if only the operating system needed to change, then by deploying an IPSec-enhanced operating system all the applications would automatically benefit from IPSec’s encryption and integrity protection services. It also provides a centralized control.

## 1.3. Tradeoff between Layer 3 and Layer 4 security

The following is a scenario where security provided by SSL can be breached.

Since TCP will not be participating in the cryptography, it is possible for an intruder to intercept packets and send some malicious data as the next packet with modified sequence number into the packet stream. TCP protocol entity at the receiving end will acknowledge such packet and send it up to TLS/SSL protocol entity, which will discard it because the integrity check will indicate the packet is bogus. When the real segment arrives, the TCP protocol entity at the receiving end will assume that it is a duplicate data, since it has already received a TCP segment with the same sequence number.

IPSEC on the other hand can provide protection on TCP header and data. So in theory, IPSec’s approach of cryptographically protecting each packet independently is a better approach.

Meanwhile if only the operating system changes, and the applications and the IPSEC Application Program Interface (API) to the applications do not change, then the power of IPSec cannot be fully utilized. The IPSEC API just tells the application what IP address is on a particular connection. It can’t inform the application of which user has been authenticated. That means that even if users have public keys and certificates, and IPSec authenticates them, there is no way for it to inform the application. Most likely after IPSec establishes an encrypted tunnel, the user will have to type a name and password to authenticate to the application. So it is important that eventually the IPSEC APIs and applications are changed so that IPSec can inform the application of something more than the IP address of the tunnel endpoint, but until they do, IPSec accomplishes the following:

- Encrypt traffic between the two nodes.

- As with firewalls, IPSec can access a policy database that specifies which IP addresses are allowed to talk to which other IP addresses.

- Some applications do authentication based on IP addresses, and the IP address from which information is received is passed up to the application. IPSec authentication is more secure  because the IPSEC endpoint authenticates the connection based on source IP address and keys in the IPSEC payload. The application would be justified in trusting the IP address asserted by the lower layer as the source.

## 1.4. Some content switches that support security [11]

- Alteon iSD-SSL Accelerator [12]:  The Alteon iSD-SSL accelerator works with an Alteon Web switch to intelligently speed secure  e-Commerce transactions by offloading Secure  Sockets Layer (SSL) processing from local servers without imposing delays on other traffic in the same data path.

- F5 Networks Big-IP Controller 3.1 [13]: F5 has long been a leader in the Internet Traffic Management space. It has an advanced web switching logic. Big-IP combines a strong, traditional load-balancing feature set with SSL acceleration ability. It extracts HTTP header information from the request to make traffic management decisions.

- Foundry Networks ServerIronXL with Internet IronWare 7.0 [14]: Foundry equips its ServerIronXL with a strong Layer 2 and Layer 3 switching and Layer 5/7 load-balancing based on cookies and SSL session IDs.

## 1.5. Focus of Thesis

This thesis work is focused on adding security to content switch [ ]. TLS/SSL is a good choice for securing connections in situations where user or server authentication is needed or where IPSec is not readily available. The major advantage of using TLS/SSL is that it is platform and application independent. Moreover most of the web browsers support SSL and TLS based connections. This makes it an ideal choice for handling the security aspect of content switch at application level rather than at the lower layers of the TCP/IP. Before going into the details of the implementation of a secure Content switch the following section talks about the working of the TLS protocol.

## 1.6. Analysis of Layer 4 Protocol (TLS Ver 1) [15]

The Transport Layer Security (TLS) protocol is based on and is similar to SSL 3.0 and is a draft standard of the IETF. The TLS working group’s first RFC (Request For Comment 2246) discusses the TLS protocol in detail. Transport Layer Security protocol makes use of a reliable transport layer, such as TCP. It provides security to any application protocol layered on top of it.

As with SSL, TLS is application protocol independent and uses a similar range of ciphers. The TLS standard, however, leaves the decisions on how to initiate TLS handshaking and how to interpret the authentication certificates to the judgment of the designers and implementers of the protocols that run on top.

### 1.6.1. Goals of TLS protocol

The goals of the TLS protocol are cryptographic security, interoperability, and extensibility, in that order of priority.

- Security: TLS protocol makes use of many cryptographic algorithms to encrypt data (i.e., algorithms to encipher data into a secret code), so that no one except the communicating parties can retrieve the contents of the data.

- Interoperability: i.e., facilitate exchange of security parameters between applications without knowledge of one another’s code.

- Extensibility:  i.e., TLS provides a framework into which new and improved asymmetric and other encryption methods can be introduced as they become available

Since cryptographic operations are computation intensive, the TLS protocol caches necessary information required so that efficiency is increased.

### 1.6.2. TLS Sessions and Connections

To provide security in data exchange, TLS creates a TLS session followed by creation of one or more TLS connection(s) between the communicating applications. A TLS connection can be imagined as a transport for providing some application service between any two peers. Technically it is thought of as a peer-to-peer relationship.

TLS session is actually an association between a client and a server. A TLS session can consist of many TLS connections, which share the same security parameters. A TLS session is created using the TLS Handshake protocol. Once a session is established, if a connection between two communicating applications breaks, a new connection can be established without undergoing the procedure of establishing a new session. This avoids the overhead of negotiating new security parameters for each connection.

To identify the session, the server sends a session identifier to the client during initial negotiation. After breaking a connection, the client can use the same session by specifying the session identifier.

There are various parameters, which identify a session

- Session identifier: The server recognizes a session according to this identifier.

- Peer certificate: A certificate is used to authenticate a user. There is a possibility that the person whom we are exchanging information with may not be a legitimate person. To prove legitimacy a user can acquire a digital certificate, which is a signed document, from a universally trusted party called Certificate Authority. A server needs to have a certificate. A client may or may not have a certificate.

- Compression method: The algorithm that will be used to compress data for this particular session.

- Cipher spec:  This specifies the data encryption algorithm that will be used to encrypt data for this session.

- Master secret: This is the 48 byte common key, i.e., a common secret, shared by the client and server.

A connection is defined by the following parameters:

- Server and client random: Random byte sequences that are chosen by the client and server to identify each connection.

- Server write MAC(Message Authentication Code) secret: A key (or secret) used to authenticate messages sent by the server.

- Client write MAC secret: A key used to authenticate messages sent by the client.

- Server write key: An encryption key used by the server to encrypt data sent to the client

- Client write key: An encryption key used by the client to encrypt data sent to the server

- Sequence number: A number to identify messages for a connection.

The use of these parameters would be explained later in the discussion.

### 1.6.3. TLS layers

TLS protocol stack consists of TLS Record protocol and TLS Handshake protocol. The TLS Record protocol provides security services to the higher-level protocols. The higher-level protocols, such as TLS Change Cipherspec protocol and TLS Alert protocol and the TLS Handshake protocol, are used for management of TLS exchanges. The TLS Handshake protocol is used to exchange authentication information and to negotiate data encryption techniques to be used between the communicating applications before the actual data is exchanged. TLS Handshake Protocol consists of a suite of three sub-protocols, which are used to allow peers to agree upon security parameters for the record layer, authenticate themselves, instantiate negotiated security parameters, and report error conditions to each other. They are TLS Change Cipherspec protocol and TLS Alert protocol and the TLS Handshake protocol itself.

The TLS Change Cipherspec protocol is used to change the encryption algorithm and other security parameters. The TLS Alert protocol is applied to exchange error messages during an ongoing communication.

#### 1.6.3.1. TLS handshake protocol

This is the most important and complex protocol of the TLS protocol stack. It operates on top of the TLS Record protocol. This protocol allows both the client and server to authenticate each other.

## Figure 1.2 - operations of the TLS Handshake Protocol

Also this protocol decides as to what encryption algorithm the client and the server will use to encrypt data. Also what keys will be used are decided using this protocol. Since all important key exchange information is dealt in using this protocol, this protocol is used before any application data is encrypted and sent. This protocol consists of exchange of multiple messages between the client and the server.

The TLS Handshake protocol can be divided into 4 phases. Figure 1.2 shows the operations of the TLS handshake protocol

Phase I: Exchange protocol version, session-id, cipher suite, compression method.

This phase is used to establish the security parameters between the client and the server. First the client initiates the request for connection. The client sends to the server various security parameters and the server may select one of them. The message sent by the client is known as ClientHello message. The various parameters sent by the client are

- Client version: The version of the TLS protocol with which the client wishes to communicate

- Random: This is a random number generated by the client for that particular session

- Session ID: To identify the session (if zero then a new session is to be created)

- Cipher suites: List of security options supported by the client

- Compression method: List of compression methods supported by the client

Phase II: server certificate phase

In response to the ClientHello message, the server responds with the ServerHello message. Out of the many preferred options sent by the client related to encryption algorithms, key exchange algorithms & compression algorithms, the server selects one of each. The server also sends digital certificate to prove its authenticity. Depending on what encryption algorithms are used, the server may optionally need to send some key exchange parameters. Also for verifying client authenticity, the server may ask for client’s digital certificate.

Phase III: client certificate phase

In this phase, the client checks the server’s validity and sends its own digital certificate, if available. If the client does not have its own digital certificate, it may request the server to provide it with some membership parameters. These parameters can be a password or a pin number, which the server may use to authenticate the client.

Phase IV: CipherSpec Exchange phase

The secure  connection is set up in this phase. After the establishment, the security parameters are passed to the TLS Record layer to affect the current connection. The client and the server also verify that both of them have the same keys used for encryption and authentication process. These keys are generated locally by both using the shared master secret. The following are the four keys generated using the master secret

- Server Write MAC key

- Client Write MAC Key

- Server Write Key

- Client Write Key

#### 1.6.3.2. TLS Record protocol

The TLS Record protocol performs some operations to secure the data. First it takes the application data to be transmitted and fragments it. It then optionally compresses the fragments using the compression method agreed upon during session establishment.  Figure 1.3 shows the Operations of TLS Record Protocol.

The Record protocol then applies a MAC (Message Authentication Code), on the compressed data and generates a checksum, which is appended to the data.  The data is then encrypted using the encryption algorithm agreed upon during session establishment. The receiver recomputes the MAC when the data arrives, in order to verify that data is sent from an authentic source.

Figure 1.3 showing the operations of a TLS Record Protocol

To calculate MAC the master secret is used. The formula for calculating MAC is

HMAC_hash (MAC_write_secret, seq_num || TLSCompressed.type || TLSCompressed.version.|| TLSCompressed.length || TLSCompressed.fragment)  where,

| HMAC_hash | A hash algorithm (agreed upon during session establishment), which maps a message of any length into a fixed length value, which is used to authenticate the message |
| --- | --- |
| ¦¦ | Concatenation |
| MAC_write_secret | Shared master secret |
| seq_num | A unique number identifying each message |
| TLSCompressed.type | Higher level protocol used to compress the fragment |
| TLSCompressed.version | The TLS version number |
| TLSCompressed.length | Length of the compressed fragment |
| TLSCompressed.fragment | If fragmentation occurs then the compressed fragment |

The TLS Record protocol then adds a TLS header to the encrypted data. Finally the data is transmitted to the destination using TCP. At the receiving end, the TLS record protocol is used to retrieve the actual data from the message received.

# CHAPTER 2

## SECURE CONTENT SWITCH

The SSL protocol is a security protocol that sits on top of TCP at the transport layer. In the OSI model, application layer protocols such as HTTP or IMAP handle user application tasks such as displaying Web pages or running email servers. Session layer protocols establish and maintain communications channels. Transport-layer protocols such as TCP and UDP, handle the flow of data between two hosts. Network layer protocols such as IP and ICMP provide hop-by-hop handling of data packets across the network.

SSL operates independently and transparently of other protocols so it will work with any application-layer and any transport-layer protocol. This allows clients and servers to establish secure SSL connections.

An application layer protocol sends unencrypted data to the session layer. TLS/SSL encrypts the data and hands it down to the lower layers. When its peer receives the data at the other end, it passes it up through the layers to the session layer where TLS/SSL decrypts it and hands it to the application layer. Since the client and the server have gone through the key negotiation handshake, the symmetric key used by SSL is the same at both ends.

Figure 2.1 shows the location of SSL in the OSI model

## 2.1. SSL Transactions [16]

To illustrate how SSL works, assume a user wants to make a purchase over the Internet and needs to send a credit card number to a secure Web site.

Figure 2.2 illustrates the steps taken during an SSL negotiation

  - Initially, the request for an SSL session comes from the browser to the Web server.

  - The Web server then sends the browser its digital certificate. The certificate contains information about the server, including the server’s public key.

  - Once the browser has the server’s certificate, the browser verifies that certificate is valid and that the CA is listed in the client’s list of trusted CA’s. The browser also checks the certificates expiration date and the Web server domain name.

  - Once a browser has determined that the server certificate is valid, the browser then generates a 48-byte master secret key. This master secret key is encrypted using server’s public key, and is then sent to the Web server.

  - Upon receiving the master secret from the browser, the Web server then decrypts this master secret key using the server’s private key.

  - As both the browser and the Web server have the same master secret key, they use this master secret to create keys for the encryption and MAC algorithms used in the bulk-data process of SSL. Since both participants used the same master key, they now have the same encryption and MAC keys.

  - As both the browser and Web serve have the same encryption and MAC keys, they use the SSL encryption and authentication algorithms to create an encrypted tunnel. Through this encrypted tunnel, they can now pass data secure ly through the Internet.

Though the authentication and encryption process may seem rather involved, it happens in less than a second. Generally, the user does not even know it is taking place. However, the user will be able to tell when the secure tunnel has been established since most SSL-enabled Web browsers will display a small closed lock at the bottom or top of their screen when the connection is secure. Users can also identify secure Web sites by looking at the Web site address; a secure Web site’s address will begin with https:// rather than the usual http://.

## 2.2.  OpenSSL: The Open Source toolkit for SSL/TLS [17]

OpenSSL is based on the excellent SSLeay [18] library developed by Eric A. Young and Tim J. Hudson. Open Source toolkit implements the Secure Socket Layer (SSL v2/v3) and Transport Layer Security (TLS v1) protocols as well as a full-strength general-purpose cryptography library.

OpenSSL contains two important libraries:

- OpenSSL SSL library implements the Secure Sockets Layer (SSL v2/v3) and Transport Layer Security (TLS v1) protocols.

- OpenSSL CRYPTO library implements a wide range of cryptographic algorithms used in various Internet standards. The services provided by this library are used by the OpenSSL implementations of SSL, TLS and they have also been used to implement SSH [19], OpenPGP [20], and other cryptographic standards.

In addition, the OPENSSL program is a command line tool for using the various cryptography functions of OpenSSL's crypto library from the shell. It can be used for

- Creation of RSA [21], DH [22] and DSA [23] key parameters.

- Creation of X.509 certificates [24] and Certificate Revocation List (CRL).

- Calculation of Message Digests

- Encryption and Decryption with Ciphers.

- SSL/TLS Client and Server Tests.

- Handling of S/MIME signed or encrypted mail

.

## 2.3. Software architecture of secure content switch

The following figure 2.3 shows the architecture of the current design of secure content switch.

Figure 2.3 Architecture of secure content switch

The following steps describe the process of handling secure requests using the secure content switch.

- The web browser makes a request to the secure content switch.

- The dispatcher module in the secure content switch forwards the request to the secure content switch child module. In the dynamic forking version of secure content switch the dispatcher module forks a child process. In the preforking version of secure content switch the dispatcher module forwards the request to a free child.

- The secure content switch child module performs the handshake with the client and reads in the request.

- The secure content switch child module then sends the request to the Rule module, which performs rule matching and returns the name of the server by which the request can be served.

- The real server connects to the web browser through the secure content switch child module (not shown in the picture).

### 2.3.1. Secure Content Switch Child Module.

The major steps involved in the working of OpenSSL are:

- First an SSL_CTX object is created as a framework to establish TLS/SSL enabled connections.

- When a network connection has been created, it can be assigned to an SSL object. After the SSL object has been created using SSL_new, SSL_set_fd or SSL_set_bio can be used to associate the network connection with the object.

- Then the TLS/SSL handshake is performed using SSL_accept or SSL_connect respectively.

- SSL_read and SSL_write are used to read and write data on the TLS/SSL connection.

- SSL_shutdown can be used to shut down the TLS/SSL connection.

Template 2.1 shows how the SSL handshake is performed using Openssl.

Template 2.1

int  server_verify=SSL_VERIFY_NONE;

char    szbuf[BUFSIZ], issuer[256];

struct front_server szclient;

SSL_CTX  *ctx;

SSL_METHOD *method=SSLv23_server_method();

X509 *ca_cert, *client_cert;

FILE *ca_fp=(FILE *) NULL;

SSL_load_error_strings();

OpenSSL_add_ssl_algorithms();

ctx=(SSL_CTX *) SSL_CTX_new(method);

if (ctx == (SSL_CTX *) NULL)     {

fatalError("Unable to create new SSL CTX\n");

goto ExitProcessing;

}

if (!SSL_CTX_load_verify_locations(ctx,ca_file,ca_path))

fatalError("Failed in SSL_CTX_load_verify_locations()!\n");

/*    ** Load Private Key    */

err=SSL_CTX_use_RSAPrivateKey_file(ctx, key_file, SSL_FILETYPE_PEM);

if (err == -1)

{

(void) fprintf(stderr,"Error reading private key\n");

SSL_CTX_free(ctx);

exit(1);

}

Template 2.1 Contd..

/*   ** Load Certificate   */

err=SSL_CTX_use_certificate_file(ctx, cert_file, SSL_FILETYPE_PEM);

if (err == -1)

{

(void) fprintf(stderr,"Error reading certificate\n");

SSL_CTX_free(ctx);

exit(1);

}

/*   ** check if the certificate and private key match   */

err = SSL_CTX_check_private_key(ctx);

if (err == -1)

{

(void) fprintf(stderr,"Error cerificate and private key donot match \n");

SSL_CTX_free(ctx);

exit(1);

}

/*    ** Load randomness    */

if (!RAND_load_file(rand_file,1024*1024))

{

(void) fprintf(stderr,"Unable to load Randomness for generating Entropy :-( \n");

}

/*** read the ca certificate and save the issuer string, we'll compare

** the client's issuer with this one, if they match allow connection

** or zap him

*/

ca_fp=fopen(ca_file,"r");

if (ca_fp == (FILE *) NULL)

fatalError("Failed to open Trusted CA certificate file: %s\n", ca_file);

ca_cert=NULL;

ca_cert=X509_new();

if (!PEM_read_X509(ca_fp,&ca_cert,NULL,NULL))

fatalError("Error reading trusted CA certificate fie: %s\n",ca_file);

X509_NAME_oneline(X509_get_issuer_name(ca_cert),issuer,256);

if (issuer == (char *) NULL)

fatalError("No issuer for trusted CA certificate file!\n");

Template 2.1 Contd..

if (ca_cert != NULL)

X509_free(ca_cert);

(void) fclose(ca_fp);

……………………

/*    ** open the server socket    */

sock_fd=serverSocket((u_short) SERVER_PORT ,1000);

if (sock_fd == -1) {

(void) fprintf(stderr,"Failed to create server\n");

exit(1);

}

g_sock_fd=sock_fd;

………………………

ssl=SSL_new(ctx);

if (ssl == NULL)

fatalError("Failed in SSL_new()!\n");

SSL_set_fd(ssl,sock_fd);

/*   ** clean up the structures     */

SSL_clear(ssl);

SSL_set_session(ssl,NULL);

SSL_set_accept_state(ssl);

/*

** session handling functions

*/

SSL_CTX_flush_sessions(ctx,SSL_SESSION_CACHE_TIMEOUT);

SSL_CTX_sess_set_new_cb(ctx, ssl_callback_NewSessionCacheEntry);

SSL_CTX_sess_set_get_cb(ctx, ssl_callback_GetSessionCacheEntry);

SSL_CTX_sess_set_remove_cb(ctx, ssl_callback_DelSessionCacheEntry);

err=SSL_accept(ssl);

if (SSL_get_error(ssl, err) == SSL_ERROR_ZERO_RETURN)

{

/* case where the connection was closed before any data was transferred    */

Template 2.1 Contd..

(void) fprintf(stderr, "SSL handshake stopped: connection was closed");

goto ExitProcessing;

return 0;

}

else if (ERR_GET_REASON(ERR_peek_error()) == SSL_R_HTTP_REQUEST)

{

/*

** case where OpenSSL has recognized a HTTP request => client speaks plain HTTP

** on our HTTPS       */

(void)fprintf(stderr, "SSL handshake failed: HTTP spoken on HTTPS port; ");

goto ExitProcessing;

return 0;

}

else if (SSL_get_error(ssl, err) == SSL_ERROR_SYSCALL)

{

if (errno > 0)

(void) fprintf(stderr,"SSL handshake interrupted by system "

"[Hint: Stop button pressed in browser?!]\n");

else

(void) fprintf(stderr, "Spurious SSL handshake interrupt"

"[Hint: Usually just one of those OpenSSL confusions!?]\n");

goto ExitProcessing;

return 0;

}

else if (err == -1)

{

fatalError("Error : unknown error in SSL_accept()\n");

goto ExitProcessing;

return 0;

}

## 2.4. Dynamic Forking SSL secure content switch

Figure 2.4 shows the flow of control in the Dynamic forking SSL secure content switch. The steps involved are

- Secure content switch is set to listen for connection requests on port 443. A successful TCP connection results in a valid socket and secure content switch creates a child secure content switch process to handle the request. Secure content switch returns to listen for the next connection request.

- The child secure content switch process negotiates the SSL connection with the client. Secure content switch then performs the SSL handshake with the client. This step involves establishing ciphers to use and providing certificate to the client for server-authentication. As part of the SSL Handshake request, the client may provide a current or previously created SessionID to reuse for the current connection. The Secure content switch manages the SessionID and this will be used as appropriate during the SSL Handshake.

- Secure content switch process receives the request for data and decrypts the data according to the negotiated SSL handshake.

- When the Secure content switch process determines it has fully received an HTTP request, it performs Rule Matching on the request to determine which Real Server can serve the request.

- The secure content switch process establishes a connection with the Real Server and forwards the request in plain HTTP.

- The secure content switch process encrypts the data received from the server and sends the data to the client.

Figure 2.4 showing the flow of control in a Dynamic forking secure content switch

Template 2.2, and 2.3 shows how the child processes are created dynamically. Code in Template 2.2 is from dyna_secure  content switch.c file and Template 2.3 is from include/msock.h file.

Template 2.2

/* open the server socket   */

sock_fd=serverSocket((u_short) SERVER_PORT ,1000);

Template 2.3

int serverSocket(u_short port,int max_server) {

int   dummy=(-1);

int    sock_fd;

u_short     nport;

/* convert port to netword byte word */

nport=htons(port);

sock_fd=getConnection(SOCK_STREAM,nport,&dummy,max_server);

return (sock_fd);

}

/** this function listens on a port and returns connections.

** it forks returns off internally, so the calling function does not  have to worry about that.

** the function will create a new process for every incoming  connection, so in the listening

** process, it will never return. Only hen a connection comes in, and we create a process for it,

** will the function return. THE CALLING FUNCION SHOULD NOT LOOP

*/

int getConnection(int socket_type,u_short port,int *listener,int max_serv) {

struct linger   li;

struct sockaddr_in  address;

int listeningSocket;

int connectedSocket = -1;

int newProcess;

int one = 1;

/* setup internet address information this is used with the bind () call  */

memset((char *) &address,0,sizeof(address));

address.sin_family=AF_INET;

address.sin_port=port;

address.sin_addr.s_addr=htonl(INADDR_ANY);

listeningSocket=socket(AF_INET,socket_type,0);

Template 2.3 Contd..

if (listeningSocket < 0)     {

(void) fprintf (stderr,"Unable to open socket!\n");

perror("socket");

exit (1);

}

if (listener != (int *) NULL)

*listener=listeningSocket;

/*** we will resuse port   */

setsockopt(listeningSocket,SOL_SOCKET,SO_REUSEADDR,(char *) &one,

sizeof(int));

/* we will set keep alive.   */

one=1;

setsockopt(listeningSocket,SOL_SOCKET,SO_KEEPALIVE,(char *) &one,

sizeof(int));

li.l_onoff=1;

li.l_linger=30;

setsockopt(listeningSocket,SOL_SOCKET,SO_LINGER,(char *) &li,

sizeof(struct linger));

if (bind(listeningSocket,(struct sockaddr *) &address, sizeof(address)) < 0)   {

(void) fprintf (stderr,"\nUnable to bind to socket at port: %d\n",

ntohs(port));

(void) fprintf (stderr,"Probably the port is already in use!\n");

(void) fprintf(stderr,"Or you do not have permission to bind!\n");

close(listeningSocket);

exit (1);

}

if (socket_type == SOCK_STREAM)    {

/* queue up max_serv connections before having them automatically rejected */

if (listen(listeningSocket,max_serv) == 0)        {

(void) fprintf(stderr,"\nhttpd listening at port: %d\n",

ntohs(port));

}

else        {

perror("listen()"); }

Template 2.3 Contd..

while (connectedSocket < 0)        {

connectedSocket=accept(listeningSocket,NULL,NULL);

if (connectedSocket < 0)            {

/** either a real error occured or blocking was

** interrupted for some reason. only abort execution

** if a real error occured  */

if (errno != EINTR) {

(void) fprintf (stderr,"unable to accept!\n");

perror("accept");

close (listeningSocket);

exit (1);

}

else

continue; /* don't fork, do the accept again*/

}

newProcess=fork();

if (newProcess < 0)            {

(void) fprintf (stderr,"failed to fork!\n");

perror("fork");

close(connectedSocket);

connectedSocket=(-1);

}

else            {

/** we have a new process (child)     */

if (newProcess == 0)     {

/** this is the new process, close our copy of the socket  */

close(listeningSocket);

*listener=(-1);

/* closed in this process, we are not responsible for it    */

}

else            {

/* this is the main loop. close copy of connected socket, and continue loop */

close (connectedSocket);

connectedSocket=(-1);

}

}

}

return (connectedSocket);

}

else

return (listeningSocket); }

## 2.5. Pre-Forking SSL SECURE CONTENT SWITCH

Figure 2.5 shows the flow of control in the Preforking secure content switch. The steps involved are

- Secure content switch is set to listen for connection requests on port 443.  Secure content switch creates a certain number of child secure content switch processes ahead of time. A successful TCP connection results in a valid socket, which is passed, to one of the process created ahead of time to handle the request. Secure content switch returns to listen for the next connection request.

- The Child Secure content switch process negotiates the SSL connection with the client. Secure content switch then performs the SSL handshake with the client. This step involves establishing ciphers to use and providing certificate to the client for server-authentication. As part of the SSL Handshake request, the client may provide a current or previously created SessionID to reuse for the current connection. The secure content switch process manages the SessionID and this will be used as appropriate during the SSL Handshake.

- Secure content switch process receives the request for data and decrypts the data according to the negotiated SSL handshake.

- When the Secure content switch process determines it has fully received an HTTP request, it performs Rule Matching on the request to determine which Real Server can serve the request.

Figure 2.5 showing the flow of control in a Pre-forking secure content switch

- The Secure content switch process establishes a connection with the Real Server and forwards the request in plain HTTP.

- The Secure content switch process encrypts the data received from the server and sends the data to the client.

Template 2.4 shows how the child processes are created dynamically. Code in Template x is from include/prefork.h file.

Template 2.4

/* create children specified by num */

static int fork_child(int num) 	{

int sv[2];

pid_t  child_pid;

int wanted = num;

while(num--)  {

if(socketpair(AF_UNIX,SOCK_STREAM,0,sv) < 0)  {

fprintf(stderr,"socketpair: %s",strerror(errno));

shutdown_server(0);

}

fcntl(sv[0],F_SETFL,O_NONBLOCK);

fcntl(sv[1],F_SETFL,O_NONBLOCK);

child_pid = fork();

if(child_pid == -1)  {

#ifdef EAGAIN

if(errno == EAGAIN) {

close(sv[0]);

close(sv[1]);

return (wanted - num);

} else {

fprintf(stderr,"fatal fork: %s",strerror(errno));

shutdown_server(0);

}

#else      }

#else

fprintf(stderr,"fatal fork: %s",strerror(errno));

shutdown_server(0);

#endif

} else if(child_pid == 0) {

struct sigaction childsig;

sigemptyset(&childsig.sa_mask);

childsig.sa_flags = 0;

childsig.sa_handler = SIG_DFL;

close(sv[0]);

Template 2.4 Contd..

sigprocmask(SIG_SETMASK,&mask,NULL);

sigaction(SIGTERM,&childsig,NULL);

#ifdef SIGCHLD

#define CHILD SIGCHLD

#elif SIGCLD

#define CHILD SIGCLD

#endif

sigaction(CHILD,&childsig,NULL);

#undef CHILD

child_main(sv[1]);

} else {

close(sv[1]);

add_child_to_list(sv[0],child_pid);

child_num++;

}

}

return wanted;

}

/* central code of the preforking code. */

void child_main(int sockd) {

int length = sizeof(struct sockaddr_in);

char message;

int sockd2;

while(cycle--)  {

message = READY;

if(send_socket(sockd,(char *)&message,sizeof(message)))

_exit(-1);

kill(parent_pid,SIGUSR1);

/*

** critical section

** the child processes need to get a lock so that the child

** processes do not fight like dogs to serve the request

** and once it gets a request it it moves out of the critical

** section

*/

if(get_lock() < 0)  {

Template 2.4 Contd..

fprintf(stderr,"Could'nt obtain lock: %s",strerror(errno));

_exit(-1);

}

if((sockd2=accept(main_sockd,(struct sockaddr *)&peer,&length))< 0)    {

fprintf(stderr,"accept: %s",strerror(errno));

_exit(-1);

}

/*  reducing the number of processes which we we donot have much  load   */

if ((scoreboard->child_num - scoreboard->busy) > spare )

cycle = 0;

if(release_lock() < 0)  {

fprintf(stderr,"Could'nt release lock: %s",strerror(errno));

_exit(-1);

}

/** end of critical section  */

message = BUSY;

if(send_socket(sockd,(char *)&message,sizeof(message)) < 0)

_exit(-1);

kill(parent_pid,SIGUSR1);

child_func(sockd2);

close(sockd2);

}

_exit(0);

}

/*  this is the startup code for setting up the child processes

** fucn is the callback function that should be invoked once it gets a request. */

void init_daemon(char *logname, int num,int max_children,int num_cycle,int perfork,int min_children, int (*func)(int),int sockd) {

int retval;

main_sockd = sockd;

logstring = logname;

initial = num;

max = max_children;

min = min_children;

Template 2.4 Contd..

cycle = num_cycle;

spare = perfork;

child_func = func;

parent_pid = getpid();

mask = block_signals();

setup_signal_handlers();

init_lock();

while(1)   {

if(child_num < initial) {

retval = fork_child(initial - child_num);

}

if(busy >= (child_num-min)) {

if(max > busy)  {

if((max - child_num) > perfork)

fork_child(initial);

else

fork_child((max - child_num));

}

}

if(get_lock() < 0)   {

fprintf(stderr,"Could'nt obtain lock: %s",strerror(errno));

_exit(-1);

}

scoreboard->busy = busy;

scoreboard->child_num = child_num;

if (scoreboard->busy >= child_num)  shutdown_server(0);

if(release_lock() < 0)

{

fprintf(stderr,"Could'nt release lock: %s",strerror(errno));

_exit(-1);

}

sigsuspend(&mask);

}

}

## 2.6. RuleModule

Rule module is an iterative server (that serves one request at a time) that makes decision on which Real Server should serve the request Figure 2.6 shows the flow of control in the Rule Module processes secure content switch.

Figure 2.6 showing the flow of control in a Rule Module

The steps involved are:

    - Rule Module is set to listen for connection requests on a particular port. A successful TCP connection results in a valid socket. The secure content switch sends information like Url, Source Portno, Source IP, HTTP Headers, Data (if any) to the Rule Module.

    - Rule Module receives the information like Url, Source PortNo, Source IP, and HTTP Headers, Data (if any).

    - The Rule Modules checks the HTTP Method, if it is Post Request it Checks the Content-Type field in the HTTP headers, if the Content-Type is “x-www-form-urlencoded” it decodes the data and populates the values in the structure (shown in Template 2.5) with the values.

    - The Rule Matching module then performs rule matching with the rules. The rules are simple if then statements (as shown in Template 2.6) and returns the server address, server name and port on which the server it is listening.

Template 2.5

struct ip_vs_cb_rule_field

{

char  name[512]; /* tag name*/

char  value[256]; /* value of the tag */

};

Template 2.6

R1: if (xml.purchase/totalAmount > 52000){ routeTo(server1, STICKY); }

R2: if (xml.purchase/customerName == "CCL") { routeTo(server2, NONSTICKY); }

R3: if (strcmp(url, "gif$") == 0) { routeTo(server3, NONSTICKY); }

R4: if (srcip == “128.198.60.1” && dstip == “128.198.192.192” &&    dstport == 80)

{ routeTo(server2, STICKY); }

Template 2.7 shows how the child secure content switch tries to connect to the rule module. If the rule module is being updated request will be send to the DEFAULT_RULE_SERVER_NAME.

Template 2.7

if((server_sock_fd=connectTo(RULE_SERVER_NAME,RULE_SERVER_PORT)) == -1) {

(void) fprintf(stderr,"Failed to connect to the rule module %s\n",RULE_SERVER_NAME);

if((server_sock_fd=connectTo(DEFAULT_RULE_SERVER_NAME,DEFAULT_RULE_SERVER_PORT )) == -1) {

(void) fprintf(stderr,"Failed to connect to the rule module %s\n",DEFAULT_RULE_SERVER_NAME);

goto  GracefulExit;

}

}

CHAPTER 3

# Performance Results

This section presents the performance results of the Linux application Level Proxy for content switch. Fig shown below shows a block diagram of Secure Linux Application level content switch.

Figure 3.1 showing the block diagram of the secure content switch test bed

Table 3.1 shows the hardware and software configuration of machines used in the test-bed.

| Machine Spec | IP Address | O/S | Web Server |
| --- | --- | --- | --- |
| a) calvin.uccs.edu DELL Dimension-4100, 933 MHz, 512MB b) oblib.uccs.edu HP Vectra VL 512 MHz, 512MB (Content switch) | 128.198.192.184 128.198.60.195 | Redhat 7.2 (2.4.9-21) Redhat 7.2 (2.4.9-21) | Apache 1.3.22 Apache 1.3.22 |
| a) dilbert.uccs.edu b) wait.uccs.edu c) wind.uccs.edu (Client) | 128.198.60.23 128.198.60.202 128.198.60.204 | a) Windows NT, 4.0 b), c) Windows-2000, Advanced Server | N/A |
| a) eca.uccs.edu b) frodo.uccs.edu c) bilbo.uccs.edu d) odorf.uccs.edu e) walrus.uccs.edu f) wallace.uccs.edu HP Kayak Machines, 233 MHz, 96MB RAM (Real Server) | 128.198.60.188 128.198.60.183 128.198.60.182 128.198.60.196 128.198.60.197 128.198.60.208 | Redhat 7.1 (2.4.3-12) | Apache 1.3.19 |

Table 3.1 Configuration of machines used in performance tests

The tests were performed using Web bench and the negotiated cipher suite for these tests are

Negotiated Cipher Suite

DES-CBC3-SHA            SSLv3 Kx=RSA      Au=RSA  Enc=3DES(168) 	Mac=SHA1

For instructions of how to set up Secure Linux Application level Content switch, refer to Appendix A.

## 3.1. Performance Test 1

Goal: check for the Performance of the Linux Application Level Content switch (secure content switch) for both SSL and NON-SSL kind of Requests

Secure content switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: Two HP Kayak Machines, 233 MHz, 96MB RAM

| Client | Request Per Second Prefork NonSecure content switch | Request Per Second Dynamic NonSecure content switch | Request Per Second Apache NonSSL | Request Per Second Dynamic Secure content switch | Request Per Second Prefork Secure content switch | Request Per Second Apache SSL |
| --- | --- | --- | --- | --- | --- | --- |
| 1_client | 148.046 | 82.588 | 244.404 | 26.992 | 23.042 | 37.450 |
| 4_client | 146.542 | 84.283 | 241.296 | 26.100 | 20.858 | 36.958 |
| 8_client | 128.688 | 82.642 | 234.867 | 26.113 | 21.704 | 37.479 |
| 12_client | 145.521 | 83.567 | 230.183 | 26.279 | 20.246 | 37.279 |
| 16_client | 148.100 | 82.017 | 236.350 | 26.425 | 21.604 | 37.396 |
| 20_client | 147.946 | 83.433 | 241.475 | 26.333 | 19.462 | 36.962 |
| 24_client | 135.046 | 82.642 | 237.050 | 26.358 | 21.004 | 37.833 |
| 28_client | 148.058 | 83.158 | 234.037 | 26.421 | 20.279 | 38.150 |
| 32_client | 126.621 | 82.767 | 241.037 | 26.275 | 20.358 | 38.346 |
| 36_client | 123.542 | 81.933 | 242.046 | 25.783 | 20.275 | 38.375 |
| 40_client | 148.121 | 81.575 | 239.567 | 25.625 | 21.188 | 37.892 |
| 44_client | 129.762 | 83.112 | 232.988 | 26.033 | 20.163 | 37.804 |
| 48_client | 148.113 | 83.421 | 243.688 | 26.304 | 20.404 | 37.571 |
| 52_client | 147.850 | 81.975 | 244.037 | 26.063 | 21.446 | 37.400 |
| 56_client | 106.900 | 82.254 | 243.258 | 26.350 | 17.363 | 37.063 |
| 60_client | 128.879 | 83.254 | 243.554 | 26.212 | 15.800 | 36.188 |

Table 3.2 showing the request/sec of different types of secure content switch

Figure 3.1 showing the request/sec of different types of secure content switch

### Dynamic Forking vs. Pre-forking secure content switch

The performance of the Dynamic forking secure content switch is better than Pre-forked secure content switch. I found out that after a while the children are created and killed immediately with out serving multiple requests. The Pre-forked server is designed to see that child SSL Processes are created ahead of time and kill them if their number exceeds a certain threshold. The reason could be that more child processes are free which implies number of requests sent by the web-bench is irregular, there by affecting the overall performance of the pre-forked secure content switch.

Cluster with secure content switch vs. standalone Apache web server

The performance of a dynamic forking secure content switch was pretty good when compared to a standalone apache server. Taking into fact that amount of computation overhead involved with extracting the HTTP headers and performing a rule matching on the HTTP header data, and routing the request to one of the Real Servers.

## 3.2. Performance Test 2

Goal: Investigate the impact of processor on the performance of the secure content switch using machines of slower processing speed

Secure content switch Configuration: one HP Vectra VL, 512 MHz, 512MB RAM

Real Server Configuration: Two HP Kayak Machines, 233 MHz, 96MB RAM

| Clients | Dynamic NonSecure content switch | Prefork NonSecure content switch | Apache Non-SSL | Dynamic Secure content switch | Prefork Secure content switch | Apache MOD-SSL |
| --- | --- | --- | --- | --- | --- | --- |
| 1_client | 19.754 | 70.233 | 209.787 | 15.588 | 23.446 | 14.163 |
| 4_client | 15.350 | 56.375 | 183.958 | 14.933 | 22.092 | 14.383 |
| 8_client | 19.629 | 90.783 | 136.775 | 15.979 | 21.608 | 14.729 |
| 12_client | 16.458 | 95.108 | 184.012 | 15.571 | 20.992 | 14.721 |
| 16_client | 21.554 | 91.979 | 182.688 | 15.137 | 20.438 | 13.913 |
| 20_client | 21.962 | 101.000 | 208.179 | 14.942 | 17.975 | 14.758 |
| 24_client | 24.621 | 84.883 | 177.971 | 18.288 | 21.375 | 14.504 |
| 28_client | 25.967 | 84.563 | 205.075 | 18.871 | 22.400 | 14.642 |
| 32_client | 22.679 | 76.279 | 183.600 | 18.262 | 20.708 | 14.675 |
| 36_client | 26.104 | 93.758 | 173.721 | 15.746 | 21.346 | 14.663 |
| 40_client | 27.579 | 91.200 | 209.475 | 15.050 | 20.196 | 14.375 |
| 44_client | 25.742 | 87.196 | 207.054 | 15.467 | 22.063 | 14.908 |
| 48_client | 25.179 | 77.683 | 180.613 | 14.342 | 21.742 | 14.704 |
| 52_client | 26.125 | 83.575 | 184.983 | 18.171 | 21.608 | 14.742 |
| 56_client | 26.404 | 74.683 | 183.721 | 18.200 | 16.692 | 14.817 |
| 60_client | 22.038 | 88.963 | 199.596 | 19.017 | 22.079 | 14.646 |

Table 3.3 showing the request/sec of different types of secure content switch

Figure 3.2 showing the request/sec of different types of secure content switch

Dynamic Forking vs. Pre-forking secure content switch

Preforking secure content switch performed better than dynamic forking version of secure content switch. This is an expected result.

Cluster with secure content switch vs. standalone Apache web server

Dynamic forking and preforking versions of secure content switch performed better than Apache web server. The reason for this performance could be attributed to the distributing of the request-fetching task to the real server thereby reducing the overload on the content switch.

Impact of processor speed on content switch

There is not much impact of processor speed on the performance of secure content switch. This clearly indicates that the most of the computation is involved in TLS/SSL encryption and decryption.

## 3.3. Performance Test 3

Goal: Study the impact of the number of rules on the Performance of the dynamic secure content switch.

Secure content switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: Two HP Kayak Machines, 233 MHz, 96MB RAM

| Client | SSL Requests Per Second for 250 Rules | SSL Requests Per Second for 300 Rules | SSL Requests Per Second for 500 Rules | SSL Requests Per Second for 1000 Rules | SSL Requests Per Second for 2000 Rules | SSL Requests Per Second for 5000 Rules |
| --- | --- | --- | --- | --- | --- | --- |
| 1_client | 27.096 | 26.879 | 27.025 | 22.896 | 26.917 | 26.917 |
| 4_client | 26.183 | 26.650 | 25.975 | 22.850 | 25.171 | 26.063 |
| 8_client | 26.450 | 26.275 | 26.058 | 21.654 | 26.329 | 26.163 |
| 12_client | 26.346 | 26.696 | 26.300 | 25.863 | 26.012 | 24.254 |
| 16_client | 26.496 | 25.808 | 26.529 | 25.904 | 26.354 | 26.163 |
| 20_client | 26.529 | 22.579 | 26.021 | 25.750 | 26.150 | 25.779 |
| 24_client | 26.538 | 24.929 | 25.908 | 26.592 | 25.871 | 26.208 |
| 28_client | 26.512 | 25.512 | 18.654 | 26.400 | 26.558 | 26.167 |
| 32_client | 26.629 | 26.108 | 23.262 | 24.254 | 26.313 | 25.996 |
| 36_client | 26.488 | 25.504 | 26.367 | 22.229 | 26.517 | 25.342 |
| 40_client | 26.521 | 25.725 | 26.608 | 23.850 | 26.429 | 26.188 |
| 44_client | 26.258 | 25.967 | 25.792 | 26.363 | 26.113 | 26.087 |
| 48_client | 26.554 | 26.004 | 26.571 | 25.833 | 26.225 | 26.017 |
| 52_client | 26.304 | 25.792 | 26.288 | 25.746 | 25.529 | 25.954 |
| 56_client | 21.804 | 25.683 | 23.025 | 26.421 | 26.208 | 26.046 |
| 60_client | 22.087 | 26.000 | 22.392 | 26.317 | 26.083 | 25.800 |

Table 3.4 showing the request/sec of different types of secure content switch

Figure 3.3 showing the request/sec of different types of secure content switch

Observation: There is not much effect of the rules on the Dynamic Forking Secure content switch, which implies that most of the computation power is used on the decryption and encryption of the SSL requests.

| Client | Non-SSL Requests Per Second for 250 Rules | Non-SSL Requests Per Second for 300 Rules | Non-SSL Requests Per Second for 500 Rules | Non-SSL Requests Per Second for 1000 Rules | Non-SSL Requests Per Second for 2000 Rules | Non-SSL Requests Per Second for 5000 Rules |
| --- | --- | --- | --- | --- | --- | --- |
| 1_client | 86.179 | 66.412 | 72.487 | 84.829 | 73.346 | 64.121 |
| 4_client | 88.171 | 66.871 | 71.954 | 86.183 | 73.121 | 63.683 |
| 8_client | 87.571 | 68.783 | 70.742 | 84.912 | 72.654 | 64.775 |
| 12_client | 88.342 | 68.367 | 72.271 | 83.675 | 70.825 | 63.946 |
| 16_client | 87.558 | 67.642 | 73.117 | 86.700 | 73.138 | 63.650 |
| 20_client | 88.971 | 70.396 | 70.671 | 86.458 | 71.008 | 64.533 |
| 24_client | 84.833 | 58.558 | 70.371 | 87.204 | 72.525 | 64.633 |
| 28_client | 85.996 | 61.300 | 72.013 | 85.842 | 72.792 | 60.896 |
| 32_client | 88.263 | 71.346 | 68.625 | 86.338 | 71.254 | 65.175 |
| 36_client | 87.579 | 72.104 | 68.029 | 86.542 | 72.908 | 65.679 |
| 40_client | 88.683 | 71.133 | 70.758 | 85.929 | 72.354 | 66.621 |
| 44_client | 87.808 | 70.317 | 70.933 | 85.079 | 72.279 | 67.542 |
| 48_client | 85.300 | 70.900 | 69.508 | 84.846 | 73.496 | 64.721 |
| 52_client | 83.287 | 63.462 | 69.800 | 73.792 | 72.150 | 66.429 |
| 56_client | 83.563 | 71.779 | 69.333 | 87.287 | 72.571 | 68.167 |
| 60_client | 85.133 | 71.196 | 69.975 | 85.396 | 70.075 | 67.321 |

Table 3.5 showing the request/sec of different types of secure content switch

Figure 3.4 showing the request/sec of different types of secure content switch

Observation: There is some impact on the performance of the Dynamic Forking Non-SSL secure content switch, the lower the number of rules the better the performance is. Overall there is no major impact of the performance of the secure content switch with increase in the number of rules.

## 3.4. Performance Test 4

Goal: Study the impact of the number of real servers on the performance of the dynamic forking secure content switch.

Secure content switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: one-five HP Kayak Machines, 233 MHz, 96MB RAM

| Client | SSL Requests Per Second with 1 RealServer | SSL Requests Per Second with 2 RealServers | SSL Requests Per Second with 3 RealServers | SSL Requests Per Second with 4 RealServers | SSL Requests Per Second with 5 RealServers |
| --- | --- | --- | --- | --- | --- |
| 1_client | 27.433 | 27.096 | 27.012 | 28.492 | 27.392 |
| 4_client | 26.542 | 26.183 | 26.029 | 26.908 | 24.842 |
| 8_client | 26.296 | 26.450 | 24.188 | 27.358 | 26.387 |
| 12_client | 25.738 | 26.346 | 23.217 | 27.367 | 25.433 |
| 16_client | 26.221 | 26.496 | 26.029 | 27.225 | 25.179 |
| 20_client | 25.225 | 26.529 | 26.396 | 25.746 | 26.342 |
| 24_client | 25.221 | 26.538 | 25.946 | 27.017 | 25.371 |
| 28_client | 25.567 | 26.512 | 26.042 | 26.933 | 25.975 |
| 32_client | 26.154 | 26.629 | 25.283 | 26.262 | 25.746 |
| 36_client | 25.996 | 26.488 | 25.758 | 27.233 | 26.396 |
| 40_client | 26.333 | 26.521 | 26.208 | 25.971 | 26.542 |
| 44_client | 25.529 | 26.258 | 25.675 | 26.700 | 25.650 |
| 48_client | 25.871 | 26.554 | 25.442 | 27.038 | 26.462 |
| 52_client | 26.117 | 26.304 | 26.329 | 26.967 | 26.146 |
| 56_client | 25.762 | 21.804 | 26.104 | 26.679 | 26.392 |
| 60_client | 26.600 | 22.087 | 25.988 | 26.229 | 25.025 |

Table 3.6 showing the Req/Sec of Dynamic Forking secure content switch

Fig 3.5 showing the Request / Second of Dynamic Forking secure content switch

Observation: There is no impact on the performance of the dynamic forking secure content switch, with the change in the number of real servers. This clearly indicates that current version of secure content switch is the bottleneck.

| Client | Non-SSL Requests Per Second with 1 RealServer | Non-SSL Requests Per Second with 2 RealServers | Non-SSL Requests Per Second with 3 RealServers | Non-SSL Requests Per Second with 4 RealServers | Non-SSL Requests Per Second with 5 RealServers |
| --- | --- | --- | --- | --- | --- |
| 1_client | 61.250 | 86.179 | 72.608 | 74.471 | 74.246 |
| 4_client | 61.596 | 88.171 | 77.063 | 74.504 | 73.979 |
| 8_client | 61.192 | 87.571 | 76.979 | 72.638 | 73.013 |
| 12_client | 59.271 | 88.342 | 77.013 | 73.500 | 74.862 |
| 16_client | 60.367 | 87.558 | 73.558 | 73.571 | 73.654 |
| 20_client | 59.858 | 88.971 | 75.883 | 73.354 | 63.254 |
| 24_client | 58.092 | 84.833 | 76.200 | 74.125 | 74.817 |
| 28_client | 59.317 | 85.996 | 76.329 | 74.396 | 75.213 |
| 32_client | 61.104 | 88.263 | 77.496 | 72.996 | 74.783 |
| 36_client | 60.083 | 87.579 | 76.275 | 74.737 | 74.746 |
| 40_client | 62.254 | 88.683 | 76.621 | 74.217 | 72.021 |
| 44_client | 62.129 | 87.808 | 76.454 | 77.967 | 74.458 |
| 48_client | 60.263 | 85.300 | 75.208 | 79.804 | 73.446 |
| 52_client | 60.321 | 83.287 | 76.225 | 78.917 | 73.525 |
| 56_client | 58.604 | 83.563 | 76.529 | 78.304 | 74.400 |
| 60_client | 61.183 | 85.133 | 76.421 | 79.583 | 74.683 |

Table 3.7 showing the req / sec of dynamic forking non-secure content switch

Figure 3.6 showing the Req / Sec of dynamic forking non-secure content switch

Observation: There is a major impact on the performance of the dynamic forking non-secure content switch, with the change in the number of real servers. Non-secure dynamic forking performs best with 2 real servers.

## 3.5. Performance Test 5

Goal: Study the impact on secure content switch of local rule module

Rule Module Server: One DELL Dimension-4100, 933 MHz, 512MB RAM

Secure Content Switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: Two HP Kayak Machines, 233 MHz, 96MB RAM

| Client | Prefork NonSecure content switch Request Per Second | Dynamic NonSecure content switch Request Per Second | Dynamic Secure content switch Requests Per Second | Prefork Secure content switch Request Per Second |
| --- | --- | --- | --- | --- |
| 1_client | 129.121 | 92.750 | 13.238 | 24.279 |
| 4_client | 91.912 | 103.142 | 11.725 | 23.621 |
| 8_client | 122.588 | 107.754 | 12.613 | 23.467 |
| 12_client | 112.358 | 87.621 | 12.808 | 23.475 |
| 16_client | 96.225 | 61.996 | 12.858 | 23.425 |
| 20_client | 133.054 | 90.983 | 12.771 | 22.650 |
| 24_client | 116.558 | 84.888 | 12.663 | 22.996 |
| 28_client | 109.467 | 79.158 | 12.875 | 22.858 |
| 32_client | 96.829 | 80.213 | 12.833 | 22.875 |
| 36_client | 107.979 | 80.742 | 12.654 | 22.779 |
| 40_client | 113.329 | 80.858 | 11.488 | 22.821 |
| 44_client | 100.350 | 77.612 | 12.929 | 23.075 |
| 48_client | 108.300 | 81.417 | 12.908 | 22.829 |
| 52_client | 113.408 | 80.675 | 12.600 | 22.254 |
| 56_client | 80.987 | 80.912 | 12.871 | 21.938 |
| 60_client | 78.692 | 80.858 | 12.642 | 22.108 |

Table 3.8 showing the Req/Sec of secure content switch with local rulemodule

Figure 3.7 showing the Req / Sec of secure content switch with local rule module

Observation: There is a major impact on the performance of the dynamic forking secure content switch, with the creation of a rule module. The preforking secure content switch performance is independent of the creation of a rule module.

## 3.6. Performance Test 6

Goal: Study the impact on secure content switch of remote rule module

Rule Module Server: One HP Kayak Machines, 233 MHz, 96MB RAM

Secure Content Switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: Two HP Kayak Machines, 233 MHz, 96MB RAM

| Client | Prefork NonSecure content switch Request Per Second | Dynamic NonSecure content switch Request Per Second | Dynamic Secure content switch Request Per Second | Prefork Secure content switch Request Per Second |
| --- | --- | --- | --- | --- |
| 1_client | 82.929 | 49.533 | 13.450 | 23.521 |
| 4_client | 99.917 | 49.783 | 11.771 | 22.671 |
| 8_client | 97.912 | 43.188 | 12.133 | 22.396 |
| 12_client | 100.683 | 81.650 | 11.963 | 22.525 |
| 16_client | 108.829 | 82.767 | 12.012 | 22.121 |
| 20_client | 87.287 | 80.850 | 11.988 | 22.483 |
| 24_client | 83.979 | 80.588 | 11.942 | 21.529 |
| 28_client | 86.075 | 75.717 | 12.042 | 21.863 |
| 32_client | 86.700 | 64.954 | 12.004 | 20.271 |
| 36_client | 86.971 | 60.896 | 12.042 | 21.100 |
| 40_client | 93.317 | 63.196 | 12.063 | 21.688 |
| 44_client | 87.254 | 71.829 | 11.996 | 21.758 |
| 48_client | 113.912 | 64.829 | 11.917 | 21.629 |
| 52_client | 100.658 | 78.625 | 12.046 | 22.346 |
| 56_client | 107.704 | 81.217 | 11.967 | 22.475 |
| 60_client | 102.021 | 81.196 | 12.021 | 21.742 |

Table 3.9 showing the Req/Sec of secure content switch with remote rule module

Figure 3.8 shows the Req/Sec of secure content switch with remote rule module

### Remote rule module vs. local rule module

There is no impact on the performance of both versions of secure content switch of rule module.

## 3.7. Performance Test 7

Goal: Study the impact of local node feature

Rule Module Server: One DELL Dimension-4100, 933 MHz, 512MB RAM

Secure Content Switch Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

Real Server Configuration: One DELL Dimension-4100, 933 MHz, 512MB RAM

| Client | Prefork NonSecure content switch Request Per Second | Dynamic NonSecure content switch Request Per Second | Dynamic Secure content switch Request Per Second | Prefork Secure content switch Request Per Second |
| --- | --- | --- | --- | --- |
| 1_client |  | 73.400 | 26.571 | 22.254 |
| 4_client |  | 73.662 | 24.983 | 22.087 |
| 8_client |  | 74.338 | 25.300 | 21.988 |
| 12_client |  | 73.942 | 22.871 | 21.571 |
| 16_client |  | 74.929 | 24.267 | 20.758 |
| 20_client |  | 72.521 | 25.408 | 20.688 |
| 24_client |  | 73.258 | 24.212 | 21.212 |
| 28_client |  | 73.442 | 24.692 | 21.358 |
| 32_client |  | 74.633 | 25.233 | 21.375 |
| 36_client |  | 71.929 | 25.400 | 21.413 |
| 40_client |  | 74.787 | 25.346 | 22.175 |
| 44_client |  | 73.733 | 25.092 | 22.483 |
| 48_client |  | 74.300 | 25.342 | 22.050 |
| 52_client |  | 73.237 | 25.317 | 20.563 |
| 56_client |  | 74.183 | 25.346 | 22.192 |
| 60_client |  | 72.975 | 24.571 | 21.929 |

Table 3.10 shows the Req / Sec of secure content switch with remote rule module

Figure 3.9 showing the Req/Sec of secure content switch in local node problem

When performing this test with both Apache as a local node and perforked secure content switch I am facing the following interesting problem

I am running the apache on port 8000, secure content switch on 80. after serving a few requests secure content switch stopped serving Requests. I stopped Apache web server, secure content switch started serving requests again. I started the Apache Web server, after serving a few requests secure content switch stopped serving Requests. This process is continuing.

The above problem indicates that secure content switch will not be able to serve requests concurrently with the local node web server. We have found that when run alone, the requests are served properly.

# Chapter 4

# Conclusion and future work

We have developed a content switch that performs the functions of a web switch with the added facility of SSL security at the Application Layer. The software package currently uses OpenSSL version 0.6. The features of our content switch include session id reuse and high encryption strength. We have tested it on a cluster test-bed using the industry standard benchmarking software and found its performance to be satisfactory.  Based on the test results we have found that there is not much improvement in terms of processor speed,

One of the improvements that are possible is reducing the bottleneck of SSL encryption / decryption. SSL transactions are computation intensive and hence become a drain on web server resources. In cases of web servers handling a large amount of traffic, the problem can become more significant. One way to alleviate the problem is to apply parallel processing techniques. But as one ponders about a solution for this problem, we need to think about how all the web servers are going to know about the TLS/SSL session information that was negotiated by another server. There is a message in the openssl group posted by Lutz Jaenicke that talks of a future version OpenSSL 0.9.7 (not yet released) that has a new function (server side) to explicitly choose the session IDs generated (rather than random values as of now). Therefore it will be possible to include a "server ID" into the session ID so that load balancing will become easier. Once the above-mentioned version is released, a solution might be in sight.

Another performance improvement can be the caching of web pages. This aspect must be handled sensibly as most of the web documents that use SSL is dynamic in nature.

One of the ways to overcome the problem of maintaining state across multiple web processes in dealing with TLS/SSL transactions is to make the connections “sticky”. The problem with this design is that the IP addresses are constantly shifting for users coming into a site from Internet service providers that use proxy servers. So users must have a “sticky” connection to the SSL server that is independent of their IP address. This can be achieved by having a cookie which identifies which Real Server has serviced the user previously.

Another suggestion for improving the current content switch performance is to have a persistent HTTP connection between the Content switch and the Real Servers, which can be used by all the processes, for all the requests.

Each of these solutions comes with its own combination of cost, performance, and flexibility of scale—proving once again that, when it comes to Web site architecture, one size never fits all.

# Appendix A

A.1. Installing of Linux Application Level Content switch

First step in installing Linux Application Level Content switch involves installing Openssl

A.1.1.  Install Openssl

Fetch and extract the distribution of OpenSSL package download the source of openssl from http://www.openssl.org/source/

Template

tar -xvzf openssl-0.9.6b.tar.gz

Build OpenSSL package with the following commands.

cd openssl-0.9.6b

./config

make

cd ..

A.1.2.	Install SSL Proxies for Content switch

Download dynamic forking and Pre-Forked versions with SSL or without SSL support from http://archie.uccs.edu/~acsd/lcs03/secure content switch0.1.1.tar.gz

Template

tar -xvzf secure content switch.tar.gz

cd secure content switch

dyna_proxy.c            Dynamic forking version of NON-Secure  content switch for Linux Application-Level Content switch 
dyna_secure  content switch.c        Dynamic forking version of Secure  content switch for Linux Application-Level Content switch 
prefork_secure  content switch.c    Pre-forking version of Secure  content switch for Linux Application-Level Content switch 
prefork_proxy.c        Pre-forking version of NON-Secure  content switch for Linux Application-Level Content switch

A.1.3.    Configure secure content switch for content switch

All the server code share the same Configuration Section, the user should edit the configuration section provided in include/config.h.  The system parameters of secure content switch server are specified in the header file. The following is the configuration section you find in the Pre-forked Version of Secure content switch. Typically, we only need to change the

SERVER_ROOT, SERVER_IP, SERVER_NAME, RULE_SERVER_NAME, RULE_SERVER_PORT, DEFAULT_RULE_SERVER_NAME, DEFAULT_RULE_SERVER_PORT.

The Editable section in Dynamic forking versions of SSL and NON-Secure  content switch Server is similar.

Template

#define CLIENT_TIMEOUT 		30

#define SERVER_ROOT			"/home/gkgodava/rulemodule"

#define LOG_FILE 			"log/ssl.log"

#define SESS_FILE			"cache/scache"

#define SERVER_IP 			"128.198.60.22"

#define SERVER_NAME			"calvin.uccs.edu"

#define RULE_SERVER_NAME		"gandalf.uccs.edu"

#define RULE_SERVER_PORT		4000

#define DEFAULT_RULE_SERVER_NAME	"calvin.uccs.edu"

#define DEFAULT_RULE_SERVER_PORT	4000

#define CA_FILE     			"testssl/ca/cacert.pem"

#define CA_PATH     			"testssl/ca"

#define KEY_FILE    	"testssl/private/private.key"

#define CERT_FILE   	"testssl/cert/newcert.pem"

#define RAND_FILE   	"testssl/random/random.pem" /* random is a junk file that contains any data--ensure it is not repeated*/

#define SSL_SESSION_CACHE_TIMEOUT 	300

#define STICKY_SIZE 			20			    /* allocation for maximum # of the sticky connection */

/*

** It does this by periodically checking how many servers

** are waiting for a request.  If there are fewer than

** MinSpareServers, it creates a new spare.  If there are

** more than MaxSpareServers, some of the spares die off.

**

*/

#define MinSpareServers 2

#define MaxSpareServers 5

/*

** Number of servers to start initially --- should be a

** reasonable ballpark figure.

*/

#define StartServers 5

/*

** Limit on total number of servers running, i.e., limit on ** the number of clients who can simultaneously connect --- ** if this limit is ever reached, clients will be LOCKED

** OUT, so it should NOT BE SET TOO LOW. It is intended

** mainly as a brake to keep a runaway server from taking ** the system with it as it spirals down...

*/

#define MaxClients 25

/*

** MaxRequestsPerChild: the number of requests each child ** process is allowed to process before the child dies.

** The child will exit so as to avoid problems after

** prolonged

*/

#define MaxRequestsPerChild 50

/*

** Listen: Allows you to bind to a specific Ports

*/

#define SERVER_PORT 			443

/*

** Prefork header file locks the following file

*/

#define PREFORK_LOCK "/tmp/install.log"

/*

** lock file for critical section handling

*/

#define CRITICAL_LOCK "/dev/zero"

A.2.  Configure LCS routing rules

Currently the rules are specified in a function called rule_configure in each of source code. Once you make changes to the rules in the rule_configure function, you need to recompile and execute the new program.

Here is the example of the rules specified in the source code:

u_long rule_configure(char *url, u_long saddr,u_long daddr, u_short sport, u_short dport, u_short protocol) {

if (strstr(url,"zbwb_20") != NULL) { 
  return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
}

if (strstr(url,"zbwb_19") != NULL) { 
  return route_to("eca.uccs.edu",NON_STICKY,saddr); 
}

if (strstr(url,"zbwb_18") != NULL) { 
  return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
} 
....

if (strstr(url,"cs522") != NULL) { 
    return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
}

if (strstr(url,"cs301") != NULL) { 
           return route_to("eca.uccs.edu",NON_STICKY,saddr); 
        }

if(strstr(url,"cs") != NULL) { 
           return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
        }

if (strstr(url,"keepalive") != NULL) { 
           return route_to("eca.uccs.edu",NON_STICKY,saddr); 
        }

if (saddr == 0x80c6a2d9){ 
           return route_to("eca.uccs.edu",NON_STICKY,saddr); 
        }

if ((atoi(rule_fields[1].value) > 0) && (atoi(rule_fields[1].value) <50000)){ 
          return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
        }

if (atoi(rule_fields[1].value) > 50000) { 
           return route_to("eca.uccs.edu",NON_STICKY,saddr); 
        }

if (strstr(url,"lcs1") != NULL) { 
           return route_to("frodo.uccs.edu",NON_STICKY,saddr); 
        }

if (strstr(url,"lcs2") != NULL) { 
           return route_to("eca.uccs.edu",NON_STICKY,saddr); 
        }

return route_to("frodo.uccs.edu",NON_STICKY,saddr);

As it can be seen in this rule set, we use two real servers: frodo.uccs.edu and eca.uccs.edu.  You may want to change them to the real servers, which you are using. The first 24 rules are used to spread the requests from WebBench benchmark program. Among them, the first 20 rules spread the load based on the leading text pattern of the url. The next 4 rules spread the load based on the file extension.  In the production environment, you may want to remove these 24 rules.

The rules with pattern "cs522", "cs301", "cs", "lcs1", and "lcs2" are used in the demo scripts. The rule with (saddr == 0x80c6a2d9) is used to demonstrate the firewall or sticky connection. The last few rules with (atoi(rule_fields[1].value)) are related to request with XML document.  The corresponding XML tag sequences are specified in

struct ip_vs_cb_rule_field rule_fields[] = 
{ 
{"purchase:1.totalAmount:1.", "" }, 
{"purchase:1.subTotal:1.", "" }, 
{"purchase:1.subTotal:2.", "" }, 
{"purchase:1.unitPrice:2.", "" } 
};

Here rule_fields[1] is referred to the tag sequence with the first subTotal tag inside the first totalAmount tag. The number after the element name refers to the specific element with in the XML document structure. When the request with such XML tag sequence arrives, the content switch will extract the value and put it in rule_fields[1].value. Since it is string, we need to convert to integer using atoi().

A.3. Compile the content switch code

Once you have modified the Editable section and the rule set, type "make". In order to compile we need to specify the ssl, crypto, dbm libraries. If you are using Redhat Linux 7.2, replace ndbm with gdbm, you will avoid the problem

#

# This is a simple make file written by Ganesh Godavari

# if u have any problems with this Makefile please contact gkgodava@archie.uccs.edu

#

CC:=		gcc

INCLUDES=	–I./include –I./.

LDLIBS=-lssl -lcrypto -lndbm

all:	prefork_proxy dyna_secure  content switch prefork_secure  content switch dyna_proxy rulemodule

prefork_proxy:		prefork_proxy.c

$(CC) $(INCLUDES) –D RULE_MODULE –o $@ $< –L../ $(LDLIBS)

dyna_secure  content switch:		dyna_secure  content switch.c

$(CC) $(INCLUDES) –o $@ $< –L../ $(LDLIBS)

prefork_secure  content switch:	prefork_secure  content switch.c

$(CC) $(INCLUDES) –D PREFORK_SSL –o $@ $< –L../ $(LDLIBS)

dyna_proxy:		dyna_proxy.c

$(CC) $(INCLUDES) –o $@ $< –L../ $(LDLIBS)

rulemodule:		rulemodule.c

$(CC) $(INCLUDES) –D RULE_MODULE –o $@ $< –L../ $(LDLIBS)

clean:

rm –f *.o dyna_secure  content switch dyna_proxy prefork_proxy prefork_secure  content switch rulemodule

APPENDIX B

WebBench [24]

WebBench was selected for testing the performance of our content switch, as it is the industry standard benchmarking tool for web servers. The basic concept of WebBench is that a set of clients on PCs across a network send requests to a controller running on the machine that houses the server. The controller coordinates these requests and forwards them to the server that we are benchmarking. The idea is to simulate a number of users sending a large number of requests to the server. The performance of the server under those conditions is recorded and displayed in a easy-to-read manner.

The controller is responsible for coordinating the requests of the client. It also sends notifications to the clients informing them when to commence and stop a test suite. It also collects information from all the clients at the end of the test. The key metrics that are measured are request rate (requests/sec) and throughput (bytes/sec).

The web server that has the maximum throughput under the condition of a high volume of requests is judged as the best server among a set of servers.

The detailed setup steps for benchmarking using WebBench are as follows:

- Install the WebBench controller software on one machine. This is different from the client software. A HTML help file found in the drive:\webbench\Controller directory can be used as a reference manual in order to understand the installation and usage.

- Install the client software on each of the machines that have been selected to send benchmarking requests to the controller.

- Modify the following files

  - drive:\webbench\clientids\client.cdb

This file contains an entry for each of the clients included in the test suite. An entry has to be added for each client containing the clients IP address and a unique ID no.

b. drive:\webbench\system32\drivers\etc\hosts

This file has to be modified to contain the name and IP address of the web server and controller

- Install the data files on the machine that hosts the Web server (to be benchmarked). The data files are bundled in a single compressed file, which can be downloaded from the same location where controller and client installation software are downloaded. For UNIX systems, the data files should be installed under the directory that is set up as document root of the Web server.

After the controller and client software are installed appropriately and data files placed correctly on the Web server, the next step is to set up the test suites. Two key test suites are static and dynamic. In static test suites static content like, ".gif", ".jpg" etc. are returned.  In dynamic test suites, dynamic content as generated from a program that runs on the Web server machine, e.g., cgi-bin programs, is tested.  There can be test suites that have a combination of static and dynamic content. A test suite itself can consist of many mixes. Note that both test suites and mixes are created/edited via the controller window. With each mix, are associated a number tunable parameters, e.g.:

- Number of clients

- Length (duration) of the mix

- Delay the client waits before starting the tests in the mix once signaled by the controller

- Think time, which is the time gap between consecutive requests in a mix

- Percentage of persistent requests

- Percentage of pipelined requests

- Percentage of SSL requests

There is a work load file associated with a mix, a sample of which is shown in Template A.14.

Template A.14

DEFINE_CLASSES

CLASS_DYNAMIC:     25

CLASS_223.gif:     15

CLASS_735.gif:     7

CLASS_6040.htm:    40

CLASS_11426.htm:   8

CLASS_404:         5

DEFINE_REQUESTS

CLASS_DYNAMIC:

GET /cgi-bin/simcgi

CLASS_223.gif:

GET /wbtree/223_1.gif

GET /wbtree/zdwb_1/223_1.gif

GET /wbtree/zdwb_1/zdwb_1/223_1.gif

GET /wbtree/zdwb_1/zdwb_1/zdwb_1/223_1.gif

CLASS_735.gif:

GET /wbtree/735_1.gif

GET /wbtree/zdwb_1/735_1.gif

GET /wbtree/zdwb_1/735_2.gif

CLASS_6040.htm:

GET /wbtree/6040_1.htm

GET /wbtree/6040_2.htm

GET /wbtree/6040_3.htm

GET /wbtree/6040_4.htm

GET /wbtree/6040_5.htm

CLASS_11426.htm:

GET /wbtree/11426_1.htm

GET /wbtree/11426_2.htm

CLASS_404:

GET /wbtree/zdwb_7/zdwb_1/zdwb_2/zdwb_2/223_1.jpg

GET /wbtree/zdwb_19/zdwb_2/zdwb_2/6040_3.html

The workload file, associated with a mix, defines distribution of various files accessed in that mix. In the sample workload file shown in Template A.14, 25 percent of the request sent in the mix will be from the dynamic class, 15 percent of the requests will be from CLASS_223.gif class and so on. The real workload files in practical are very huge, with several hundred requests in each class. Note that the request data files are of different sizes. Further details on setting up several other mix parameters can be found in WebBench help and by actual use of controller software.

There are several example test suites that come with controller installation software and are located in drive:\webbench\Controller\Suites\WebBench directory, with each test suite file having a ".tst" extension. There are also several sample workload files with ".wl" extension, located in the same directory.

Once the test suites are set up, the benchmark tests are ready to be commenced. To start the benchmarks first the controller should be started. After the controller is started, all clients (on all the machines that are setup as clients) have to be started separately. One can see a message on the bottom of client window if it was able to connect properly to the controller. Once all clients are connected to the controller, the tests can be finally be started by selecting an appropriate menu option on the controller window.

Once all the tests are completed clicking the Results menu and choosing the appropriate option can see the results.

Due to export restrictions online copy of the WebBench software supports only 40-bit encryption. Since 40-bit is a very weak encryption secure content switch does not accept connections. In order to perform web bench test one needs to order a copy of their software, which supports 128-bit encryption.

Bibliography

[1] Akamai technologies http://www.akamai.com/index_flash.html

[2] Speedera http://www.speedera.com/flash_index.html

[3] Digitalisland http://www.digitalisland.com/

[4] George Apostolopoulos, David Aubespin, Vinod Peris, Prashant Pradhan, Debanjan Saha, "Design, Implementation and Performance of a Content-Based Switch", Proc. Infocom2000, Tel Aviv, March 26 - 30, 2000, http://www.ieee-infocom.org/2000/papers/440.ps

[5] Leon-Garcia. Widjaja, "Communication Networks: Fundamental Concepts and Key Architectures," McGraw-Hill, 2000

[6] IP Security Protocol, http://www.ietf.org/html.charters/ipsec-charter.html

[7] SSLv3 Internet Draft (obsolete). ftp://ftp.ietf.org/internet-drafts/draft-ietf-tls-ssl-version3-00.txt.

[8] RFC2246 - "The TLS Protocol Version 1.0"  ftp://ftp.isi.edu/in-notes/rfc2246.txt

[9] Netscape web browser http://www.netscape.com/

[10] Microsoft Internet Explorer web browser of Microsoft Technologies http://www.microsoft.com

[11] Gregory Yerxa and James Hutchinson, "Web Content Switching" , http://www.networkcomputing.com

[12] Web switch product of nortel networks http://www.nortelnetworks.com/products/01/alteon/isdssl/index.html

[13] web switch product of F5networks http://www.f5networks.com/

[14] Foundry ServIron Installation and Configuration Guide, May 2000. http://www.foundrynetworks.com/techdocs/SI/index.html

[15] A report submitted by Gaurav Sharma, Ajay Mansata "http://unofficial.umkc.edu/beardc/CS520/tls_sharma_mansata.doc"

[16] white paper by cacheflow http://www.cacheflow.com/files/whitepapers/wp_ssl_primer.pdf

[17] OpenSSL: The Open Source toolkit for SSL/TLS (http://www.openssl.org)

[18] The SSLeay package is copyright Eric Young and is available free for commercial and non-commercial use.

[19] ssh prtocol http://www.ietf.org/html.charters/secsh-charter.html

[20] OpenPGP the most widely used email encryption standard in the world. http://www.openpgp.org/

[21] RSA algorithm invented in 1978 by Ron Rivest, Adi Shamir, and Leonard Adleman. http://www.rsasecurity.com/

[22] The Diffie-Hellman Key Agreement, http://www.hamiltonlabs.com/links.htm

[23] NIST, FIPS PUB 186, "Digital Signature Standard", May 1994.

[24] Enchance features and performance of content switches by chandra prakash, 2001

# Text boxes

Decrypt the data

And populate the rules with values (if any)

No

Yes

Establish Connection with Default Rule Server Module

No

IS

(Method == Post)

Perform rule matching and send back the Real Server Name, Address and Port # on which Real Server is listening

IS

(content type == x-www-form-urlencoded)

No

Yes

Send Url, Src portno, Src IP, HTTP Headers, Data (if any) to the Rule Module

Yes

Establish Connection with Rule Server Module

LACS Child

Retrieve Server Information Rule Matching Module

Retrieve Object From the Server

Using Standard   HTTP

Encrypt the Object Per Session Information and Send it to the Web Browser

Send Object Information To Rule Matching Module

Decrypt Object

Using SSL Session

Information

SSL Request

Yes

Existing

SSL Session

Yes

No

IP/IPsec

IP

TCP

HTTP     IMAP     FTP  …

TCP

SSL or TLS

HTTP     IMAP     FTP  …

Request From Web Browser to the LACS

Linux Application Level Content Switch (LACS)

Child 2

Child 1

Child n

Negotiate SSL Session

Yes

No

Existing

SSL Session

Retrieve Object From the Server

Using Standard HTTP

Encrypt the Object Per Session Information and Send it to the Web Browser

Retrieve Server Information Rule Matching Module

Send Object Information To Rule Matching Module

Yes

Decrypt Object

Using SSL Session

Information

Negotiate SSL Session

SSL Request

Fork ()

Child LACS

Linux Application

Level

Content Switch (LACS)

Request From Web Browser to the LACS

Phase 4:

Optionally send client certificate response if requested.

Phase 3:

Client

Server

ClientHello

ServerHello

Certificate

Certificate Request

ServerHelloDone

Certificate

Certificate Verify

ChangeCipherSpec

Handshake

ChangeCipherSpec

Handshake

Phase 2:

Establish protocol version,

session-id, cipher suite, compression method.

send server certificate and request client certificate

Change CipherSpec

and finish handshake.

Phase 1: