MPLS and IPSec VPNs combined -

A brief status report

- IPSec provides encryption and/or authentication. Works at layer 3.

- MPLS provides routing control and (consequently) QoS. Works at layer 2.5 (?). i.e. inserts an MPLS label between the layer 3 header (say IP) and layer 2 header (say Ethernet. Can also be frame or ATM).

- Their combination gives the best of both worlds. The nice thing about it is, that they work at different layers, and hence seem to fit very well with each other.

How the setup looks

on alpha : 	eth0 = 192.168.0.1,	eth2 = 128.198.1.1

on lamar:	eth0 = 192.168.1.2,	eth2 = 192.168.2.2

The results presented here are for 'ping -I 192.168.0.1 192.168.2.3'

Details of the setup (1)

(1) Setup an IPSec VPN betwe alpha(eth2) and lamar (eth0). (details of ipsec.conf below)

config setup

# THIS SETTING MUST BE CORRECT or almost nothing will work;

# %defaultroute is okay for most simple cases.

interfaces="ipsec0=eth0 ipsec1=eth1 ipsec2=eth2"

# Debug-logging controls:  "none" for (almost) none, "all" for lots.

klipsdebug=all

plutodebug=all

# Use auto= parameters in conn descriptions to control startup actions.

plutoload=%search

plutostart=%search

# Close down old connection when new one using same ID shows up.

#       uniqueids=yes

#conn %default

conn a2l

keyingtries=0

# sample VPN connection

# Left security gateway, subnet behind it, next hop toward right.

left=192.168.1.1

leftsubnet=192.168.0.0/24

leftnexthop=192.168.1.2

# Right security gateway, subnet behind it, next hop toward left.

right=192.168.1.2

rightsubnet=192.168.2.0/24

rightnexthop=192.168.1.1

# To authorize this connection, but not actually start it, at startup,

# uncomment this.

auto=start

authby=rsasig

leftid=@alpha.uccs.edu

rightid=@lamar.uccs.edu

rightrsasigkey=0sAQOSxZRaWBqtPx3k6rSQ...

leftrsasigkey=0sAQNvPwFQOa...

Details of the setup (2)

(2) Setup an MPLS VPN between the same interfaces.

on alpha :  (ma = alias for /root/mpls-linux-1.1/utils/mplsadm2)

(iptables = /root/iptables-1.2.7a/iptables)

ma -A -O 0

(Key: 0x00000002)

ma -O 0x00000002 -o push:gen:16:set:eth2:ipv4:192.168.1.2

iptables -A OUTPUT -t mangle -d 192.168.1.2/24 -j MPLS --set-key 0x00000002

ma -A gen:16:0

ma -A -I gen:17:0 -i pop:peek

ma -L eth2:0

on lamar :  (ma = alias for /root/mpls-linux-1.1/utils/mplsadm2)

(iptables = /root/iptables-1.2.7a/iptables)

ma -A -O 0

(Key: 0x00000002)

ma -O 0x00000002 -o push:gen:17:set:eth0:ipv4:192.168.1.1

iptables -A OUTPUT -t mangle -d 192.168.1.1/24 -j MPLS --set-key 0x00000002

ma -A gen:17:0

ma -A -I gen:16:0 -i pop:peek

ma -L eth0:0

Details of the setup (3)

Step (3) : Setup appropriate routing entires and firewall (Firewall setup shown in lastpresentation. Just the routing table is shown here)

ON APLHA

Destination     Gateway         Genmask         Flags Metric Ref    Use Iface

128.198.61.0    0.0.0.0         255.255.255.128 U     0      0        0 eth1

128.198.61.0    0.0.0.0         255.255.255.128 U     0      0        0 ipsec1

192.168.2.0     192.168.1.2     255.255.255.0   UG    0      0        0 ipsec2	<---

192.168.1.0     0.0.0.0         255.255.255.0   U     0      0        0 eth2 	<-----

192.168.1.0     0.0.0.0         255.255.255.0   U     0      0        0 ipsec2	<---

192.168.0.0     0.0.0.0         255.255.255.0   U     0      0        0 eth0

192.168.0.0     0.0.0.0         255.255.255.0   U     0      0        0 ipsec0

127.0.0.0       0.0.0.0         255.0.0.0       U     0      0        0 lo

128.198.61.1    0.0.0.0         UG    0      0        0 eth1

ON LAMAR

Destination     Gateway         Genmask         Flags Metric Ref    Use Iface

192.168.2.0     0.0.0.0         255.255.255.0   U     0      0        0 eth2 	<---

192.168.2.0     0.0.0.0         255.255.255.0   U     0      0        0 ipsec2	<---

128.198.60.0    0.0.0.0         255.255.255.0   U     0      0        0 eth1

128.198.60.0    0.0.0.0         255.255.255.0   U     0      0        0 ipsec1

192.168.1.0     0.0.0.0         255.255.255.0   U     0      0        0 eth0	<---

192.168.1.0     0.0.0.0         255.255.255.0   U     0      0        0 ipsec0	<---

192.168.0.0     192.168.1.1     255.255.255.0   UG    0      0        0 ipsec0

127.0.0.0       0.0.0.0         255.0.0.0       U     0      0        0 lo

0.0.0.0         128.198.60.129  0.0.0.0         UG    0      0        0 eth1

On alpha, do a

ping -I 192.168.0.1 192.168.2.3

How it looks on alpha at 192.168.1.1 (eth2)

... on alpha (at 192.168.0.1 i.e. eth0)

... and how it looks on lamar at 192.168.1.2 (eth0)

... and at 192.168.2.2 (eth2) on lamar