Intruder Detection and Isolation Protocol (IDIP)

Application Layer Protocol Definition

Active Networks Intrusion Detection and Response Program

Technical Information Report

February 2002

Prepared Under Contract N66001-00-C-8602 for

SPAWARSYSCEN San Diego

53560 Hull Street
San Diego, California 92152-5410

Prepared By:

| Kelly Djahandari | Dan Schnackenberg |
| --- | --- |
| Brett Wilson | Travis Reid |
| Jason Thorpe( |  |
| NAI Labs | Boeing Phantom Works |
| Network Associates, Inc. | MS 88-12 |
| 3060 Washington Road | PO Box 3999 |
| Glenwood, Maryland 21738 | Seattle, Washington 98124-2499 |

Abstract

This technical report documents the Application Layer of the Intruder Detection and Isolation Protocol (IDIP) developed under DARPA’s Dynamic, Cooperating Boundary Controllers program, Adaptive System Security Policy program, Automatic Response to Intrusion program, and Multicommunity Cyber Defense program. These programs developed and tested concepts for automated intrusion response, including IDIP.  The focus of the Dynamic, Cooperating Boundary Controllers contract was to validate that using IDIP for automated intrusion response enables systems to track network intruders back to their origin and dynamically change network-level access control policies in response to network-based attacks.  The Adaptive System Security Policy program extended the original concepts to develop mechanisms that allow optimal response for various network-based attacks. The response mechanisms adapt to changing threat environments. The Automatic Response to Intrusion program advanced the original concepts by integrating diverse access control, intrusion detection, and network management components into an intruder response system.  The Multicommunity Cyber Defense program extended the ideas further to cooperate across small to very large-scale networks of networks that span numerous administrative domains.

IDIP consists of two distinct layers: the Application Layer and the Message Layer. This layer construct is based on the OSI Protocol Layer Model. This document details the objectives, specification, and operations of the IDIP Application Layer.

1	INTRODUCTION	1

1.1	IDIP Application Layer Objectives	1

1.2	IDIP Application Overview	1

2	IDIP ARCHITECTURE	3

3	IDIP APPLICATION LAYER MESSAGES	4

3.1	IDIP Application Message Header	4

3.2	Core IDIP Messages	8

3.2.1	Trace/Report/Do Message	8

3.2.1.1	Trace Header	9

3.2.1.2	Results Header	9

3.2.1.3	Requested Action Headers	10

3.2.1.4	Extensions	13

3.2.1.5	Trace Data	17

3.2.2	DC Report Message	19

3.2.3	DC Do/DC Do Response Message	20

3.2.4	DC Undo/DC Undo Response Message	20

3.2.5	DC Notify Message	21

3.2.6	Control Message	22

3.2.7	DC Query Message	23

3.2.8	File Transfer Message	23

3.3	DC Internal Messages	24

3.3.1	DC Merge Report	24

3.3.2	Attack-o-Meter Message	28

3.4	Vulnerability Scanning Support Messages	28

3.4.1	Scan Configuration Message	28

3.4.2	Scan Control Message	30

3.4.3	Scan Results Message	30

3.5	Inter-Community Support Messages	32

3.5.1	DC – EBC Messages	32

3.5.1.1	Trace Escalation Message	32

3.5.1.2	EBC Translation Message	34

3.5.2	DC to DC Messages	35

3.5.2.1	DC-to-DC Report Message	36

3.5.2.2	CONE Message	36

3.5.2.3	Alert Sharing Message	39

3.5.3	DC Internal Messages for Inter-Community Support	40

3.5.3.1	Trust Status Message	40

3.6	IDIP Message Requirements	41

4	CISL FORMAT	42

4.1	CIDF Header	45

4.2	CISL Trace/Report  Message	45

4.2.1	ByMeansOf SID	45

4.2.1.1	Attack SID	45

4.2.1.2	SendMessage SID	46

4.2.2	Do SID	46

4.2.2.1	TraceMessage SID	46

4.2.2.2	BlockMessage SID	47

4.2.2.3	AuditMessage SID	47

4.2.2.4	LimitMessage SID	47

4.2.2.5	Request SID	47

4.2.3	Did SID	47

4.2.3.1	TraceMessage SID (Did)	47

4.2.3.2	BlockMessage SID (Did)	48

4.2.3.3	AuditMessage SID (Did)	48

4.2.3.4	LimitMessage SID (Did)	48

4.2.3.5	Request SID (Did)	48

4.3	CIDF Extensions	48

4.3.1	Original Message SIDs	48

4.3.2	MPOG SIDs	49

4.3.3	Local Response Data SIDs	50

4.3.4	Rate Limiting SIDs	50

4.3.5	Detector-Specific SIDs	51

4.3.6	Inter-Community SIDs	52

5	OPERATION	53

5.1	Inbound Messages	53

5.2	Outbound Messages	53

5.3	Core Message Processing	53

5.3.1	Trace/Report Message Processing	53

5.3.1.1	IDIP Agent node	53

5.3.1.2	Discovery Coordinator	53

5.3.2	DC Do	54

5.3.3	DC Undo	54

5.3.4	DC Do Response and DC Undo Response	54

5.3.5	DC Notify	55

5.3.6	DC Control Messages	55

5.3.7	DC Query	55

5.3.8	File Transfer	55

6	REFERENCES	56

A	Appendix: Attack Codes	57

A.1	Penetration Attack Codes	57

A.2	Denial of Service Attack Codes	60

A.3	Unusual Access Attack Codes	61

A.4	Flooding Attack Codes	62

A.5	Probing Attack Codes	62

Figure 1 IDIP Protocol Layering	3

Figure 2 IDIP Application Message Header	4

Figure 3 IDIP Address Description	7

Figure 4 Trace Message	8

Figure 5 Trace Header	9

Figure 6 Results Header	10

Figure 7 Trace Requested Action Header	11

Figure 8 Audit Header	11

Figure 9 Block Header	11

Figure 10 Limit Header	12

Figure 11 Allow Header	12

Figure 12 Local Response Header	12

Figure 13 Trace Extensions	13

Figure 14 Refer Header	14

Figure 15 Response Header	14

Figure 16 Trace Response Header	14

Figure 17 Audit Response Header	15

Figure 18 Block Response Header	15

Figure 19 Limit Response Header	16

Figure 20 Request Response Header	16

Figure 21 Allow Response Header	16

Figure 22Data Format	17

Figure 23 CIDD	17

Figure 24 DC Undo Message	20

Figure 25 Notify Message Header	21

Figure 26 Notify Entry	22

Figure 27 Control Message	23

Figure 28 DC Query Message	23

Figure 29 File Transfer Message	24

Figure 30 Merge Report Message	25

Figure 31 Merge Report ID Description	26

Figure 32 Responder Description	27

Figure 33 Blocking Rule Description	27

Figure 34 Attack Path Description	28

Figure 35 Attack-o-Meter Message	28

Figure 36 Scan Configuration Message	29

Figure 37 Scan Description	29

Figure 38 Scan Control Message	30

Figure 39 Scan Results Message	31

Figure 40 Vulnerability List Description	31

Figure 41 Vulnerability Status Description	31

Figure 42 Trace Escalation Message	33

Figure 43 EBC Translation Message	34

Figure 44 DC-to-DC Message Header	35

Figure 45 CONE Message	37

Figure 46 Alert Sharing Message	40

Figure 47 Trust Status Message	40

Table 1 Application Class IDs	7

Table 2 Local Response Actions	13

Table 3 Protocol Numbers	18

Table 4 IDIP Device Types	21

Table 5 Scan Flags	30

Table 6 Vulnerability Status Values	32

Table 7 DC-to-DC Message Types	36

Table 8 CONE Phases	38

Table 9 CONE Request and Offer Values	39

Table 10 IDIP CISL values	45

| API | Application programmer’s interface |
| --- | --- |
| CIDD | Common IP Datagram Description |
| CIDF | Common Intrusion Detection Framework |
| CISL | Common Intrusion Specification Language |
| CONE | Cooperation Negotiation |
| DC | Discovery Coordinator |
| EBC | Edge Boundary Controller |
| GIDO | Generalized Intrusion Detection Objects |
| ICMP | Internet Control Message Protocol |
| IDIP | Intruder Detection and Isolation Protocol |
| IDS | Intrusion Detection System |
| IP | Internet Protocol |
| LAN | Local area network |
| MPOG | Multi-Protocol Object Gateway |
| NKID | Neighborhood Key Information Distribution |
| OSI | Open Systems Interconnection |
| SID | Semantic Identifier |
| TCP | Transmission Control Protocol |
| UDP | User Datagram Protocol |
| WAN | Wide area network |

# INTRODUCTION

The Intruder Detection and Isolation Protocol (IDIP) Application Layer defines the messages and procedures used by IDIP applications to support intruder isolation and containment. IDIP applications use IDIP Trace messages to describe network-based intrusions. These messages are passed to neighboring IDIP devices to trace the path of the intrusion, and provide the information necessary for each device along this path to determine an appropriate response. Other IDIP application messages are used to support this tracing and response mechanism.

IDIP is designed to minimize the size and number of messages required to support intrusion response. Application Layer messages are primarily sent only after an intrusion has been detected. Once the response has been initiated, the protocol attempts to only send messages to components that potentially could have witnessed part of the attack.  In addition, IDIP components send reports of the responses to a centralized management component called the Discovery Coordinator (DC).

The IDIP Application Layer has been designed to be relatively independent of the other IDIP protocols. These protocols are described in references [1] through [7]. This document defines the IDIP Application Layer.

## IDIP Application Layer Objectives

The IDIP Application Layer objectives include the following.

- Support for autonomous operation by each IDIP response component. This requires that the IDIP Trace message include all information required for IDIP components to determine the appropriate response.

- Support for both local and global policies. The application is not required to comply with a global policy, but the approach allows a central management component to set IDIP system-wide policies.

## IDIP Application Overview

IDIP systems are organized into IDIP communities.  Each community is an administrative domain, with intrusion detection and response functions managed by the Discovery Coordinator.  Communities are furthered organized into IDIP neighborhoods.  These neighborhoods are the collection of components with no other IDIP node between them.  Boundary control devices are members of multiple IDIP neighborhoods.  When an attack traverses an IDIP-protected network, each IDIP node along the path is responsible for auditing the event (i.e., the offending connection or datagram stream).

An IDIP Trace message is forwarded throughout the IDIP nodes when an event or event sequence is detected that is determined to be sufficiently intrusive to warrant a response.   The IDIP node at the detector of the potential attack specifies what type of response is needed.  Each node that gets the trace message can decide whether or not to follow the suggested response or take some other node-specific action based on local policy.  This reaction to the attack is a temporary response until a DC directive is sent.  After processing a Trace message, the IDIP node sends a Report message to the DC.  The Report message is a copy of the Trace message and is sent so that the DC can devise a collective scheme to combat the attack.  Once the DC determines an optimal response, it sends directives out to the nodes that need alerting.  The directives are sent in a DC Do message. This communication is supported through CISL [8] developed by the CIDF working group.  The three IDIP messages that follow the CISL format are the Trace, Report, and Do messages.

There are several types of IDIP devices.  They are the intrusion detection systems (IDS), boundary controllers (i.e., firewalls and routers), edge boundary controls (EBC) (boundary controllers that are at a community boundary), Discovery Coordinators (DC), and agent nodes (end systems). The DC handles the network management and coordinates attack responses.  It handles the distribution of cost models and policy rules.

# IDIP ARCHITECTURE

The IDIP protocol comprises of two main protocol layers: the IDIP Application Layer and the IDIP Message Layer.  The IDIP Application layer performs the application-specific processing and policy related functions (e.g., auditing and blocking).  The IDIP Message Layer performs reliable exchange of IDIP messages across the UDP transport-layer protocol.

| Internet Protocol Suite Layer |  | IDIP Protocol Entity |
| --- | --- | --- |
| Application |  | IDIP Application |
|  |  | IDIP Message (includes NKID and HELLO protocols) |
| Transport |  | UDP |
| Network |  | IP |

Figure 1 IDIP Protocol Layering

The Application layer is the highest level and is responsible for managing the content of IDIP messages.   IDIP applications register with the Message Layer for certain types of Application layer messages.  When a message of the specified type is received, it is forwarded to the Application layer.

When sending a message to another node or to the Discovery Coordinator, the application fills in certain fields of the IDIP Message Layer header[8].  It inserts the version number, the flags to be set, the length of the message, the destination IP address, message priority, application process’ ID and boot time.  It also sends the next header type for the next type field.

The IDIP Application Layer depends on the IDIP Message Layer for reliable delivery of IDIP messages to neighbors and to route IDIP Discovery Coordinator message to and from the Discovery Coordinator node. The Application Layer relies on the Message Layer security and integrity/authentication features. The Application Layer also uses the neighbor time delta mechanism provided by the Message Layer, which determines the delta between the local clock and each neighbor’s clock.

# IDIP APPLICATION LAYER MESSAGES

Most communication in the IDIP Application Layer is based on CIDF’s Common Intrusion Specification Language (CISL) [8].  Along with the use of several of the CISL’s Semantic Identifiers (SIDs), IDIP follows the same encoding and decoding guidelines.

The CISL is based on the use of S-Expressions and SIDs to express information about possible system intrusions.  There are specific rules that are outlined in the CISL definition document[8] on the format and use of S-Expressions.  When encoding and decoding an S-Expression, an IDIP node uses the same encoding and decoding rules of CISL.  The only exception is that IDIP does not require the S-Expression to be canonicalized in lexicographical order, as does CISL.

Upon initialization, each IDIP application registers the types of messages that it will accept from the IDIP Message Layer. Upon receipt of an IDIP application message, if the message is in CISL, the message is decoded from CISL to IDIP data format. If the message is in IDIP wire format, the message is decoded to IDIP data format. Trace, Report, and DC Do messages are encoded into CIDF CISL before giving to the IDIP Message Layer for transmission. This section describes the IDIP data format.

Throughout this protocol specification, all fields are in network byte order.  All headers and lists are 32-bit aligned.  Each attack description must be 32-bit aligned (zero padded).  The length for attack descriptions does not include any trailing padding required to cause the description to be 32-bit aligned.  Throughout this protocol specification, all pad fields are set to 0 on transmission and ignored on receipt.

## IDIP Application Message Header

Figure 2 shows the IDIP application message header format. The subsequent text describes the use of each field specified.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Version | Class ID |
| --- | --- |
| Length (4 octets) |
| Timestamp (4 octets) |
| Thread ID (4 octets) |
| Originator IDIP Address (16 octets) |
| Flags | Pad |
| Timediff (4 octets) |

Figure 2 IDIP Application Message Header

- Version:			Identifies the version of protocol.

IDIP Version: 		0x0010

CIDF Version: 	0x0100

- Class ID:			Class IDs from the CISL and additional IDIP classes. A list of the class IDs is found below in Table 1 Application Class IDs.

| Class ID | Class Name | Description |
| --- | --- | --- |
| 0x0020 | Trace | Agent-to-agent trace message. |
| 0x0022 | Report | Agent-to-DC traceback report message. |
| 0x0024 | Notify | Agent-to-DC neighborhood change message. |
| 0x0027 | Exchange | Agent-to-Agent message of unspecified format. |
| 0x002A | DC Undo | DC-to-agent message to undo a DC directive do response. |
| 0x002C | DC INFOCON | DC-to-agent message to change INFOCON |
| 0x002E | DC Do | DC-to-agent message to take a specified response. |
| 0x0038 | DEFPOS | DC-to-agent message to change DEFPOS |
| 0x003A | DC Do Response | Agent-to-DC response to a DC Do message. |
| 0x003B | DC Undo Response | Agent-to-DC response to a DC Undo message. |
| 0x003E | DC to Agent Set | DC-to-Agent message to set some value. |
| 0x003F | DC to Agent Set Response | Agent-to-DC message response to a DC–to-Agent Set message. |
| 0x0040 | DC to Agent Get | DC-to-Agent message to get some value. |
| 0x0041 | DC to Agent Get Rsp | Agent-to-DC message response to a DC-to-Agent Get message. |
| 0x0042 | DC to AgentD Set | DC–to-agent daemon message to set some value. |
| 0x0043 | AgentD to DC Set Rsp | Agent daemon-to-DC response to a DC to AgentD Set message. |
| 0x0044 | Agent to DC Get | Agent-to-DC message to get some value from the DC. |
| 0x0045 | DC to Agent Get Response | DC-to-Agent response to an Agent-to-DC Get message. |
| 0x0046 | Agent to DC Info | Agent-to-DC message to report status to the DC. |
| 0x0047 | Agent to Agent | Agent-to-Agent message from one agent to another. |
| 0x0048 | DC to DC | DC-to-DC message from one DC to another. |
| 0x0049 | DC to DC Set | DC-to-DC message to set some value. |
| 0x004A | DC to DC Get | DC-to-DC message to get some value. |
| 0x004B | DC to DC Info | DC-to-DC informational message. |
| 0x4001 | Log Request | Internal DC message. Unused but planned for future use. |
| 0x4002 | Log Rsp | Internal DC message. Unused but planned for future use. |
| 0x4003 | State | Internal DC message. Unused but planned for future use. |
| 0x4005 | Merge Report | Internal DC message that represents merged reports. |
| 0x4006 | Merge Undo | Internal DC message to undo report that is associated with an internal merge report. |
| 0x4008 | Attack-O-Meter | Internal DC message to direct changes in its attack-o-meter display. |
| 0x400A | Operational Values | Internal DC message to pass new operational values. |

Table 1 Application Class IDs

- Length:			Length of the header and the following data.

- Timestamp:		Timestamp of the last event that contributed to the message (either by adding to or creating the message).

- Thread ID:			Unique ID of the thread.

- Originator IDIP Address:	Unique identifier information for the originator. The data description is as follows in Figure 3 IDIP Address Description.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

IPv4 Address (4 octets)

Identifier (4 octets)

Boottime (4 octets)

Pad (4 octets)

Figure 3 IDIP Address Description

- IPv4 Address: IP address of the IDIP node.

- Identifier:	Process ID of the IDIP process.

- Boottime:	Boot time of the IDIP node.

- Flags:			Unused.

- Pad:			Zero-padded octets.

- Timediff:			Time difference between nodes. Used only by extensions.

## Core IDIP Messages

The Class ID in the application header corresponds to the message type that follows the application header.  IDIP has a set of core messages.  This section describes these messages.

### Trace/Report/Do Message

Class ID: Trace, Report, DC Do

IDIP Trace, Report and DC Do messages use the same types of headers.  A Report message is simply a copy of a Trace message, and a DC Do is a directive from the DC node to a node in its domain.  This section describes the IDIP formats of the trace message sections, both Report and DC Do messages use parts or all of these sections.  Once the formats are supplied, the node encodes the IDIP format into the CIDF format for delivery.  On receipt, the message can be decoded back to the IDIP format, or any other format.

The IDIP format of the Trace message is shown below in Figure 4 Trace Message.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Results Header (784 octets)

Trace Header (24 octets)

Requested Action Headers

Extension Headers

Data

Figure 4 Trace Message

- Results Header:		Details the information on the attack.

- Trace Header:		Gives information on the auditing of the session or process under investigation.

- Requested Action Header:	Suggested action to take by the originating IDIP node.

- Extension Headers:	Extension headers may or may not be present.  They are added when a node receives a trace and forwards it on to its neighbors and/or sends the report to the DC. The extensions describe the action taken by a node and any translations of data.

- Data:			Details the actual data of the suspected attack.

#### Trace Header

Figure 5 shows the Trace header format. The subsequent text describes the use of each field specified.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Event Count (4 octets)

Examine From (4 octets)

Examine Until (4 octets)

Original Thread ID (4 octets)

Figure 5 Trace Header

- Event count:		Number of events of this type the originating IDIP node saw.

- Examine From:	Examine the audit log from this time.

- Examine Until:	Examine the audit log until this time.

- Original Thread ID:	Unique identification of the original thread.

#### Results Header

The Results header holds the information about the attack for which the trace message or report message is sent out.  Following is the syntax of the Results header.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Severity | Certainty | Outcome |
| --- | --- | --- |
| Attack code (4 octets) |
| Attack start (4 octets) |
| Attack end (4 octets) |
| Observer (256 octets) |
| Attack name (256 octets) |
| Detector Specific (256 octets) |

Figure 6 Results Header

- Severity:		Severity of attack.  0xff is used for unknown.

- Certainty:		Certainty of attack. 0xff is used for unknown.

- Outcome:		Outcome of attack. 0x7fff is used for unknown.

- Attack code:		Code of attack.  See Appendix A for list of attack codes.

- Attack start:		Time of the start of the attack.

- Attack end:		Time of the end of the attack.

- Observer:		String identifying the observer of the attack.

- Attack name:		String representing the detector’s name for the attack.

- Detector Specific:	String representing detector-specific data.

#### Requested Action Headers

The requested action headers contain the information on what the detecting node suggests should be done as a result of the attack.  There can be one or more different types of actions that may be taken at the same time.  The node receiving the trace decides on what actions, if any, are actually taken.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Audit Header

Block Header

Allow Header

Request Header

Limit Header

Figure 7 Trace Requested Action Header

- Audit Header:	This specifies the time interval for an event or group of events to be audited.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Audit From (4 octets)

Audit Until (4 octets)

Figure 8 Audit Header

Audit From:	Timestamp of the start of the audit.

Audit Until:	Timestamp of the end of the audit.

- Block Header:	This specifies the time interval for an event or group of events to be blocked.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Block From (4 octets)

Block Until (4 octets)

Figure 9 Block Header

- Block From:	Timestamp of the start of the block.

- Block Until:	Timestamp of the end of the block.

- Limit Header:	Certain types of attacks, call for limiting the burst rate and average rate of packets being received (e.g., flood attack).  This specifies the time interval, packet and burst rate that an event or group of events is limited.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Limit From (4 octets)

Limit Until (4 octets)

Limit Rate (4 octets)

Burst Rate (4 octets)

Action (4 octets)

Figure 10 Limit Header

- Limit From:	Timestamp of the start of the rate limiting.

- Limit Until:	Timestamp of the end of the rate limiting.

- Limit Rate:	Allowable rate of packets to accept.

- Burst Rate:	Allowable burst rate of packets to accept.

- Action:		Drop packets (value of 0) or queue packets (value of 1).

- Allow Header:	When blocking a group of events the allow header can be used to identify exceptions to the group.  This header specifies the time interval to allow the event or group of events to be allowed to process.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Allow From (4 octets)

Allow Until (4 octets)

Figure 11 Allow Header

- Allow From:	Timestamp of the start of the allow.

- Allow Until:	Timestamp of the end of the allow.

- Request Header:	This is a local message, where an IDS of the node has detected a possible attack.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Action (4 octets)

Request From (4 octets)

Request Until (4 octets)

Figure 12 Local Response Header

- Action:		Action requested by local detector.	The valid values are shown below in Table 2.

| Value | Name | Description |
| --- | --- | --- |
| 1 | No Local Response | No action is to be taken. |
| 2 | Local Response | Local response requested. |
| 3 | Terminated | Terminate the connection, user, process, session, and/or account. |
| 4 | Disabled | Disable connection, user, process, session, and/or account. |
| 5 | Enabled | Enable connection, user, process, session, and/or account. May be used with disabled to disable all with exceptions. |
| 6 | Halted | Halt the node. |
| 7 | Fireback | Respond back to attacking machine. Unused. |
| 8 | Rebooted | Reboot the node. |

Table 2 Local Response Actions

- Request From:		When to start the requested action.

- Request Until:		When to end the requested action.

#### Extensions

An extension is an addendum to a trace that has been forwarded.  Each node adds an extension to a trace message when forwarding it.  The extension describes the node’s response to the trace message and necessary translations, if any.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Extension Header

Refer Header

Response Headers

Figure 13 Trace Extensions

- Extension Header:	The extension header has the same syntax as the application header (see Figure 2 IDIP Application Message Header). The two message types that use the extension are the DC Do Response and a forwarded trace message. The extension is used by the DC to determine the attack path and help with finding the optimal response for each of the nodes.

- Refer Header:	The refer header references who sent the original header, and from whom the trace message was received.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Originator IDIP Address (16 octets)

Thread ID (4 octets)

Received From (4 octets)

Figure 14 Refer Header

- Originator IDIP Address:	IDIP address information of the sender of the trace message. See Figure 3 IDIP Address Description.

- Thread ID:			Thread ID of the original packet.

- Received From:		Reference IP of node who sent request.

- Response Headers:

Response headers are included in the extension, and describe the action taken by the node that is forwarding the trace message.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Trace Response Header

Audit Response Header

Block Response Header

Allow Response Header

Limit Response Header

Request Response Header

Figure 15 Response Header

- Trace Response Header:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Event Count (4 octets)

Examine From (4 octets)

Examine Until (4 octets)

Original Thread ID (4 octets)

I/O In (4 octets)

I/O Out (4 octets)

Figure 16 Trace Response Header

- Event count:		Number of events of this type the originating IDIP node saw.

- Examine From:		Examined the audit log from this time.

- Examine Until:		Examined the audit log until this time.

- Original Thread ID:	Unique identification of the original thread.

- I/O In:			Interface Trace request received.

- I/O Out:			Interface Trace response occurs.

- Audit Response Header

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Audit From (4 octets)

Audit Until (4 octets)

I/O In (4 octets)

I/O Out (4 octets)

Figure 17 Audit Response Header

- Audit From:	Time the audit started.

- Audit Until:	Time the audit will end

- I/O In:		Request interface.

- I/O Out:	Response interface.

- Block Response Header

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Block From (4 octets)

Block Until (4 octets)

I/O In (4 octets)

I/O Out (4 octets)

Figure 18 Block Response Header

- Audit From:	Time the audit started.

- Audit Until:	Time the audit will end

- I/O In:		Request interface.

- I/O Out:	Response interface.

- Limit Response Header

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Limit From (4 octets)

Limit Until (4 octets)

Limit Rate (4 octets)

Burst Rate (4 octets)

Action (4 octets)

I/O In (4 octets)

I/O Out (4 octets)

Figure 19 Limit Response Header

- Limit From:	Time the audit started.

- Limit Until:	Time the audit will end.

- Limit Rate:	Rate of packets per seconds.

- Burst Rate:	Maximum number of packets.

- Action:		Drop or queue packets.

- I/O In:		Request interface.

- I/O Out:	Response interface.

- Request Response Header

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Action (4 octets)

Request From (4 octets)

Request Until (4 octets)

Figure 20 Request Response Header

- Action:		Time the audit started.

- Request From:	Time the audit will end

- Request Until:	Rate of packets per seconds

- Allow Response Header

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Allow From (4 octets)

Allow Until (4 octets)

I/O In (4 octets)

I/O Out (4 octets)

Figure 21 Allow Response Header

- Allow From:	Time the audit started.

- Allow Until:	Time the audit will end

- I/O In:		Request interface.

- I/O Out:	Response interface.

#### Trace Data

Trace data describes the specific information known about the suspected attack.  Trace data is used for the trace information as well as the response requested.  Not every field is required.  There simply needs to be enough information for a node to identify the event.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

CIDD

XCIDD

Session ID

PID

Username

Hostname

Groupname

Procname

Role

ReqSecProto

Figure 22Data Format

- CIDD:	A CIDD is a Common IP Datagram Description.  The information in a CIDD describes the IP header of an attack packet(s). The CIDD is the most common type of Trace data for attack traceback.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| IP Protocol (1 octet) | Protocol Mask (1 octet) |  |
| --- | --- | --- |
| IP Source (4 octets) |
| IP Source Mask (4 octets) |
| IP Destination (4 octets) |
| IP Destination Mask (4 octets) |
| Protocol Port Ranges (10 octets) |

Figure 23 CIDD

- IP Protocol:		IP protocol used.

| Protocol | Number |
| --- | --- |
| ICMP | 0x01 |
| TCP | 0x06 |
| UDP | 0x17 |

Table 3 Protocol Numbers

- Protocol Mask:	Protocol Mask.   If 0, then ignore the IP protocol.

- IP Source:		IP of the source of the attack message.

- IP Source Mask:	Source Mask.  If 0, then ignore the source IP.

- IP Destination:	IP of the destination of the attack message.

- IP Destination Mask:	Destination Mask. If 0, then ignore the destination IP.

- Protocol Port Ranges:  The format of the port ranges depends on the type of protocol used.  The format is shown below.

  - TCP:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| TCP Source Port Min | TCP Source Port Max |
| --- | --- |
| TCP Dest. Port Min | TCP Dest. Port Max |
| Flags | Flags Mask |  |

- TCP Source Port Min:	Minimum TCP source port.

- TCP Source Port Max:	Maximum TCP source port.

- TCP Dest. Port Min:	Minimum TCP destination port.

- TCP Dest. Port Max:	Maximum TCP destination port.

- Flags:			TCP/IP flags.

- Flags Mask:		TCP flags mask

  - UDP:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| UDP Source Port Min | UDP Source Port Max |
| --- | --- |
| UDP Dest. Port Min | UDP Dest. Port Max |

- UDP Source Port Min:	Minimum UDP source port.

- UDP Source Port Max:	Maximum UDP source port.

- UDP Dest. Port Min:	Minimum UDP destination port.

- UDP Dest. Port Max:	Maximum UDP destination port.

  - ICMP:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| ICMP Type | Type Mask | Code | Code Mask |
| --- | --- | --- | --- |

- ICMP Type:		ICMP Type

- Type Mask:		ICMP Type Mask

- Code:			ICMP Code

- Code Mask:		ICMP Code Mask

  - Port:	This is the generic port range syntax.  It can be used for both TCP and UDP.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Source Port Min | Source Port Max |
| --- | --- |
| Dest. Port Min | Dest Port Max |

- Source Port Min:	Minimum source port.

- Source Port Max:	Maximum source port.

- Dest. Port Min:	Minimum destination port.

- Dest. Port Max:	Maximum destination port.

- XCIDD: 		Translated CIDD. The format is the same as the CIDD, but with the translated information.  See Figure 23 CIDD.

- UID: 			User ID

- Session ID: 	Session ID

- PID: 			Process ID

- Username:		Name of user.

- Hostname:		Name of host.

- Groupname: 	Name of group.

- Procname: 		Name of process.

- Role: 			MPOG role. Used when Trace data is in DC Do message.

- ReqSecProto: 	MPOG requires security protocol. Used when Trace data is in DC Do message.

### DC Report Message

Class ID: Report

When a node creates a Trace message, the node sends a copy of the Trace message to the Discovery Coordinator as a DC Report message by changing the Class ID in the application Header to Report.

On receipt of a Report message, the Discovery Coordinator reports the event to applications that register an interest in reports.  These applications perform application-specific processing that may require sending DC Do messages to IDIP nodes.

See Section 3.2.1 for the format of a DC Report message.

### DC Do/DC Do Response Message

Class ID: DC Do, DC Do Response

On sending a DC Do message, the Discovery Coordinator records the message as pending response.  Failure to receive a DC Do Response message indicates failed IDIP components.

On receipt of a DC Do message, a node takes the action specified in the DC Do message, and sends the Discovery Coordinator a DC Do Response message.

See Section 3.2.1 for the format of the DC Do message.

### DC Undo/DC Undo Response Message

Class ID: DC Undo, DC Undo Response

The DC Undo message is a DC to Agent DC directive to an IDIP node to undo a previous response.

On sending a DC Undo message, the Discovery Coordinator records the message as pending response. Failure to receive a DC Undo Response message indicates failed IDIP components.

On receipt of a DC Undo message, a node takes the action specified in the DC Undo message, and sends the Discovery Coordinator a DC Undo Response message.

Figure 24 shows the DC Undo Message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Originator IDIP Address (16 octets) |
| --- |
| Thread ID (4 octets) |
| Succeeded | Pad |

Figure 24 DC Undo Message

- Originator IDIP Address:	IDIP address information of the node that sent the original DC do directive. See Figure 3 IDIP Address Description.

- Thread ID:			Thread ID of the original DC Do directive.

- Succeeded:		Boolean used for the response to an undo directive to indicate if the original DC Do directive was successfully removed.

### DC Notify Message

Class ID: Notify

A node sends the DC a Notify message whenever a neighbor’s state changes (e.g., neighbor becomes unresponsive).

On receipt of a Notify message, the DC updates its state representing the IDIP topology.

A Notify message comprises of a Notify message header and one or more Notify entries.

Notify Header:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Length | Dev Type | Comm Type |
| --- | --- | --- |
| Node IP (4 octets) |

Figure 25 Notify Message Header

- Length: 		Number of bytes in the Notify Header and Notify Entries.

- Device Type:	Bit field describing the type of device of sender. A node can be a combination of these device types. The valid values are found below in Table 4 IDIP Device Types.

| Bit Value | Name | Description |
| --- | --- | --- |
| 0x01 | DC | Device is a Discovery Coordinator. |
| 0x02 | End System | Device is an end system. |
| 0x04 | Router | Device is a network router. |
| 0x08 | Application Proxy | Device is an application proxy. |
| 0x16 | Network IDS | Device is a network intrusion detection system. |
| 0x32 | Remote DC | Device is a remote Discovery Coordinator. |
| 0x64 | Edge | Device is an IDIP edge node. |

Table 4 IDIP Device Types

- Comm Type:	Type of communication used by sender, multicast (value of 1) or unicast (value of 2).

- Node IP:		IP address of the interface to the DC.

Notify Entry:

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Interface (4 octets) |
| --- |
| Identity (4 octets) |
| Time Delta (4 octets) |
| Dev Type | Comm Type | Proxy | Alive |
| Time Signd | Pad |

Figure 26 Notify Entry

- Interface:		IP address of the interface to the neighbor.

- Identity: 		IP address of neighbor.

- Time Delta: 	Time difference between the node and neighbor (in seconds).

- Device Type: 	Bit field describing the type of device of neighbor. A node can be a combination of these device types. See Table 4 IDIP Device Types.

- Comm Type: 	Type of communication, multicast or unicast of neighbor.

- Proxy:		Identifies if neighbor is a proxy to the DC.

- Alive:		Indicates if the neighbor is alive.

- Time Signed:	Indicates if time delta is from signed source.

### Control Message

Class ID: 	DC_INFOCON, DEFPOS

The DC sends an INFOCON or DEFPOS control message to all IDIP components in the Discovery Coordinator’s community when the local INFOCON or DEFPOS level changes.

On receipt of a control message, an IDIP node changes its local control value and takes the local actions required for control changes (e.g., policy change). The value (INFOCON or DEFPOS) that needs to change is specified by the message’s class id.

Figure 27 shows the DC INFOCON and DEFPOS message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Control Value (4 octets)

Figure 27 Control Message

- Control Value: 	Number between 1 and 5 indicating the control value.

### DC Query Message

Class ID: DC-to-Agent Get, Agent–to-DC Get Response

Message Type: Table Update, Get Neighborhood Status

DC sends a DC Query message requesting information from the agent, such as neighborhood status or current blocking table.

Figure 28 shows the DC Query message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Type-Specific Data (variable length)

Figure 28 DC Query Message

- Message Type:		Type of message. This value is either Table Update (value of 4) for sending current blocking table, or Get Neighborhood Status (value of 6) for sending current neighborhood status.

- Type-Specific Data:	For the DC-to-Agent Get message, the data is null. For the Agent-to-DC Get Response message, the data is the neighbor table if Table Update requested, or the neighborhood table if Get Neighborhood Status requested.

### File Transfer Message

Class ID: DC-to-Agent Get Response, DC-to-AgentD Set, DC-to-Agent Set, Agent-to-DC Get

Message Type: Push File, Get File

A node can request a file from the DC using an Agent-to-DC Get message with the Get File message type. Upon receipt of an Agent-to-DC Get message with Get File message type, the DC responds to the request by sending the node the file using a DC-to-Agent Get Response File Transfer message.

A DC can send a node a file, without the node requesting a file. The DC uses a DC-to-Agent Set or DC-to-AgentD Set message with the Push File message type.  This is used to update files, such as sending modified cost models to the agents. Upon receipt of a DC-to-Agent Set or DC-to-AgentD Set message, the agent saves the file then processes its contents.

Figure 29 shows the File Transfer message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Filename (256 octets)

File (variable length)

Figure 29 File Transfer Message

- Message type: 	Type of message. This value is either Push File (value of 1) or a Get File (value of 3).

- Filename:		Name of file being transferred from DC to Agent.  It is a null-terminated ASCII string.

- File:		The file, if the DC is sending a file. Null if the agent is sending a request for a file.

## DC Internal Messages

DC Internal Messages are used to communicate between DC applications.

### DC Merge Report

Class ID: Merge Report, Merge Undo

DC attack reports of ongoing attacks are merged together to create a more comprehensive report. The DC outputs a DC Merge Report for other DC processes to use, such as the process displaying the attack path.

Figure 30 shows the Merge Report message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Merger ID (276 octets) |
| --- |
| Merged ID 0 (276 octets each) … Merged ID 4 |
| Attack ID (4 octets) |
| Start (4 octets) |
| End (4 octets) |
| Protocol | Severity | Pad |
| Min Source Port | Max Source Port |
| Min Target Port | Max Target Port |
| Detector Count (4 octets) |
| Detector 0 (4 octets each) … Detector 5 |
| Responder Count (4 octets) |
| Responder 0 (1 octet each) … Responder 4 |
| Path Count (4 octets) |
| Path 0 (50 octets each) … Path 9 |

Figure 30 Merge Report Message

- Merger ID:		Identification for this merged report. See Figure 31 Merge Report ID for the format.

- Merged IDs:		Previous IDs that have been merged (maximum of 5). The data description is as follows in Figure 31 Merge Report ID.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Originator IDIP Address (16 octets)

Thread ID (4 octets)

From Community (256 octets)

ID (4 octets)

Figure 31 Merge Report ID Description

- Originator IDIP Address: 	Unique IDIP address information of the node. See Figure 3 IDIP Address Description.

- Thread ID: 		Unique identifier of the thread.

- From Community:	Community that is the source of the trace in an EBC-to-EBC trace message. Source of the message in a DC-to-DC report message.  Community is a null-terminated ASCII string.

- ID:				DC-generated ID assigned to attack.

- Attack ID:			Attack ID from the list of attack codes.  See Appendix A.

- Start:			Start time of the attack.

- End:			End time of the attack.

- Protocol:			Attack protocol number. See Table 3 Protocol Numbers.

- Severity:			Attack severity. Range of 0-100 with 100 being highest severity.

- Pad:			Zero-filled bits.

- Min Source Port:		Attack source port range start.

- Max Source Port:		Attack source port range end.

- Min Target Port:		Attack target port range start.

- Max Target Port:		Attack target port range end.

- Detector Count:		Number of detectors listed (maximum of 6).

- Detectors:			IP Addresses of detectors of the attack.

- Responder Count:		Number of responders listed (maximum of 5).

- Responders:		Responders of the attack. The data description is as follows in Figure 32 Responder Description.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Response Node (4 octets)

Merger ID (4 octets)

Response Count (4 octets)

Blocking Rule 0 (38 octets each) … Blocking Rule 3

Figure 32 Responder Description

- Response Node: 	IP address of node that responded.

- Merger ID:		Merged ID of report first placed in.

- Response Count:	Number of blocking rules in report (maximum of 4).

- Blocking Rule:	Description of the response taken. The data description is as follows in Figure 33 Blocking Rule Description.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Type | Pad |
| --- | --- |
| From (4 octets) |
| Until (4 octets) |
| Blocks (28 octets) |

Figure 33 Blocking Rule Description

- Type: 		Type of blocking response.

Block UID	1

Block SID	2

Block PID 	3

Block CIDD	4

- From:		Time response initiated.

- Until:		Time response ends.

- Blocks:	The CIDD or ID blocked depending on the blocking type.

- Path Count:	Number of paths listed (maximum of 10).

- Path:		Path of the attack. The data description is as follows in Figure 34 Attack Path Description.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Node 0 (4 octets each) … Node 11

Length (4 octets)

Direction (4 octets)

Figure 34 Attack Path Description

- Node:		IP Addresses of nodes in attack path.

- Length:	Length of path.

- Direction:	Direction of the attack along the path. If direction is source to target, the value is greater than 0. If the direction is unknown, the value is 0. If the direction is target to source, the value is less than 0.

### Attack-o-Meter Message

Class ID: Attack-O-Meter

Internal DC message used to change the attack-o-meter display.

The Attack-o-Meter message format is described below in Figure 35.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Value (4 octets)

Figure 35 Attack-o-Meter Message

- Value:	Attack-o-Meter value, ranges from 0 to 99 (inclusive).  0 being the lowest.

.

## Vulnerability Scanning Support Messages

Vulnerability Scanning Support Messages are used to inform the scanner node what to scan and inform responder nodes when a vulnerability scan is to occur.

### Scan Configuration Message

Class ID: DC-to-Agent Set

Message Type: Scan Config

This is a  message from the DC to a scanner to schedule a scan or remove a scan request from the schedule.

Figure 36 shows the Scan Configuration message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Scan Handle (4 octets)

Time (4 octets)

Delta (4 octets)

Scan List: Scan Description 0 (4 octets each) … Scan Description 3

Figure 36 Scan Configuration Message

- Message Type:	Message type of Scan Config (value of 4).

- Scan Handle:	A DC assigned handle for a scan schedule.  It is used when the DC wants to remove a scan from the schedule.

- Time:		When to scan the first time.

- Delta:		Repeat scan every delta seconds.

- Scan List:		The scan list is comprised of 4 scan descriptions, one for each IP address to be scanned. Figure 37 shows the syntax of a scan description.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Scan Set (4 octets)

IP (4 octets)

Vulnerability ID 0 (4 octets each) … Vulnerability ID 699

Figure 37 Scan Description

- Scan Set:	Flag to allow special sets of scans.  It is an integer value.  Table 5 Scan Flags lists the possible values.

| Value | Name | Description |
| --- | --- | --- |
| 1 | Normal | Perform all scans listed. |
| 2 | Default | Perform all default scans. |
| 3 | As Above | Perform the same set of scans as previous scan description in the scan list. |
| 4 | All Scans | Perform all available scans. |
| 5 | All But | Perform all but listed scans. |
| 6 | Class C | Perform scan on all addresses in a Class C network. |

Table 5 Scan Flags

- IP:			IP address of node to be scanned.

- Vulnerability ID:	Identifies the vulnerability to scan for on a node.

### Scan Control Message

Class ID: Agent-to-agent

Message Type: Start Scan, Stop Scan

This is a message from one IDIP node to another, to notify the node of a vulnerability scan is to start or that a scan is finished.

Figure 38 shows the Scan Control message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Scan List: Scan Description 0 … Scan Description 3

Figure 38 Scan Control Message

- Message Type:	This either notifies that the scan is to be stopped (value of 1) or that it is to be started (value of 2).

- Scan List:		Describes scans to be performed or finished.  See Figure 37 Scan Description

### Scan Results Message

Class ID: Agent-to-DC Info

Message Type: Scan Results

When an agent has the results of a vulnerability scan, the results are sent to the DC using a Scan Results message. The DC uses this information to change response policy.

Figure 39 shows the Scan Results message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Vulnerability List (variable length)

Figure 39 Scan Results Message

- Message Type:		Message type of Scan Results (value of 5).

- Vulnerability List:		List of the vulnerability scan results. The end of the list is marked by a zero-filled entry.  Figure 40 shows the vulnerability list format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

IP (4 octets)

Vulnerability Status 0 (8 octets) … Vulnerability Status 699

Figure 40 Vulnerability List Description

- IP:		IP address of node scanned.

- Vulnerability Status: 	List of vulnerabilities and the status of the node for that vulnerability. The vulnerability status has the data format shown in Figure 41.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Vulnerability ID (4 octets)

Status (4 octets)

Figure 41 Vulnerability Status Description

- Vulnerability ID:	The vulnerability scanner’s id for the vulnerability.

- Status:		Status of the scan.  List of values is shown below in Table 6.

| Value | Name | Description |
| --- | --- | --- |
| 1 | Not Tested | Vulnerability test of that vulnerability not performed. |
| 2 | Not Vulnerable | Node is not vulnerable to that vulnerability. |
| 3 | Vulnerable | Node is vulnerable to that vulnerability. |

Table 6 Vulnerability Status Values

## Inter-Community Support Messages

### DC – EBC Messages

Messages between a Boundary Controller on the edge of a community (Edge Boundary Controller (EBC)) and its DC are described here.

#### Trace Escalation Message

Class ID: Agent-to-DC Get, DC-to-Agent Get Response

Message Type: Trace Escalation

When an EBC receives a Trace message from inside its community and determines the attack path is through it or an EBC receives a Trace message from outside its community, the EBC checks its policy as to what it should do with the Trace message. If the policy is to Ask Operator, the EBC sends a Trace Escalation message to its DC to request what action it should take with the trace message. On receipt of a Trace Escalation message, the DC gets operator input as to the action the EBC should take. The operator response to continue or terminate is sent back to the EBC in a Trace Escalation Response message. A new EBC policy may also be included in the response message.

The Trace Escalation message follows the IDIP Application Header. The Trace Escalation message format is shown in Figure 42.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Trace ID (4 octets)

EBC IP Address (4 octets)

Name (256 octets)

Message Direction (4 octets)

Message Severity (4 octets)

Message Certainty (4 octets)

Message Attack ID (4 octets)

Trace Status (4 octets)

Policy Size (4 octets)

Figure 42 Trace Escalation Message

- Message Type:		Message Type of Trace Escalation (value of 8).

- Trace ID:			Unique trace message ID.

- EBC address:		IP address of the edge boundary controller.

- Name:			Name of community trace message is ‘going to’ or ‘coming from’.

- Message Direction:	Defines if the message is an inbound or outbound message.

Inbound:	1

Outbound:	2

- Message Severity:		Trace message severity, number from 0-100.  The higher the value the more severe.

- Message Certainty:	Trace message certainty, number from 0-100.  The higher the value, the more certain.

- Message Attack ID:	Attack ID in the Trace message.

- Trace Status:		Used in the DC response. An Approve Trace response will continue the traceback.  A Reject Trace response will terminate the traceback.

Reject Trace:		1

Approve Trace:	2

- Policy Size:		The size of a policy file, if appended. If no policy file is appended, the policy size is 0.

#### EBC Translation Message

Class ID: Agent-to-DC Info

Message Type: New EBC Translation

The Edge Boundary Controller (EBC) sends an EBC Translation Message to its DC if it makes changes to the trace message before continuing the trace message to/from a remote community.  The EBC can translate IP addresses to hide internal network address information. If the translation occurs, the DC needs to know about the changes to apply to the DC-to-DC report message from the remote community.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Community (256 octets)

Local Address (16 octets)

Remote Address (16 octets)

Local Thread ID (4 octets)

Remote Thread ID (4 octets)

Local Path 1 (4 octets) … Local Path IP 12 (4 octets)

Remote Path 1 (4 octets) … Remote Path 12 (4 octets)

Local Path Length (4 octets)

Remote Path Length (4 octets)

Figure 43 EBC Translation Message

- Message Type:		Message type of New EBC Translation (value of 12).

- Community:		The destination community on an outgoing trace message. The source community on an incoming trace message. Community is a null-terminated ASCII string.

- Local Address:		Local address information of originator.

- Remote Address:		Translated address information of originator of trace message.

- Local Thread ID:		Local Thread ID.

- Remote Thread ID:	New Thread ID used for trace message.

- Local Paths:		Local community IP addresses of traceback path.

- Remote Paths:		Translated IP addresses of traceback path.

- Local Path Length:	Number of IP addresses in local path.

- Remote Path Length:	Number of IP addresses in remote path.

### DC to DC Messages

A DC-to-DC Message is sent from one community’s DC to another community’s DC. A DC-to-DC message comprises of a DC-to-DC Message header and a message.  The data in the message depends on the message type.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Message Type (4 octets)

Community Name (256 octets)

Remote DC (4 octets)

Figure 44 DC-to-DC Message Header

- Message Type: 		Type of DC-to-DC Message. The valid values are listed below in Table 7.

| Value | Name | Description |
| --- | --- | --- |
| 0x09 | DC-to-DC | DC to DC message |
| 0x0A | DC-to-DC Report | Merged traceback report |
| 0x0B | Cone Protocol | Cooperation Negotiation message |
| 0x0D | Alert Sharing | Alert Sharing message |
| 0x0E | Correlator Data | Correlation data sharing message |

Table 7 DC-to-DC Message Types

- Community Name:	Name of the community sending the message.

- DC Remote: 		IP address of remote Discovery Coordinator. Unused.

#### DC-to-DC Report Message

Class ID: DC-to-DC INFO

Message type: DC-to-DC Report

DC-to-DC report messages are used to collect information from different communities about a single attack.  DC attack reports of ongoing attacks are merged together to create a more comprehensive report. Before the DC sends a report message, the information may be sanitized, based on the policy for sending reports to the other community.

The DC-to-DC Report message consists of the Application Header, followed by the DC-to-DC message header, followed by the Merge Report message as shown in Figure 30.

#### CONE Message

Class ID: DC-to-DC

Message type: CONE

The Cooperation Negotiation message is sent from one community DC to another community DC to negotiate intrusion traceback and response services.  On receipt of a CONE message, the DC gets operator input for the need of services such as traceback, report, blocking, propagation, alert sharing, and correlation data sharing. The negotiation continues until one of the communities accepts or rejects the proposed service offering and requirements.

The CONE message header follows the DC-to-DC message header. Figure 45 describes the CONE message.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

| Message Type (4 octets) |
| --- |
| Version | Phase | Sequence Number |
| Originating Community (256 octets) |
| Trace & Rpt Req (1 octet) | Trace & Rpt Offer (1 octet) | Trace & Block Req (1 octet) | Trace & Block Offer (1 octet) |
| Limit Traceback Req (1 octet) | Limit Traceback Offer (1 octet) | Send Intrusion Alert Req (1 octet) | Send Intrusion Alert Offer (1 octet) |
| Send Anomalous Events Req (1 octet) | Send Anomalous Events Offer (1 octet) |  |
| Text Message (256 octets) |

Figure 45 CONE Message

- Message Type:	Type of message. Cone Message has the value of CONE Protocol, a value of 11.

- Version: 		Version of CONE protocol.

- Phase:		Phase of the negotiation. The valid values are listed below.

| Value | Name | Description |
| --- | --- | --- |
| 0x00 | None | No negotiation |
| 0x01 | Initiator Proposal | Initiator offer |
| 0x02 | Responder Proposal | Responder offer |
| 0x03 | Initiator Accept | Initiator initially accepts proposal |
| 0x04 | Initiator Accept Final | Initiator accepts responder-accepted proposal |
| 0x05 | Initiator Terminate | Initiator terminates negotiation |
| 0x06 | Responder Accept | Responder initially accepts proposal |
| 0x07 | Responder Accept Final | Responder accepts initiator-accepted proposal |
| 0x08 | Responder Terminate | Responder terminates negotiation |

Table 8 CONE Phases

- Sequence Number: 	Sequence number of message.

- Originating Community:	Name of sender’s community as a null terminated ASCII string.

- Trace & Rpt Req:		Trace and Report request value. The sender specifies if it requests the other community to continue traceback messages from the sender’s community and to report the status of the traceback to the sender’s community.

- Trace & Rpt Offer:	Trace and Report offer value. The sender specifies if the sender’s community will continue traceback messages from the other community and to report the status of the traceback to the other community.

- Trace & Block Req:	Trace and Block request value. The sender specifies if it requests the other community to perform the traceback and suggested response if the other community is along the attack path.

- Trace & Block Offer:	Trace and Block offer value. The sender specifies if the sender’s community will perform the traceback and suggested response if the sender’s community is along the attack path.

- Limit Traceback Req: 	Propagation request value. The sender specifies if it wants the other community to limit traceback to its community boundary.

- Limit Traceback Offer:	Propagation offer value. The sender specifies if the sender’s community will limit traceback to its community boundary.

- Send Intrusion Alert Req:		Send Intrusion Alert request value. The sender specifies if it requests intrusion alert messages from the other community.

- Send Intrusion Alert Offer: 	Send Intrusion Alert offer value. The sender specifies if it will send intrusion alert messages to the other community.

- Send Anomalous Events Req:	Send Anomalous Events request value. The sender specifies if it requests correlation data from the other community.

- Send Anomalous Events Offer:	Send Anomalous Events offer value. The sender specifies if it will send correlation data to the other community.

The CONE request and offer values are listed below.

| Value | Name | Value for |
| --- | --- | --- |
| 0x00 | None | Request or Offer |
| 0x01 | Yes | Request or Offer |
| 0x02 | Ask Operator | Request or Offer |
| 0x04 | Preferred | Request only. |
| 0x08 | Non Essential | Request only. |
| 0x10 | No | Request or Offer |

Table 9 CONE Request and Offer Values

- Text Message:	Optional text message.

#### Alert Sharing Message

Class ID: DC-to-DC Info

Message types: Alert Sharing, Correlator Data

The Alert Sharing message is used to exchange correlation data or intrusion detection alert information between DCs in different communities.  The message is sent out to all participating communities.  Participating communities are those that allow alert messages according to their community policy.

The Alert Sharing message follows the DC-to-DC message header. Figure 46 shows the Alert Sharing message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Originating Community (256 octets)

Data Length (4 octets)

Type-Specific Data (variable length)

Figure 46 Alert Sharing Message

- Originating Community:		Sender’s community name as a null-terminated ASCII string.

- Data Length:			Length of Type-Specific data in octets.

- Type-Specific Data:		Variable-length alert or correlator data.

### DC Internal Messages for Inter-Community Support

#### Trust Status Message

Class ID: Trust Notify

The Trust Status message is used to notify DC applications when the trust status of a community has changed.

The Trust Status message follows the IDIP Application Header. Figure 47 shows the Trust Status message format.

1	2	3

0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1	2	3	4	5	6	7	8	9	0	1

Community (256 octets)

Status (4 octets)

Figure 47 Trust Status Message

- Community:	Community Name as a null-terminated ASCII string.

- Status:		New trust status.

High Trust		90

Medium Trust		50

Low Trust		10

## IDIP Message Requirements

Each Application Layer message must meet a set of minimal requirements.  In general, each message must contain a valid class id and valid length fields.  The length of the message must also match with the specified size of the format.  In addition, each class of messages may have certain aspects that must be correct for the message to be processed.

Trace, Report, and DC Do messages must follow the CISL format.  A CISL message is composed of a CISL header, followed by one or more GIDO’s.  The size of the message must be at least the size of the CIDF header. Each GIDO must in turn be large enough to hold the SID and the GIDO length.

In addition to conforming to the specified length requirements, each GIDO must contain a valid SID. SID data that is in the form of null-terminated strings must be at least the size of one character and not greater than the max value.

# CISL FORMAT

CIDF’s CISL [8] is used to transport IDIP Trace, Report, and DC Do messages from one IDIP node to another.  The on-the-wire format is the octet break down of the SID. IDIP data format is encoded into CISL before sending a Trace, Report, or DC Do message to another IDIP node.

The CISL S-Expression GIDOs (Generalized Intrusion Detection Objects) are built from the IDIP format to be transmitted.  GIDO fields are of the form (length, SID, data).  Each IDIP format header (described in Section 3) or segment of data in the message is encoded into a GIDO.

The following is a table of the CISL values used in IDIP.

| Name | SID |
| --- | --- |
| And | 0x08004001 |
| Allow MPOG | 0x08B0E005 |
| Attack | 0x08000081 |
| Attack ID | 0x06000073 |
| Attack Name | 0x04B0E013 |
| Attack Specifics | 0x08001014 |
| Audit Path | 0x08001065 |
| Audit Message | 0x08000072 |
| Begin Time | 0x02000002 |
| Block Account | 0x08B0E00b |
| Block Message | 0x08000073 |
| Block MPOG | 0x08B0E004 |
| Block Path | 0x08001066 |
| By Means Of | 0x08004007 |
| Certainty | 0x00000006 |
| CIDF Originator | 0x04B0E002 |
| CIDF Return Code | 0x01000008 |
| Copy | 0x08000001 |
| Detector Specific Data | 0x04B0E014 |
| Did | 0x08000824 |
| Do | 0x08000811 |
| End Time | 0x02000003 |
| Entering New Community (IDIP extension) | 0x08B0E015 |
| Execute | 0x08000011 |
| Filename | 0x04000012 |
| File Source | 0x08001021 |
| Fireback | 0x08B0E00d |
| Groupname | 0x04000024 |
| Hostname | 0x0400000c |
| Initiator | 0x08001001 |
| Limit Message | 0x08B0E00d |
| Local Response | 0x08B0E00c |
| Machine | 0x08001043 |
| Message | 0x08001051 |
| MPOG Role | 0x04B0E006 |
| MPOG Security Protocol | 0x04B0E007 |
| Multiplier | 0x0200007b |
| Observer | 0x08001003 |
| Outcome | 0x08005001 |
| Process | 0x08001011 |
| Process ID | 0x02000027 |
| Process name | 0x04000028 |
| Rate | 0x08B0E00f |
| Reboot | 0x08000091 |
| Refer To GIDO (IDIP extension) | 0x02000078 |
| Request | 0x08000801 |
| Send Message | 0x08000041 |
| Session ID | 0x02B0E00a |
| Severity | 0x00000007 |
| Shutdown | 0x08000092 |
| Source IP Address | 0x0200003b |
| Target | 0x08001004 |
| Terminate | 0x08000014 |
| Thread ID | 0x02B0E003 |
| Trace Message | 0x08000074 |
| Trace Path | 0x08001062 |
| Translate | 0x08000821 |
| User ID | 0x0200001f |
| Username | 0x0400001c |
| When | 0x08005002 |

Table 10 IDIP CISL values

The following briefly describes the conversion from IDIP format to CISL.

## CIDF Header

CIDF header information comes from the IDIP header information. Following the CIDF header is the CISL encoded IDIP Trace, Report, or DC Do message.

## CISL Trace/Report  Message

A Trace or Report message describes the attack and actions to take by combining ByMeansOf SID with Do SIDs using an And SID.

### ByMeansOf SID

ByMeansOf SID describes the attack (Attack SID) and the cause of the attack (SendMessage SID).

#### Attack SID

The Attack SID describes the specific attack information such as the observer (Observer SID), the target (Target SID), the certainty, the severity, the attack id (AttackSpecifics SID), the outcome of the attack (Outcome SID), and the time of the attack (When SID).

- Observer SID - consists of the ProcessName SID. The ProcessName comes from the IDIP observer field in the Results header (see Figure 6).

- Target SID - describes the attack destination, which can be an IPV4Address SID and/or a HostName SID. The IPV4 address comes from the IDIP CIDD data field IPdestination.  The HostName SID comes from the Hostname Trace data. See Section 3.2.1.5 for more information about Trace data.

- AttackSpecifics SID - describes the attack. The AttackSpecifics SID values come from the Results header (see Figure 6).  It can include:

- Certainty SID – value from the certainty field.

- Severity SID – value from severity field.

- AttackID SID – value from attack_code field.

- AttackName SID – value from attack_name field.

- DetectorSpecificData SID – value from detector_specific field.

- Outcome SID - describes the attack outcome. The Outcome SID contains the CIDFReturnCode SID whose value come from the outcome field in the Results header (see Figure 6).

- When SID - When used in the Attack description, the When SID describes the time of the attack. It gets its values from the Attack Start and Attack End fields in the Results header (see Figure 6).

#### SendMessage SID

The SendMessage SID describes the message specifics of the attack. The SendMessage SID may contain an Initiator SID, Receiver SID, Message SID, and When SID.

- Initiator SID - data comes from the Trace data. Initiator SID may contain the following SIDs:

- SourceIPV4Address – value from IPsource in CIDD data field.

- UserID – value from UID data field.

- ProcessID – value from PID data field.

- SessionID – value from SID data field.

- UserName – value from Username data field.

- GroupName – value from Groupname data field.

- ProcessName – value from Procname data field.

- Receiver SID - data comes from the Trace data. Receiver SID may contain the DestinationIPV4Address SID that gets its value from the IPdestination data field in the IDIP CIDD data. The Receiver SID may also contain the UserID, ProcessID, SessionID, UserName, GroupName, or ProcessName SIDs like the Initiator SID.

- Message SID - Message SIDs get their data from the Trace data and Results header. The Message SID may contain the following SIDs:

- IPV4Protocol – value from CIDD data field.

- DestinationIPV4Address – value from CIDD data field.

- Multiplier – If the event count is more than one (from the Trace header), the Multipler SID is used.

- When SID- The When SID in the SendMessage SID gets its data from the Trace header Examine From and Examine Until fields (see Figure 5).

### Do SID

The Do SID includes the requested actions. There are usually multiple Do SIDS in a Trace or Report message. There is a separate Do SID clause for each TraceMessage SID, BlockMessage SID, AuditMessage SID, LimitMessage SID, and local response Request SID.

#### TraceMessage SID

The TraceMessage SID includes the timeframe used for traceback (When SID), a description of the attacker (Initiator SID), and the attack description information (Message SID). The Message SID uses a ReferTo SID to not replicate the attack description data. The TraceMessage SID may include an Initiator SID (see above description of Initiator SID). The When SID contains the Examine From and Examine Until values from the Trace Header (see Figure 5).

#### BlockMessage SID

The BlockMessage SID includes the timeframe to block (When SID) and the block request information (Message SID). The Message SID data comes from the IDIP Trace data, and is usually the CIDD data (see Figure 23). The When SID contains the Block From and Block Until values from the Block Header (see Figure 9).

#### AuditMessage SID

The AuditMessage SID includes the timeframe to audit (When SID) and the audit request information (Message SID). The Message SID data comes from the IDIP Trace data, usually the CIDD data (see Figure 23). The When SID contains the Audit From and Audit Until values from the Audit Header (see Figure 8).

#### LimitMessage SID

The LimitMessage SID includes the timeframe to rate limit (When SID) and the limit request information (Message SID). The Message SID data comes from the IDIP Trace data, usually the CIDD data (see Figure 23) and the rate limiting data (LimitRate, BurstRate, Action) from the Limit header. The When SID contains the Limit From and Limit Until values from the Limit header (see Figure 10).

#### Request SID

The Request SID specifies the local response request. The Request SID includes the timeframe of the request (When SID) and the specific local responses (Local_Response, Terminate, Fireback, Rebooted, and Halted SIDs)

### Did SID

The Did sentence specifies the response taken. The IDIP extensions are expressed in a Did SID. The Did sentence may be composed of a TraceMessage SID, BlockMessage SID, LimitMessage SID, AuditMessage SID, and Request SID. These SIDs used in the Did sentence have additional information from the Do sentence SIDs.

#### TraceMessage SID (Did)

The TraceMessage SID includes the thread id (ThreadID SID), attack outcome (Outcome SID), TracePath SID, translated time (When SID using attack start and end times from Results header (Figure 6)), and attack description information (Message SID).

The TracePath SID may contain the following SIDs:

- ReceivedFrom – IPv4 address of the sending node (from Received From field in Refer header (Figure 14)).

- ReceivedVia – IPv4 interface address on which Trace message received (from I/O In field in Response header (Figure 15)).

- IPV4Path – Array of two IPv4 addresses indicating path through IDIP node (from I/O In and I/O Out fields in Response header).

#### BlockMessage SID (Did)

The BlockMessage SID includes the BlockPath SID, the timeframe of blocking (When SID) and the block information (Message SID). The Message SID data comes from the IDIP Trace data, and is usually the CIDD data (see Figure 23). The BlockPath SID contains an array of two IPv4 addresses indicating the blocked path through the IDIP node (from I/O In and I/O Out fields in Trace Response header (Figure 16)).

#### AuditMessage SID (Did)

The AuditMessage SID includes the AuditPath SID, the timeframe of auditing (When SID) and the audit information (Message SID). The Message SID data comes from the IDIP Trace data, usually the CIDD data (see Figure 23). The When SID contains the Audit From and Audit Until values from the Audit Header (see Figure 8). The AuditPath SID contains an array of two IPv4 addresses indicating the audited path through the IDIP node (from I/O In and I/O Out fields in the Trace Response header (Figure 16)).

#### LimitMessage SID (Did)

The LimitMessage SID includes the LimitPath SID, the timeframe of the rate limiting (When SID) and the limit request information (Message SID). The Message SID data comes from the IDIP Trace data, usually the CIDD data (see Figure 23) and the rate limiting data (LimitRate, BurstRate, Action) from the Limit header. The When SID contains the Limit From and Limit Until values from the Limit header (see Figure 10).  The LimitPath SID contains an array of two IPv4 addresses indicating the rate limited path through the IDIP node (from I/O In and I/O Out fields in the Trace Response header (Figure 16)).

#### Request SID (Did)

The Request SID specifies the local response request. The Request SID includes the outcome (Outcome SID), the timeframe of the request (When SID) and the specific local responses (Local_Response, Terminate, Fireback, Rebooted, and Halted SIDs)

## CIDF Extensions

IDIP had to extend the CISL language with the following SIDs.

### Original Message SIDs

All IDIP application messages have an originator that identifies the source of the message. There is also a unique thread identifier. These CISL extensions are needed for indicating the IDIP originator of a message and for one message to refer to another message. These SIDs extended CISL for unique IDIP originator information.

Name: ReferToGido

Code: 0x08B0E001

Type:  attribute

Description: Used to reference the original packet.

May Contain: CIDFOriginator, ThreadID

Name: CIDFOriginator

Code: 0x04B0E002

Type: array of bytes

Description: Description of the message originator. Contains three components, the first is the IP address of the originator node, the second is the process id of the originator process, and the third is the boot time of the originating node.

Name: ThreadId

Code: 0x02B0E003

Type: ulong

Description: Unique identifier for the thread.

### MPOG SIDs

Multi-Protocol Object Gateway (MPOG) is a security gateway for CORBA and Java RMI traffic. MPOG acts as an application firewall proxy to protect CORBA and Java RMI servers by providing selective access to them by remote clients.  MPOG is another IDIP boundary controller device. The following SID extensions were needed for MPOG. These SIDs extended CISL for MPOG-specific responses.

Name: BlockMPOG

Code: 0x08B0E004

Type: Verb

Description: Specified entities to be blocked or were blocked by MPOG.

May Contain: MPOG_Role, MPOG_Securitiy_Protocol, UserName, Account

Name: AllowMPOG

Code: 0x08B0E005

Type: Verb

Description: Specified entities to be allowed or were allowed by MPOG.

May Contain: MPOG_Role, MPOG_Securitiy_Protocol, UserName, Account

Name: MPOG_Role

Code: 0x04B0E006

Type: String

Description: The MPOG RoleName.

Name: MPOG_Security_Protocol

Code: 0x04B0E007

Type: String

Description: Security Protocol required by MPOG.

### Local Response Data SIDs

These SIDs extended CISL for IDIP local responses.

Name: SessionID

Code: 0x02B0E00a

Type: ulong

Description: The ID number of a session.

Name: BlockAccount

Code: 0x08B0E00b

Type: role

Description: Describes entities to be blocked or were blocked.

May Contain: UserName, UserID, GroupName, FileName, Did

Name: Local_Response

Code: 0x08B0E00c

Type: role

Description: Describes the local node response data.

May Contain: Account Data (UserName, GroupName, UserID, or Account), Process Data (ProcessID, SessionID, ProcessName), or Connection Data.

Name: Fireback

Code: 0x08B0E00d

Type: verb

Description: Send a response attack to an attacking machine. Unused.

### Rate Limiting SIDs

These SIDs extended CISL for IDIP rate limiting responses.

Name: LimitMessage

Code: 0x08B0E00e

Type: verb

Description: Specified messages are rated limited.

May Contain:

When: This contains the time at which (or during which) the rate limiting was performed.

LimitPath: The path(s) being rate limited.

Message: The message(s) being rate limited.

Rate: The rate limiting values.

Name: LimitPath

Code: 0x08001067

Type: role

Description: Information about how a component rate limited an event.

May Contain:

IPV4Path: Contains two elements, the first representing the connection into the component, the second the connection out of the component that the specified audit is being performed on.

Name: Rate

Code: 0x08B0E00f

Type: adverb

Description: Describes the rate limiting.

May Contain: LimitRate, BurstRate, Action

Name: LimitRate

Code: 0x02B0E010

Type: ulong

Description: The maximum packets per second at which to transmit packets.

Name: BurstRate

Code: 0x02B0E011

Type: ulong

Description: The maximum number of packets that can be transmitted at one time. If the BurstRate is reached, packets are filtered.

Name: Action

Code: 0x02B0E012

Type: ulong

Description: Rate Limit Action: drop packets or queue packets.

### Detector-Specific SIDs

These SIDs extended CISL for when a detector needs to add additional information not currently in IDIP.

Name: AttackName

Code: 0x04B0E013

Type: String

Description: String representing the detector’s name for the attack.

Name: DetectorSpecificData

Code: 0x04B0E014

Type: String

Description: String representing detector-specific data.

### Inter-Community SIDs

This SID extended CISL to indicate a message came from another community.

Name: EnteringNewCommunity

Code: 0x08B0E015

Type: role

Description: Indicates message received from another community

May Contain:

DomainName: String indicating the community name.

SourceIPV4Address: The source address of the inter-community message.

DestinationIPV4Address: The destination address of the inter-community message.

# OPERATION

## Inbound Messages

Upon initialization, each IDIP node registers the types of message classes that it will accept.

## Outbound Messages

When sending out an IDIP message, the Application Layer fills out the IDIP header information.  When sending a message, the application fills in certain fields of the IDIP Message Layer header[8].  It inserts the version number, the flags to be set, the length of the message, the destination IP address, message priority, application process’ ID and boot time.  It also sends the next header type for the next type field.

For most IDIP response messages, the syntax is the same as the initial message.  The difference is in the class field, which indicates that it is a response message.

## Core Message Processing

### Trace/Report Message Processing

#### IDIP Agent node

On receipt of a Trace message, an IDIP agent node searches its audit trail for events matching the attack description.  If a match is found, the node

- Determines the response that will be done by the node and enacts the response.

- Forwards the trace request to all neighbors along the attack path.  This forwarded trace message must include addendums that describe the response taken, plus any translation required.

- Sends a copy of the trace message as a report message to the Discovery Coordinator.

If the node does not find a match because the node was not monitoring for the data, the node sends a trace message out each interface and a report to the Discovery Coordinator.

If the node does not find a match and was monitoring for the data, the node only sends a report to the Discovery Coordinator.

#### Discovery Coordinator

When a DC receives a report from an agent node, the DC merger process stores the report in a database.  It also combines like attacks into an internal report.  If the originator of the report matches an existing database entry, the new report is merged with the database entry.  Then it checks the database for any overlaps.   If the report was merged with a database entry, then check the merged report for a match with the database.  If there is a match, then merge the data entry with the merged reports.  If the original report was not merged with a database entry, create a new entry with a new report ID. After the report sent in is processed the node decides if it should send an internal report out.  If the report sent in is valid and all of its information not already covered in another report, an internal report is sent out to the other DC applications.

### DC Do

The IDIP Application layer uses the CIDF’s CISL’s Do message.  The message follows the same basic structural format of a Trace or Report message.  The block/allow/limit directives are given in the block/allow/limit headers.

Upon receiving a DC Do message, an agent node extracts the results header and refer header.  Next it extracts all the block headers.  For each block header, the node adds the specified instance to its block database to be blocked.  It uses the block from and block to fields to determine how long to block.  Afterwards it adds a block response to the outgoing message for each block header it receives.  The same thing is done for the allow headers.  The allow header, allows for exceptions to the block command.  For example, a block directive will command that a group of sessions, except for two specific ones in that group, to be blocked.  The group will be described in the block header, while the exceptions will be shown in an allow header or headers.  Limit headers are also extracted.  Valid headers are added to the block database, with the limit information that is sent in the limit header.  The agent node also searches for local request headers.  When found, the node completes the request.

The block/allow/limit headers will only be added to the database if the following is true.

- The entry is not already in the database

- At least one valid data entry (e.g. - CIDD, username, process name)

- The block, allow, or limit time has not already passed

After the DC Do message has been processed, an extension is added to the return message, describing the action taken, if any, by the node.  The return message is the DC Do response message.

### DC Undo

The DC sends a DC Undo message to an agent node to remove a response directed via a previously sent DC Do message. The DC sends the DC Undo message with the originator and thread id of the previous DC Do message (see Figure 24).  On sending a DC Undo message, the Discovery Coordinator records the message as pending response.  Failure to receive a DC Undo Response message indicates failed IDIP components.

When the agent node receives a DC Undo message, it removes all block, allow, and audit responses involved with the originator and thread id. The agent node sets the Boolean value Succeeded in the DC Undo Message to indicate whether the undo response was successful.

### DC Do Response and DC Undo Response

DC Do/Undo response messages are received by the DC from an agent node.  The message is a response to a DC Do or DC Undo directive.  If the DC Do or DC Undo response is not received before the timeout expires, the DC acts as if the IDIP node has failed and updates its topology accordingly.

### DC Notify

A node sends the DC a Notify message whenever a neighbor’s state changes (e.g., neighbor becomes unresponsive). When the neighborhood changes, a value is sent to indicate a DC Notify message needs to be sent to the DC. Periodically the sender process of the IDIP Message Layer checks this value and sends a DC Notify message if the value is set. The sender process fills in the Notify Message Header (Figure 25) with information about itself and a Notify Entry (Figure 26) for each neighbor.

On receipt of a Notify message, the DC updates its state representing the IDIP topology.

### DC Control Messages

The DC sends an INFOCON or DEFPOS control message to all IDIP components in the Discovery Coordinator’s community when the local INFOCON or DEFPOS level changes.

On receipt of an INFOCON control message, an IDIP node changes its local INFOCON value. On receipt of a DEFPOS control message, an IDIP node changes its local DEFPOS value. A node may have different response policies for different INFOCON and/or DEFPOS values.

### DC Query

DC sends a DC Query message requesting information from the agent node, such as neighborhood status or current blocking table.

When an agent node receives a request for its current blocking table, it formats the block and allow tables into human readable strings and sends the buffer to the DC in an Agent-to-DC Get Response message.

When an agent node receives a request for its current neighborhood status, the agent node sets a value to indicate to the sender process to send a DC Notify message to the DC. It then forwards the DC Query message to its other neighbors.

### File Transfer

An agent node can request a file from the DC using an Agent-to-DC Get message with the Get File message type. Upon receipt of an Agent-to-DC Get message with Get File message type, the DC responds to the request by sending the node the file using a DC-to-Agent Get Response File Transfer message.

A DC can send a node a file, without the node requesting a file. The DC uses a DC-to-Agent Set or DC-to-AgentD Set message with the Push File message type.  This is used to update files, such as sending modified cost models to the agents. Upon receipt of a DC-to-Agent Set or DC-to-AgentD Set message, the agent saves the file then processes its contents.

# REFERENCES

- The Boeing Company. Neighborhood Key Information Distribution (NKID) Protocol (Draft), Boeing Document Number D658-10818-1, February 1998.

- Trusted Information Systems, Inc. Intruder Detection Isolation Protocol (IDIP) Authentication Header (AH), TIS Report Number 0699D, November 1997.

- Trusted Information Systems, Inc., Intruder Detection Isolation Protocol (IDIP) Encapsulating Security Payload (ESP), TIS Report Number 0698D, November 1997.

- Trusted Information Systems, Inc., IDIP AH with Hashed Message Authentication Codes (HMAC)-SHA-1, TIS Report Number 0700D, November 1997.

- Trusted Information Systems, Inc., IDIP ESP with SKIPJACK Cipher Block Chaining (CBC), TIS Report Number 0701D, November 1997.

- Trusted Information Systems, Inc., Intruder Detection and Isolation Protocol (IDIP) Transport Security Protocol Interface, TIS Report Number 0697D, November 1997.

- NAI Labs and The Boeing Company. Intruder Detection and Isolation Protocol (IDIP) Message Layer, NAI Labs Report #02-005, February 2002.

- Rich Feiertag, Cliff Kahn, Phil Porras, Dan Schnackenberg, Stuart Staniford-Chen, Brian Tung, “A Common Intrusion Specification Language (CISL)”, http://www.isi.edu/~brian/cidf/drafts/language.txt/, June 1999.

# Appendix: Attack Codes

## Penetration Attack Codes

| Code | Attack | Description |
| --- | --- | --- |
| 0x0001002 | Password | Password Guessing attack. Multiple failed attempts to log into a host. |
| 0x0001003 | Unserviced Ports | Use of ports that are not supported within a network or at a host. |
| 0x0001004 | Door Knob | Doorknob Rattling attack. Attempts to use well-known account and passwords. |
| 0x0001005 | ICMP Redirect | Use of ICMP redirect message. |
| 0x0001006 | Routing Protocol | Attempts to change routing information inappropriately. |
| 0x0001007 | Network File System | General NFS attack. |
| 0x0001008 | Mail From Pipe | RFC-822 “Reply-to” field has the “¦” character to trigger one of Sendmail’s flaws. |
| 0x0001009 | Remote Finger | Sending a large remote finger request in an attempt to overflow the finger daemon’s buffer. |
| 0x000100a | Seq Num Guess | Sequence number guessing attack. |
| 0x000100b | Admind | Unauthorized access attempt using Rpc.Admind. |
| 0x000100c | BackOrifice | BackOrifice command detection. |
| 0x000100d | DNS Hostname Overflow | DNS hostname overflow attack (CA-98.05). |
| 0x000100e | DNS Length Overflow | DNS length overflow attack (CA-98.05). |
| 0x000100f | Email Debug | Email debug attack. |
| 0x0001010 | Email Decode | SMTP decode attack. |
| 0x0001011 | Email Listserv Overflow | Email listserv buffer overflow attack. |
| 0x0001012 | Email Wiz | Email WIZ attack. |
| 0x0001013 | Finger Perl | Perl and DGUX fingerd exploit check. |
| 0x0001014 | FTP Args | FTP args core dump exploit check. |
| 0x0001015 | FTP Bounce | FTP Bounce attack check (CA-97.27) |
| 0x0001016 | FTP Privilegedbounce | FTP Privileged port bounce attack check. |
| 0x0001017 | FTP Privilegedport | FTP Privileged port attack check. |
| 0x0001018 | FTP Root | FTP CWD ~root attack. |
| 0x0001019 | FTP Site Exec Dotdot | FTP site exec .. attack. |
| 0x000101a | FTP Site Exec Tar | FTP site exec tar attack. |
| 0x000101b | HTTP Campas | HTTP campas cgi-bin attack. |
| 0x000101c | HTTP Count | HTTP count cgi-bin exploit check (CA-97.24). |
| 0x000101d | HTTP Dotdot | HTTP .. attack. |
| 0x000101e | HTTP Glimpse | HTTP glimpse cgi-bin attack. |
| 0x000101f | HTTP IE BAT | HTTP Internet Explorer .BAT file attack. |
| 0x0001020 | HTTP IE3 URL | HTTP Internet Exploerer 3.0 .URL/.LNK attack. |
| 0x0001021 | HTTP IIS3 ASP 2e | HTTP IIS 3.0 ASP %2e attack. |
| 0x0001022 | HTTP IIS3 ASP Dot | HTTP IIS 3.0 ASP . attack. |
| 0x0001023 | HTTP NCSA Buffer Overflow | HTTP NCSA httpd buffer overflow attack. |
| 0x0001024 | HTTP Novell Convert | HTTP Novell convert cgi-bin attack. |
| 0x0001025 | HTTP PHF | HTTP PHF attack. |
| 0x0001026 | HTTP PHP Overflow | HTTP PHP buffer overflow attack. |
| 0x0001027 | HTTP PHP Read | HTTP PHP cgi-bin file read attack. |
| 0x0001028 | HTTP SCO View Source | HTTP SCO view-source cgi-bin attack. |
| 0x0001029 | HTTP SGI Handler | HTTP SGI handler cgi-bin attack. |
| 0x000102a | HTTP SGI Webdist | HTTP SGI Webdist cgi-bin attack. |
| 0x000102b | HTTP Unix Passwords | HTTP access of Unix password file. |
| 0x000102c | HTTP Website Sample | HTTP WebSite Win-C-Sample exploit check. |
| 0x000102d | HTTP Website Uploader | HTTP WebSite Uploader File Upload check. |
| 0x000102e | Ident Newline | Ident newlines attack. |
| 0x000102f | Ident Overflow | Ident buffer overflow attack. |
| 0x0001030 | IMAP overflow | IMAP buffer overflow attack. |
| 0x0001031 | INN Control | INN control message attack. |
| 0x0001032 | INN Overflow | INN buffer overflow attack. |
| 0x0001033 | IPFrag | IP fragmentation attack. |
| 0x0001034 | IRC Daemon Overflow | IRCd buffer overflow attack. |
| 0x0001035 | Kerberos User Snarf | Kerberos IV user snarf attack (CA-96.03). |
| 0x0001036 | NFSGUESS | NFS file handle guess attack. |
| 0x0001037 | NFSMKNOD | Detect NFS mknod attempt. |
| 0x0001038 | NFSUID | NFS UID bug attack. |
| 0x0001039 | NIS Overflow | NIS Buffer overflow attack (CA-98.06). |
| 0x000103a | PCNFSDEXEC | PCNFSd exec attack (CA-96.08). |
| 0x000103b | POP Overflow | POP buffer overflow attack (CA-97.09 and CA-98.08). |
| 0x000103c | Remotewatch | HP/UX remote watch attack. |
| 0x000103d | Rlogin Froot | Rlogin –froot attack. |
| 0x000103e | SMB Password Overflow | SMB SessionSetupAndX password overflow. |
| 0x000103f | Statd Dotdot | Statd file creation attack. |
| 0x0001040 | Statd Overflow | Statd buffer overflow attack. |
| 0x0001041 | Sun SNMP Backdoor | Sun SNMP Backdoor. |
| 0x0001042 | TFTP Get | Decode TFTP get command. |
| 0x0001043 | TFTP Put | Decode TFTP put command. |
| 0x0001044 | Windows Pwl access | Windows .pwl password file access attempt. |
| 0x0001045 | Ypupdate Exec | Ypupdated exec attack (CA-95.17). |
| 0x0001046 | Mountd | Mountd buffer overflow (CA-98.12). |
| 0x0001047 | Tooltalk Overflow | Tooltalk stack overflow (CA-98.11). |
| 0x0001048 | MIME Buffer Overflows | MIME buffer overflow (CA-98.10). |
| 0x0001049 | FTPD | FTP Signal handling vulnerability (CA-97.16). |
| 0x000104a | Metamail | Metamail MIME vulnerability (CA-97.14). |
| 0x000104b | Rlogin Term | Rlogin buffer overflow (CA-97.06). |
| 0x000104c | Sendmail | Email MIME buffer overflow (CA-97.05). |
| 0x000104d | Talkd | Talkd stack smashing (CA-97.04). |
| 0x000104e | FTP Site Exec Any | FTP site exec .. attack. |
| 0x000104f | Buffer Overflow | General buffer overflow, such as eject, ffbconfig, fdformat. |
| 0x0001050 | Reserved User Exec | Reserved account (not intended to run processes) executed code. |
| 0x0001051 | Rserved Auth Violation | Authority violation (EUID not Author). |
| 0x0001052 | Unauth Environment Mod | User altered environment configuration of other user. |
| 0x0001053 | PS Exploit | Unix PS vulnerability. |
| 0x0001054 | Bad Passwd Mod | Unauthorized password modification. |
| 0x0001055 | Bad System Bin Mod | Unauthorized modification to system executable. |
| 0x0001056 | Root By Nonadmin | Root was acquired by user not designated as an administrator. |
| 0x0001057 | Root By Unknown Method | Root was acquired by an unknown method (not SU, not setuid). |
| 0x0001058 | FTP Anon Fsmod | Anonymous FTP user modified filesystem. |
| 0x0001059 | FTP Reservd Name | FTP login using reserved account name. |
| 0x000105a | FTP Sensitive File Retr | FTP sensitive file retrieval. |
| 0x000105b | FTP Site Exec | FTP site exec attack. |
| 0x000105c | FTP Core Dump | FTP core attack. |
| 0x000105d | Syslog Buffer Overflow | Syslog buffer overflow (CA-95.13). |
| 0x000105e | Frame Spoofer | Frame spoofer attack. |
| 0x000105f | FTP Write | FTP write attack. |
| 0x0001060 | HTTP Tunnel | HTTP tunnel attack. |
| 0x0001061 | NCFTP | NCFTP attack. |
| 0x0001062 | NETBUS | Netbus attack. |
| 0x0001063 | NETCAT | Netcat attack. |
| 0x0001064 | PPMACRO | PPMACRO attack. |
| 0x0001065 | SSH Trojan | SSH trojan attack. |
| 0x0001066 | XLOCK | Xlock attack. |
| 0x0001067 | XSNOOP | Xsnoop attack. |
| 0x0001068 | ANYPW | Anypw attack. |
| 0x0001069 | CASESEN | Casesen attack. |
| 0x000106a | Loadmodule | Loadmodule attack. |
| 0x000106b | NTFSDOS | NTFSDOS attack. |
| 0x000106c | PERL | Perl attack. |
| 0x000106d | SECHOLE | Sechole attack. |
| 0x000106e | XTERM | Xterm attack. |
| 0x000106f | YAGA | Yaga attack. |

## Denial of Service Attack Codes

| Code | Attack | Description |
| --- | --- | --- |
| 0x0002001 | Domain Name Service | DNS Cache Poisoning (CA-98.05). |
| 0x0002002 | SYN Flood | SYN Flood attack (CA-96.21). Multiple connection attempts with no SYN acknowledgement. |
| 0x0002003 | ICMP Bomb | Ping of Death attack (CA-96.26). Very large ICMP ping. |
| 0x0002004 | Source Is Target | Land denial of service attack (CA-97.28). |
| 0x0002005 | ICMP Broadcast | Smurf denial of service attack (CA-98.01). |
| 0x0002006 | UDP Echo | Chargen/echo denial of service attack, aka Pepsi (CA-96.01). |
| 0x0002007 | Ascend Kill | Ascend kill denial of service attack. |
| 0x0002008 | Email Qmail Length | SMTP Qmail length denial of service attack. |
| 0x0002009 | Email Qmail RCPT | SMTP Qmail RCPT denial of service attack. |
| 0x000200a | Finger Bomb | Redirecting finger. |
| 0x000200b | HTTP Apache DOS | HTTP Apache denial of service attack. |
| 0x000200c | Rwhod Overflow | Rwhod buffer overflow attack. |
| 0x000200d | SNMP Delete WINS | SNMP attack against WINS server. |
| 0x000200e | Talk Flash | Talk flash attack. |
| 0x000200f | Teardrop | TearDrop fragmentation attack and variations (CA-97.28). |
| 0x0002010 | UDPBomb | UDP mal-formed packet attack. |
| 0x0002011 | Windows OOB | Windows out-of-band denial of service attack (WinNuke). |
| 0x0002012 | Processtable Exhaustion | Resource Exhaustion: process table. |
| 0x0002013 | Filesystem Exhaustion | Resource Exhaustion: file system. |
| 0x0002014 | FTP Nlist | FTP NLIST denial of service. |
| 0x0002015 | Cisco CR COS | Cisco_CR_Dos denial of service. |
| 0x0002016 | Email XCHG AUTH | EMAIL_XCHG_AUTH denial of service. |
| 0x0002017 | NNTP XCHG AUTH | NNTP XCHG AUTH denial of service. |
| 0x0002018 | Solaris Mail Bomb | Solaris mail bomb attack. |
| 0x0002019 | Unsolicited ICMP Replies | Unsolicited ICMP replies. |
| 0x000201a | ARP Poison | ARP Poison attack. |
| 0x000201b | HTTP Apache Back | HTTP Apache back attack. |
| 0x000201c | CrashIIS | Crash IIS attack. |
| 0x000201d | Selfping | Selfping attack. |
| 0x000201e | SSHprocessTable | SSH process table attack. |
| 0x000201f | Syslogd | Syslogd attack. |

## Unusual Access Attack Codes

| Code | Attack | Description |
| --- | --- | --- |
| 0x0003001 | Unusual File | Unusual get/put of a file, such as /etc/passwd. |
| 0x0003002 | Unusual Connection | Connection not usually expected, but permitted by policy. Connection need not complete. |
| 0x0003003 | Unusual Traffic | Unusual traffic pattern. |
| 0x0003004 | ARP | ARP “down host” check. |
| 0x0003005 | HTTP Shells | HTTP Shell interpreter accesses check. |
| 0x0003006 | Ident Error | Ident error in request |
| 0x0003007 | IPDuplicate | Check for duplicate IPs. |
| 0x0003008 | IPUnknownProtocol | Detect unknown IP protocol. |
| 0x0003009 | RealSecure Kill | Detect RealSecure session kills |
| 0x000300a | SelSvch | SelSvc remote holdfile attack. |
| 0x000300b | SourceRoute | Detect source-routed connections |
| 0x000300d | Windows Registry Read | Decode Windows remote registry read. |
| 0x000300e | HTTP ActiveX | Detect ActiveX controls in HTTP traffic. |
| 0x000300f | HTTP Java | Detect Java in HTTP traffic. |
| 0x0003010 | HTTP ShockWave | Detect ShockWave applets in HTTP traffic. |
| 0x0003011 | HTTP Vulnerable Client | HTTP Vulnerable Client check. |
| 0x0003012 | IPProtocolViolation | Malformed packets that violate TCP/IP rules. |
| 0x0003013 | Packet Capturing Remote | Remote use of packet capturing tools. |
| 0x0003014 | Packet Capturing Tool | Local use of packet capturing tools. |
| 0x0003015 | Windows Access Error | Errors while connecting to Windows servers. |
| 0x0003016 | Windows Null Session | Windows null session login (possible anonymous user backdoor). |
| 0x0003017 | Illegal Login Attempt | Attempted illegal login. |
| 0x0003018 | Illegal Login | Successful illegal login. |
| 0x0003019 | Priv Escalate | Illegal Privilege Escalation. |
| 0x000301a | TimeWarp | Local host clock has been set back more than “cnt” seconds. |
| 0x000301b | Suspicious Argument | Suspicious Unix SYSCALL Argument name. |
| 0x000301c | Root Core Create | Unix root core file creation. |
| 0x000301d | Root Core Access | Unix root core file access. |
| 0x000301e | Private File Alteration | Suspicious private file alteration. |
| 0x000301f | Suspicious File Creation | Suspicious file creation. |
| 0x0003020 | System Resourc Alteration | Modification of system resource. |
| 0x0003021 | Suspicious SETUID File | Suspicious SETUID file created. |
| 0x0003022 | Warez Client | Warez Client activity. |
| 0x0003023 | Warez Server | Warez Server activity. |
| 0x0003024 | Trojan Horse Exec | Possible Trojan Horse execution. |
| 0x0003025 | Lost Critical Process | Critical process killed. |
| 0x0003026 | Lodmodule | Possible Loadmodule attack. |
| 0x0003027 | Access Denied | Access denied to a file or object. |
| 0x0003028 | Rexd | Rexd used to remotely execute a command. |
| 0x0003029 | Rexec | Rexec used to remotely execute a command. |
| 0x000302a | Rsh | Rsh used to remotely execute a shell command. |
| 0x000302b | SubSeven Scan | SubSeven_Scan a Windows 98 backdoor providing undetected access to an infected machine. |
| 0x000302c | Disallowed Command | Command not allowed. |
| 0x000302d | Device Permisc | Permiscuous device. |
| 0x000302e | Disallowed Privalege | Privilege not allowed. |
| 0x000302f | Process Subversion | Process subversion. |
| 0x0003030 | Process Abuse | Process abuse. |
| 0x0003031 | Multisource Echo Storm | Echo flood from multiple sources. |
| 0x0003032 | ICMP Unreachable Storm | ICMP unreachable flood. |
| 0x0003033 | Bad Fragement Flood | Bad fragment flood. |

## Flooding Attack Codes

| Code | Attack | Description |
| --- | --- | --- |
| 0x0004001 | UDP Service Flood | Unusually high number of UDP datagrams. |
| 0x0004002 | ICMP Flood | Unusually high number of ICMP datagrams. |
| 0x0004003 | HTTP Get | HTTP Get attack |

## Probing Attack Codes

| Code | Attack | Description |
| --- | --- | --- |
| 0x0005001 | Port Scan | Messages to a number of ports to determine which services are available on a component. |
| 0x0005002 | DNS Hinfo | DNS requests for host information. |
| 0x0005003 | DNS Zone High Port | DNS Zone transfer from high port number. |
| 0x0005004 | DNS Zone Transfer | DNS Zone transfers |
| 0x0005005 | Email Expn | Decode SMTP Expn: line. |
| 0x0005006 | Email Vrfy | Decode SMTP Vrfy: line. |
| 0x0005007 | FTP SYST | Use of FTP SYST command. |
| 0x0005008 | HTTP Nphtestcgi | HTTP nph-test-cgi attack (CA-97.07). |
| 0x0005009 | HTTP SGI Wrap | HTTP SGI wrap cgi-bin attack. |
| 0x000500a | HTTP Testcgi | HTTP test-cgi attack. |
| 0x000500b | IPHalfScan | TCP half scan attack. |
| 0x000500c | ISS | Detect ISS scan (CA-93.14). |
| 0x000500d | Pmapdump | Portmap dump attack. |
| 0x000500e | Satan | Detect a normal or heavy SATAN scan of a machine (CA-95.07a). |
| 0x000500f | Trace Route | Traceroute being used to map the net. |
| 0x0005010 | FTP CWD Probe | FTP Directory probing |
| 0x0005011 | HTTP Authentication | HTTP Authentication attack. |
| 0x0005012 | IMAP Password | IMAP password attack. |
| 0x0005013 | IMAP User | IMAP user attack. |
| 0x0005014 | POP User | POP user attack. |
| 0x0005015 | POP Password | POP password attack. |
| 0x0005016 | Light Satan | Light SATAN scan of a machine. |
| 0x0005017 | Ping Scan | Ping scan. |
| 0x0005018 | Finger Probe | Finger probe. |
| 0x0005019 | Port Map Dump | Port map dump scan. |
| 0x000501a | Ruser | Ruser scan. |
| 0x000501b | Mount Scan | Mount scan |
| 0x000501c | Ping Sweep | Ping sweep. |
| 0x000501d | Horizontal Scan | Horizontal scan. |
| 0x000501e | ICMP Echo Scan | ICMP echo scan. |
| 0x000501f | Inside Sniffer | Inside Sniffer scan. |
| 0x0005020 | NT Infoscan | NT Infoscan. |
| 0x0005021 | Queso | Queso scan. |
| 0x0005022 | Reset Scan | Reset scan. |

# Footnotes

( Integrated Technology Solutions, Inc. 8775 Cloudleap Ct, Suite 200, Columbia, MD 21045.