## CHAPTER 6

#### LOAD-BALANCING ALGORITHM SIMULATION

We have developed the load balancing algorithms in Chapter 2, analyzed the web and client characterization in Chapter 4 and designed the simulation parameters and simulation program in Chapter 5. In this chapter we will simulate the developed load balancing algorithms. In next chapter, we will give some network design issues based on our simulation results.

Our simulation includes following contents.

- Algorithm’s performance

- Range of algorithm’s application

- Adjusting range of parameters of some load balancing algorithms.

We will use the following criterions developed in Chapter 2 to evaluate the load balancing algorithms.

- Average response time. We will generate requests to the network, calculate the time from sending requests to receiving the response documents.

- Queuing delays such as the delay at web server and router.

- Transmission delay.

- Propagation delay.

- Processing delays such as processing delay at web server and router.

- Imbalance rate.

6.1 LBA-I LOAD-BALANCING ALGORITHM

### In this section, we simulate the balancing performance of LBA-I, LBA-I-1, LBA-I-2 algorithms using Jew Jersey and r50 networks. We will compare LBA-I, LBA-I-1, LBA-I-2 algorithm results with the random and RR algorithm.

6.1.1 New Jersey Network

The topology of the New Jersey LATA Network is shown in Figure 5-1. Table 6-1 lists its simulation parameters.

# Table 6-1 Simulation Parameters of New Jersey LATA Network

| Number of Nodes | 116 |
| --- | --- |
| Number of Clients | 100 |
| Number of Web | 3 (N07, N08, N10) |
| Web Processing Power | N07 – 10MB, N08 - 3*10MB, N10 - 5*10MB |
| Number of Sub nets | 5 (1 –N01, 2 –N02, 3 – N03, 4 –N05, 5 – N06) |
| Number of Routers | 8 |
| Average Router Processing Power | 1000 Mb |
| Average Client processing Power | 10MB |
| Range of Request Size | 1 ~ 10 KB |
| Range of Request Interval | < 1 ~ 4 s |
| Range of Request Number | 800 ~ 10000 |

### Figure 6-1 shows the distribution of the document size used for the simulation, which is generated based on the analysis results of the web workload characterization.

Figure 6-1 Distribution of Document Size

Figure 6-2 shows the distribution of request interval used for the simulation, which is set based on the analysis results of client workload characterization. We will test the impact of the variation in the distribution of both request interval and document size on our load-balancing algorithms in chapter 7.

Figure 6-2 Distribution of Request Interval

Figure 6-3 is the average response time in seconds when the number of requests varies from 800 to 10000 using the above simulation parameters.

Figure 6-3 New Jersey LATA Network Average Response Time

Table 6-2 summaries the statistic characterization of those algorithms

Table 6-2 Statistic Characterization of Load-Balancing Algorithms

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Response Time (s) | 0.013440 | 0.014754 | 0.013725 | 0.013750 | 0.013760 |
| Average Web Queuing Delay (s) | 0.000094 | 0.000162 | 0.000086 | 0.000107 | 0.000103 |
| Average Router Queuing Delay (s) | 0.00001 | 0.000014 | 0.000010 | 0.000007 | 0.000009 |
| Average Transmission Delay (s) | 0.012362 | 0.013539 | 0.012646 | 0.012621 | 0.012540 |
| Average Propagation Delay (s) | 0.000243 | 0.000242 | 0.000254 | 0.000252 | 0.000254 |
| Average Processing Delay (s) | 0.000728 | 0.000796 | 0.000729 | 0.000766 | 0.000763 |
| Imbalance Rate | 0.059942 | 1.197764 | 0.004982 | 0.513013 | 0.515555 |

Table 6-3 shows the percentage of each delay in the average response time.

### Table 6-3 Percentage of Each Delay in Average Response Time

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Web Queuing Delay (s) | 0.69940% | 1.11416% | 0.62659% | 0.77818% | 0.74854% |
| Average Router Queuing Delay (s) | 0.08184% | 0.09491% | 0.07285% | 0.05091% | 0.06540% |
| Average Transmission Delay (s) | 91.9792% | 91.7898% | 92.1384% | 91.7890% | 91.1337% |
| Average Propagation Delay (s) | 1.80803% | 1.64067% | 1.85063% | 1.83272% | 1.84593% |
| Average Processing Delay (s) | 5.41666% | 5.39661% | 5.31147% | 5.57090% | 5.54505% |

Table 6-4 lists the percentage of the reduced average response time of the algorithm LBA-I relative to other algorithms.

Table 6-4 Algorithm LBA-I Performance Improvement Relative to Other Algorithms

| Algorithm | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- |
| Percentage | 8.88% | 2.076% | 2.254% | 2.325% |

From Table 6-3 we can see that the transmission delay is the most important factor for response time. Ninety percent of response time comes from the transmission delay.  LBA-I algorithm reduces the transmission delay since the algorithm takes the path condition into account. On the other hand, the LBA-I-2 algorithm dose not improve the balancing effect and has longer transmission delay since it dose not take the path condition into account. Because the router queuing delay is only 1% of the response time for this small network, the algorithm LBA-I-1 will miss the fastest transmission path if the algorithm takes the router queuing delay into account in this case. Therefore the LBA-I-1 algorithm has longest transmission delay. Figure 6-4 shows the transmission delay of the algorithm LBA-I, LBA-I-1 and LBA-I-2.

.

Figure 6-4 Transmission Delay of Different Algorithms

Next we will analyze the allocating decision of a LBA. We choose the second LBA of the network topology shown in Figure 5-1 and analyze the following information that makes up of the allocating decision.

- Path

There are three paths.

### Path 1: N02N04N07 to web server N07 and its processing power is 10MB.

Path 2: N02N00N03N08 to web server N08 and its processing power is 3*10MB.

Path 3: N02N04N10 to web server N10 and its processing power is 5*10MB.

Table 6-5 is a summary the path information, where D, B, and H represents distance, bandwidth, and hops, respectively.

### Table 6-5 Path Information

|  | Total D | Total B | Total H | D/B | D/B + H |
| --- | --- | --- | --- | --- | --- |
| Path 1 | 80 km | 14.7 Mb | 2 | 5.44 | 7.44 |
| Path 2 | 130 km | 29.8 | 3 | 4.36 | 7.36 |
| Path 3 | 90 km | 14.9 | 2 | 6.04 | 8.04 |

- Web Server Processing Power

The processing powers of web server N07, N08, and N10 are 10MB, 30MB, 50MB, respectively.

- Router Queuing Delay and Loads of Web Servers

The router queuing delay and web server loads are dynamic information. We assume at beginning that the all web servers have the same loads that are 100, and all routers have the same queuing delay that is 0.00001 second.

If a new request comes and its size is 20*8+145 = 305 bites. Based on above assumptions, algorithm LBA-I will allocate the new request to web server N08 (D/B + load/processing power=15.44, 7.69, 8.04), algorithm LBA-I-1 will allocate the new request to web server N10 (17.44,10.69,10.04), and algorithm LBA-I-2 will allocate the new request to N10 (10,3.33,2.0). The response time from LBA N02 to web server N07, from LBA N02 to web server N08, and from LBA N02 to web server N10 are 0.0009387, 0.0008328, and 0.001027 second, respectively. We can see that allocating to web server N08 will have best response time and the algorithm LBA-I has the desired allocating policy.

Figure 6-5 shows the load imbalance rates of algorithm LBA-I, LBA-I-1 and LBA-I-2 when the number of request numbers is from 800 to 10000.

Figure 6-5 Imbalance Rates of Algorithm LBA-I, LBA-I-1 and LBA-I-2

The algorithm LBA-I-2 has the smallest imbalance rate. However this algorithm has the longest response time, which means that considering the processing power of web server is not a good load-balancing metrics. The metric and imbalance only gives the web load balancing status, and does not indicate the balancing effect of the algorithm. The average response time metric is a more reasonable one.

6.1.2 RANDOM 50 NETWORK

The r50 network topology is given in Appendix A and its simulation parameters are listed in Table 6-6:

Table 6-6 Simulation Parameters for Network r50

| Number of Nodes | 890 |
| --- | --- |
| Number of Clients | 800 |
| Number of Webs | 10 |
| Number of Sub nets | 40 |
| Maximum Link Degree | 11 |
| Average Link Degree | 8 |
| Distance | 100 km ~ 1000 km |
| Number of Routes | 40 |
| Average Router Processing Power | 1000 Mb |
| Average Client Processing Power | 10MB |
| Range of request Size | 1 ~ 10 KB |
| Range of Request Interval | Less 1 ~ 4 sec |
| Range of Request Number | 800 ~ 10000 |

The distribution of document size is shown in Figure 6-1, and the distribution of request interval is plotted in Figure 6-2.

Figure 6-6 shows the average response time of algorithm LBA-I, LBA-I-1 and LBA-I-2 when the number of requests varies from the 800 to 10000.

Figure 6-6 Average Response Time

Table 6-7 summaries the statistic characterization of the different algorithms.

Table 6-7: Statistic Data of Algorithm LBA-I, LBA-I-1 and LBA-I-2

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.025717 | 0.024988 | 0.026782 | 0.026648 | 0.027160 |
| Ave Web Queuing Delay (sec) | 0.000073 | 0.000076 | 0.000008 | 0.000008 | 0.000016 |
| Average Router Queuing Delay (s) | 0.000018 | 0.000024 | 0.000020 | 0.000022 | 0.000018 |
| Average Transmission Delay (s) | 0.022513 | 0.021820 | 0.022560 | 0.022791 | 0.022904 |
| Average Propagation Delay (s) | 0.002263 | 0.002263 | 0.003430 | 0.003435 | 0.003412 |
| Average Processing Delay (s) | 0.000851 | 0.000810 | 0.000781 | 0.000809 | 0.000823 |
| Imbalance Rate | 0.251540 | 0.276905 | 0.014812 | 0.128199 | 0.147359 |

Table 6-8 shows the percentage of each delay in the average response time. For example, the average transmission delay of algorithm LBA-I is 0.022513 second and the average response time is 0.025717 second, the average transmission delay holds 87.54% (0.022513/0.025717=87.54%) of the average response time.

### Table 6-8 Percentage of Each Delay in Average Response Time

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Web Queuing Delay | 0.2838% | 0.30414% | 0.02987% | 0.03002% | 0.05891% |
| Average Router Queuing Delay | 0.0699% | 0.09694% | 0.07467% | 0.08255% | 0.06627% |
| Average Transmission Delay | 87.544% | 87.3219% | 84.2356% | 85.5261% | 84.3298% |
| Average Propagation Delay | 8.7996% | 9.05634% | 12.8071% | 12.8902% | 12.5555% |
| Average Processing Delay | 3.3090% | 3.24155% | 2.91613% | 3.03587% | 3.03019% |

From Table 6-8 we can see that the transmission delay is the most important factor for response time. Eighty five percent of response time comes from the transmission delay. LBA-I algorithm reduces the transmission delay since the algorithm takes the path condition into account. On the other hand, the LBA-I-2 algorithm dose not improve the balancing effect since it dose not take the path condition into account. Algorithm LBA-I-1 has better balancing-effect for this case, because when the network gets bigger, the path from LBA to web servers will have through more hops and the router queuing delay becomes larger. Comparing Tables 6-3 and 6-8 we can see that the prorogation delay is increased from 1% to 10%. The path factor is more important for bigger network than the smaller network, so algorithm LBA-I and LBA-I-1 give better balancing effect for r50 network than New-J network.

Algorithm LBA-I-1 reduces 6.698%, 6.229%, 7.997% of response time compared to algorithm LBA-I-2, RR, and Random, respectively. Algorithm LBA-I reduces 3.976%, 3.49365%, 5.312% of response time compared to algorithm LBA-I-2, RR, and Random, respectively.

Figure 6-7 shows the propagation delay for algorithm LBA-I, LBA-I-1 and LBA-I-2. Algorithm LBA-I and LBA-I-1 have much less propagation delay than other algorithms.

Figure 6-7 Propagation Delay of Algorithm LBA-I, LBA-I-1 and LBA-I-2

Figures 6-8 and 6-9 show the transmission delay and imbalance rate of algorithm LBA-I, LBA-I-1, and LBA-I-2.

Figure 6-8 Transmission Delay of Algorithm LBA-I, LBA-I-1 and LBA-I-2

Figure 6-9 Imbalance Rate of Algorithm LBA-I, LBA-I-1 and LBA-I-2

Algorithm LBA-I-2 has the smallest imbalance rate. However this algorithm has longer transmission delay and propagation delay. Once again it shows that a load-balancing algorithm considering only the processing power of web server will not be good one. The metric and imbalance only gives the web load balancing status, and does not indicate the balancing effect of the algorithm. The average response time metric is a more reasonable one.

6.2 LBA-II LOAD-BALANCING ALGORITHM

For algorithm LBA-I, LBA-I-1, and LBA-I-2, all LBAs do not communicate each other and they have zero overheads. However, because they do not communicate each other, it is possible that many LBAs will assign requests to the same web server at the same time. Figure 6-10 is the assignments of web server 1 at 0.2 seconds from simulation beginning at New-J network. We can see that at 0.2 seconds simulation, three LBAs assign requests to web server 1 at the same time.

# Figure 6-10 Web Server Assignment

The LBA-II algorithm requires the communication among LBAs. When a LBA made an assignment decision, it reports this assignment decision to other LBAs and other LBAs update their assignment table and revalue their allocating decision. The LBA-II algorithm also have more accurate information about each web server loads. There are three variations of the LBA-II algorithm, LBA-II, LBA-II-1, and LBA-II-2.

6.2.1 ALGORITHM LBA-II (I), LBA-II (I-1) AND LBA-II (I-2)

Algorithm LBA-II is much different from algorithm LBA-I, LBA-I-1 and LBA-I-2 since algorithm LBA-II will generate extra packets and have very heavy overhead communication between LBAs. For example, the r50 network has 40 LBAs. If each LBA processes 1000 requests, it will generate 1000*39*40 extra packets and the overhead is (1000*39*40)/(1000*40) ( 400%. Too much overhead communication will slow down the transmission and degrade the balancing effect. Here we just use the New-J network to show this fact. Table 6-10 summarizes the balancing effect of algorithm LBA-II (I), LBA-II (I-1) and LBA-II (I-2).

Table 6-10 Statistic Data of Algorithm LBA-II (I), LBA-II (I-1) and LBA-II (I-2)

|  | LBA-II(I) | LBA-II(I-2) | LBA-II(I-1) | LBA-I | LBA-I-2 | LBA-I-1 |
| --- | --- | --- | --- | --- | --- | --- |
| Average Response Time (s) | 0.02820 | 0.02853 | 0.0284 | 0.01344 | 0.01373 | 0.01475 |
| Average Web Queuing Delay (s) | 0.0008 | 0.0008 | 0.00103 | 0.00009 | 0.00009 | 0.00016 |
| Average Router Queuing Delay (s) | 0.00003 | 0.00002 | 0.00002 | 0.00001 | 0.00001 | 0.00001 |
| Average Transmission Delay (s) | 0.02579 | 0.02672 | 0.02639 | 0.01236 | 0.01265 | 0.01354 |
| Average Propagation Delay (s) | 0.00023 | 0.00023 | 0.00022 | 0.00024 | 0.00026 | 0.00024 |
| Average Process Delay (s) | 0.00156 | 0.00159 | 0.00165 | 0.00073 | 0.00073 | 0.00080 |

From Table 6-10, it is clear that algorithm LBA-II has much worse balancing effect since it significantly increases the transmission delay time. Comparing to algorithm LBA-I, algorithm LBA-II (I) has increased the transmission time by 108.58%. Similarly, algorithm LBA-II (I-1) has increased the transmission time by 97.36% comparing to algorithm LBA-I-1.

Table 6-11 is the overhead statistic data of algorithm LBA-II (I) when the number of requests varies from 800 to 10000.

Table 6-11 Overhead of Algorithm LBA-II (I)

| Number of Requests | Number of Overhead Events | Number of Overhead Events/Number of Requests |
| --- | --- | --- |
| 800 | 3200 | 400% |
| 1000 | 4000 | 400% |
| 2000 | 8000 | 400% |
| 3000 | 12000 | 400% |
| 5000 | 20000 | 400% |
| 7000 | 28000 | 400% |
| 9000 | 36000 | 400% |
| 10000 | 40004 | 400% |

From the above discussion, we can see that algorithm LBA-II has very heavy overhead that degrades the balancing effect. In order to decease the overhead communication between LBAs; we have developed algorithm LBA-II-1.

6.2.2 ALGORITHM LBA-II-1 (I), LBA-II-1 (I-1) AND LBA-II-1 (I-2)

For algorithm LBA-II-1, LBA communicates only to its neighbor LBA, and this can reduce the overhead generated by algorithm LBA-II. In Chapter 2, we have derived LBA-II-1 (I), LBA-II-1 (I-1) and LBA-II-1 (I-2) algorithm by modifying LBA-II (I), LBA-II (I-1) and LBA-II (I-2) algorithm, respectively. We use the New-J network to test algorithm LBA-II-1 (I), LBA-II-1 (I-1) and LBA-II-1 (I-2). Table 6-12 summarizes the balancing effect of algorithm LBA-II-1 (I), LBA-II-1 (I-1) and LBA-II-1 (I-2).

Table 6-12 Statistic Data of Algorithm LBA-II-1 (I), LBA-II-1 (I-1) and LBA-II-1 (I-2)

|  | LBA-II-1(I) | LBA-II-1(1-2) | LBA-II-1(I-1) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.014959 | 0.018324 | 0.015856 |
| Average Web Queuing Delay (s) | 0.000073 | 0.000005 | 0.000094 |
| Average Router Queuing Delay (s) | 0.000018 | 0.000015 | 0.000015 |
| Average Transmission Delay (s) | 0.013829 | 0.017214 | 0.014650 |
| Average Propagation Delay (s) | 0.000232 | 0.000398 | 0.000238 |
| Average Processing Delay (s) | 0.000806 | 0.000693 | 0.000858 |

Comparing Table 6-12 with Table 6-10, we can see that algorithm LBA-II-1 reduce average response time since algorithm LBA-II-1 (I), LBA-II-1 (I-1) and LBA-II-1 (I-2) reduce the transmission delay. Comparing to algorithm LBA-II (I), algorithm LBA-II-1 (I) has reduced the transmission time by 86%. Similarly, algorithm LBA-II-1 (I-1) has reduced the transmission time by 80% comparing to algorithm LBA-II (I-1).

Table 6-13 is the overhead statistic data of algorithm LBA-II-1 (I) when the number of requests varies from 800 to 10000.

Table 6-13 Overhead of Algorithm LBA-II-1 (I)

| Number of requests | Number of Overhead Events | Number of Overhead Events/Number of Requests |
| --- | --- | --- |
| 800 | 1600 | 200% |
| 1000 | 2000 | 200% |
| 2000 | 4000 | 200% |
| 3000 | 6000 | 200% |
| 5000 | 10000 | 200% |
| 7000 | 14000 | 200% |
| 9000 | 18000 | 200% |
| 10000 | 20000 | 200% |

Comparing Table 6-13 and 6-11, algorithm LBA-II-1 has significantly reduced the overhead. But comparing to algorithm LBA-I, LBA-I-1, algorithm LBA-II-1 still has worse balancing effect. We need further to reduce the overhead.

6.2.3 ALGORITHM LBA-II-2 (I), LBA-II-2 (I-1), LBA-II-2 (I-2)

In algorithm LBA-II-2, each LBA does not report all the allocating decisions. The LBA waits until it have already made a few allocating decisions, then sends messages to its neighbor LBAs.  The message includes recent assigning decisions. The overhead required for the communication among LBAs will be decreased in algorithm LBA-II-2. In Chapter 2, we have derived LBA-II-2 (I), LBA-II-2 (I-1), and LBA-II-2 (I-2) algorithm by modifying LBA-I, LBA-I-1, and LBA-I-2 algorithm, respectively.

Table 6-14 summarizes the balancing effect of algorithm LBA-II-2 (I), LBA-II-2 (I-1), and LBA-II-2 (I-2). The algorithm is implemented in the way that each LBA sends a message to its neighbor LBA after every 2-assignment decision has been made.

Table 6-14 Statistic Data of Algorithm LBA-II-2 (I), LBA-II-2 (I-1), and LBA-II-2 (I-2)

|  | LBA-II-2(I) | LBA-II-2(1-2) | LBA-II-2(I-1) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.020400 | 0.020052 | 0.019128 |
| Average Web Queuing Delay (s) | 0.000019 | 0.000030 | 0.000057 |
| Average Router Queuing Delay (s) | 0.000021 | 0.000021 | 0.000030 |
| Average Transmission Delay (s) | 0.019210 | 0.018862 | 0.017940 |
| Average Propagation Delay (s) | 0.000434 | 0.000434 | 0.000419 |
| Average Processing Delay (s) | 0.000717 | 0.000706 | 0.000678 |

Table 6-15 is the overhead statistic data of algorithm LBA-II-2 (I) when the number of requests varies from 800 to 10000.

Table 6-15 Overhead of Algorithm LBA-II-2 (I)

| Number of Requests | Number of Overhead Events | Number of Overhead Events/Number of Requests |
| --- | --- | --- |
| 800 | 800 | 100% |
| 1000 | 1000 | 100% |
| 2000 | 2000 | 100% |
| 3000 | 4000 | 100% |
| 5000 | 5000 | 100% |
| 7000 | 6000 | 100% |
| 9000 | 9000 | 100% |
| 10000 | 10000 | 100% |

Table 6-16 summarizes the balancing effect of algorithm LBA-II-2 (I), LBA-II-2 (I-1), and LBA-II-2 (I-2). The algorithm is implemented in the way that each LBA sends a message to its neighbor LBA after every 3-assignment decision has been made.

Table 6-16 Statistic Data of Algorithm LBA-II-2 (I), LBA-II-2 (I-1), and LBA-II-2 (I-2)

|  | LBA-II-2(I) | LBA-II-2(1-2) | LBA-II-2(I-1) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.020541 | 0.020315 | 0.019319 |
| Average Web Queuing Delay (s) | 0.000033 | 0.000039 | 0.000057 |
| Average Router Queuing Delay (s) | 0.000020 | 0.000016 | 0.000026 |
| Average Transmission Delay (s) | 0.019332 | 0.019109 | 0.018133 |
| Average Propagation Delay (s) | 0.000437 | 0.000432 | 0.000420 |
| Average Processing Delay (s) | 0.000719 | 0.000718 | 0.000683 |

Table 6-17 is the overhead statistic data of algorithm LBA-II-2 (I) when the number of requests varies from 800 to 10000.

Table 6-17 Overhead of Algorithm LBA-II-2 (I)

| Number of Requests | Number of Overhead Events | Number of Overhead Events/Number of Requests |
| --- | --- | --- |
| 800 | 534 | 66% |
| 1000 | 666 | 66% |
| 2000 | 1345 | 66% |
| 3000 | 2000 | 66% |
| 5000 | 2666 | 66% |
| 7000 | 3324 | 66% |
| 9000 | 4666 | 66% |
| 10000 | 6000 | 66% |

Comparing results given in Tables 6-12 to 6-17, we can see that algorithm LBA-II-2 really reduces the overhead, but its balancing effect becomes worse. Among algorithm LBA-II, LBA-II-1, and LBA-II-2, algorithm LBA-II-1 has the best balancing effect, algorithm LBA-II has heaviest overhead, and algorithm LBA-II-2 has least overhead.

Table 6-18 summarizes the balancing effect of algorithm LBA-II-1 (I), LBA-II-1 (I-1), and LBA-II-1 (I-2) on the r50 network.

Table 6-18 Statistic Data of Algorithm LBA-II-1 (I), LBA-II-1 (I-1), and LBA-II-1 (I-2)

|  | LBA-II-1 (I) | LBA-II-1 (I-2) | LBA-II-2 (I-1) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.0432090 | 0.042960 | 0.0388030 |
| Average Web Queuing Delay (s) | 0.000060 | 0.00083 | 0.000031 |
| Average Router Queuing Delay (s) | 0.00001 | 0.000144 | 0.00001 |
| Average Transmission Delay (s) | 0.039086 | 0.036521 | 0.034830 |
| Average Propagation Delay (s) | 0.002671 | 0.004281 | 0.002692 |
| Average Processing Delay (s) | 0.001392 | 0.001193 | 0.001240 |

Table 6-19 summarizes the balancing effect of algorithm LBA-II-2 (I), LBA-II-2 (I-1) and LBA-II-2 (I-2) on the r50 network. The algorithm is implemented in the way that each LBA sends a message to its neighbor LBA after every 2-assignment decision has been made.

Table 6-19 Statistic Data of Algorithm LBA-II-2 (I), LBA-II-2 (I-1) and LBA-II-2 (I-2)

|  | LBA-II-2 (I) | LBA-II-2 (I-2) | LBA-II-2 (I-1) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.053848 | 0.051338 | 0.052993 |
| Average Web Queuing Delay (s) | 0.005752 | 0.004703 | 0.005440 |
| Average Router Queuing Delay (s) | 0.000046 | 0.000047 | 0.000031 |
| Average Transmission Delay (s) | 0.046735 | 0.045184 | 0.046224 |
| Average Propagation Delay (s) | 0.000119 | 0.000185 | 0.000127 |
| Average Processing Delay (s) | 0.001196 | 0.001219 | 0.001171 |

From Tables 6-19, 6-7, and 6-18, we can see that algorithm LBA-II-1 and LBA-II-2 have the worse balancing effect.

6.3 LBA-III ALGORITHM

In LBA-I and LBA-II algorithms, we measure the path condition by the distance, bandwidth and the number of hops, and those data is from static information. In fact, the path condition changes with time.  For a network, it is possible that the path with short distance and high bandwidth may have the long transmission delay. In Chapter 2, we have developed algorithm LBA-III that periodically probes the path traffic status, and makes the allocating decision based on the dynamic path information and static web information as follows.

We use the New-J network to test algorithm LBA-III. Table 6-20 gives the average response time and number of overhead events when the probing period varies from 1 second to 15 seconds. For this test, we fixed the number of requests to 5000.

Table 6-20 Statistic Data of the Algorithm LBA-III

| Probing Period (s) | Average Response Time (s) | Number of Overhead Events | Web Queuing Delay (s) |
| --- | --- | --- | --- |
| 1 | 4.533115 | 192 | 4.517046 |
| 2 | 1.112819 | 93 | 1.096773 |
| 3 | 0.608334 | 60 | 0.592442 |
| 4 | 0.391298 | 45 | 0.375134 |
| 5 | 0.253026 | 30 | 0.237011 |
| 6 | 0.209628 | 30 | 0.193572 |
| 7 | 0.229610 | 15 | 0.213727 |
| 8 | 0.214584 | 15 | 0.198664 |
| 9 | 0.112236 | 15 | 0.096376 |
| 10 | 0.084037 | 15 | 0.068143 |
| 11 | 0.059053 | 15 | 0.043167 |
| 12 | 0.048980 | 15 | 0.033113 |
| 15 | 0.016176 | 5 | 0.0000306 |

Table 6-21 gives the average response time and number of overhead events when the probing period varies from 3 to 15 seconds on the r50 network.

Table 6-21 Statistic Data of the Algorithm LBA-III

| Probing Period (s) | Average Response Time (s) | Number of Overhead Events | Web Queuing Delay (s) |
| --- | --- | --- | --- |
| 3 | 91.330958 | 3770 | 76.330958 |
| 4 | 55.70020 | 2920 | 47.526337 |
| 5 | 32.494338 | 2160 | 28.653681 |
| 6 | 22.106920 | 1850 | 19.754481 |
| 7 | 15.513986 | 1600 | 15.513986 |
| 8 | 10.521476 | 1200 | 10.521476 |
| 9 | 9.618965 | 1200 | 9.063232 |
| 10 | 6.085396 | 800 | 5.660862 |
| 11 | 5.660862 | 800 | 3.591400 |
| 13 | 2.893801 | 450 | 2.706136 |
| 15 | 2.538491 | 400 | 2.320166 |

From Tables 6-21 and 6-22, we can see that the algorithm LBA-III has longer average response time, and longer web queuing delay.

6.4 LBA-IV ALGORITHM

For LBA-I, LBA-II and LBA-III algorithms, the LBA and web server do not communicate each other and the LBA does not know the real loads of the web sites. LBA estimates the load status of the web servers. The estimate used in these algorithms may not always reflect the actual load of the web server. In algorithm LBA-IV, the web servers report their left load information periodically so that the LBA can periodically update their assignment tables based on the real loads.

In Chapter 2, we have derived algorithm LBA-IV-1, LBA-IV-2, and LBA-IV-3. For algorithm LBA-IV-1, the LBA allocates new requests only based on the web server left load information and do not take the web processing power and the path information into account. Algorithm LBA-IV-2 makes assignment decision by combining the web processing power and the left load information. Algorithm LBA-IV-3 makes assignment decision based on static path information, web condition and the left load information.

We use the New-J network to test algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3. Figure 6-11 shows their balancing effect when the period of load information report is 2 seconds. Table 6-22 summarizes their balancing effect

Figure 6-11 Average Response Time of Algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3

Table 6-22 Statistic Data of Algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3

|  | LBA-IV-1 | LBA-IV-2 | LBA-IV-3 |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.020262 | 0.026393 | 0.027869 |
| Average Web Queuing Delay (s) | 0.004340 | 0.010626 | 0.011021 |
| Average Router Queuing Delay (s) | 0.000033 | 0.000056 | 0.000067 |
| Average Transmission Delay (s) | 0.014357 | 0.014236 | 0.014293 |
| Average Propagation Delay (s) | 0.000257 | 0.000251 | 0.000250 |
| Average Processing Delay (s) | 0.001275 | 0.001223 | 0.001239 |

Table 6-23 summarizes the overhead information of algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3

Table 6-23 Overhead of Algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3

| Number of Requests | Number of Extra Events | Number Extra Events/Number of Requests |
| --- | --- | --- |
| 800 | 75 | 9.98 % |
| 1000 | 100 | 9.99 % |
| 2000 | 195 | 9.745 % |
| 3000 | 270 | 8.99 % |
| 4000 | 360 | 8.99 % |
| 5000 | 450 | 8.99 % |
| 7000 | 615 | 8.78 % |
| 9000 | 790 | 8.75 % |

From Figure 6-11, Tables 6-22 and 6-23, we can see that algorithm LBA-IV-1, LBA-IV-2, and LBA-IV-3 have very poor balancing effect. This is due to three reasons: 1) big overhead, 2) starting error, Before the first report, we allocate all requests to web server 1 and 3) the report period. Longer report period can reduce the extra events, but between reports, the loads of web servers have already be changed and the algorithm still use the old load data.

We eliminate the starting error by randomly assigning the requests before the first report comes. The LBA-IV-1 (2), LBA-IV-2 (2) and LBA-IV-3 (2) algorithms modify the LBA-IV-1, LBA-IV-2 and LBA-IV-3 algorithm. The second method is that we assign all requests to the web server with maximum process power before the first report comes. The LBA-IV-1 (3), LBA-IV-2 (3) and LBA-IV-3 (3) algorithm modify the LBA-IV-1, LBA-IV-2 and LBA-IV-3.Figure 6-12 shows the balancing effect of algorithm LBA-IV-1 (2), LBA-IV-2 (2) and LBA-IV-3 (2) when the report period is 2 seconds. Table 6-24 lists their statistic characterizations.

.

Figure 6-12 Average Response Time

Table 6-24 Statistic Data of Algorithm LBA-IV-1 (2), LBA-IV-2 (2) and LBA-IV-3 (2)

|  | LBA-IV-1(2) | LBA-IV-2(2) | LBA-IV-3(2) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.020096 | 0.026088 | 0.027453 |
| Average Web Queuing Delay (s) | 0.004185 | 0.010231 | 0.011767 |
| Average Router Queuing Delay (s) | 0.000073 | 0.000080 | 0.000078 |
| Average Transmission Delay (s) | 0.014305 | 0.014295 | 0.014133 |
| Average Propagation Delay (s) | 0.000253 | 0.000260 | 0.000254 |
| Average Processing Delay (s) | 0.001281 | 0.001221 | 0.001219 |

The overhead is given in Table 6-23. From Tables 6-22 and 6-24, we can see that the average response time of algorithm LBA-IV-1 (2), LBA-IV-2 (2) and LBA-IV-3 (2) is improved.

Figure 6-13 shows the average response time of the algorithm LBA-IV-1 (3), LBA-IV-2 (3), and LBA-IV-3 (3). Table 6-25 summarizes the statistic characterization of algorithm LBA-IV-1 (3), LBA-IV-2 (3) and LBA-IV-3 (3).

Figure 6-13 Average Response Time

Table 6-25 Statistic Data of Algorithm LBA-IV-1 (3), LBA-IV-2 (3) and LBA-IV-3 (3)

|  | LBA-IV-1(3) | LBA-IV-2(3) | LBA-IV-3(3) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.019813 | 0.027384 | 0.027217 |
| Average Web Queuing Delay (s) | 0.003938 | 0.011747 | 0.011464 |
| Average Router Queuing Delay (s) | 0.000043 | 0.000052 | 0.000049 |
| Average Transmission Delay (s) | 0.014300 | 0.014105 | 0.014221 |
| Average Propagation Delay (s) | 0.000256 | 0.000249 | 0.000251 |
| Average Processing Delay (s) | 0.001275 | 0.001232 | 0.001233 |

Their overheads are given in Table 6-23. From Tables 6-22, 6-24 and 6-25, we can see that algorithmLBA-IV-1 (3) and LBA-IV-3 (3) improve the average response time further.

Next we analyze the effect of the report period on the load balancing. Figure 6-14 shows the average response time of algorithm LBA-IV-1 (3) when the report period varies from 1 second to 10 seconds. Table 6-26 lists the corresponding overhead variations.

Figure 6-14 Average Response Time

Table 6-26 Overhead of Algorithm LBA-IV-1 (3)

| Report Period (s) | Number of Extra Events | Number of Extra Events/Number of requests |
| --- | --- | --- |
| 1 | 210 | 20.97% |
| 2 | 105 | 10.48% |
| 3 | 60 | 5.990% |
| 4 | 45 | 4.490% |
| 5 | 30 | 2.490% |
| 6 | 30 | 2.490% |
| 7 | 15 | 1.990% |
| 8 | 15 | 1.490% |
| 9 | 10 | 0.990% |
| 10 | 10 | 0.990% |

From Figure 6-14 and Table 6-26, it is clear that the report period has significant effect on the average response time. Both too small report period and too long report period worsen the balancing effect. If the report period is too long, the load information of web servers can not be timely updated and the allocating decision is made based on too old load information. This will degrade the algorithm performance. On the other hand, if the report period is too small, the heavy overhead communication between the LBA and web will slow down the transmission and worsen the balancing effect. How to reduce the overhead generated by the algorithm is the key to improve the balancing effect. We use the following methods to improve the algorithm balancing effect.

- Estimate the load of web server using mathematical model

We use a longer report period, and between reports, we use the first order random walking model to estimate the load of the web server. The LBA-IV-1 (E), LBA-IV-2 (E), and LBA-IV-3 (E) algorithm modify the LBA-IV-1, LBA-IV-2 and LBA-IV-3 algorithms with this estimate method. For algorithm LBA-IV-1 (E), LBA-IV-2 (E), and LBA-IV-3 (E), we have

Load estimate = old load + document size with highest probability

Because we already had the statistic characterization of document size, we choose the document size that has highest probability plus the old load as our load estimate.

- Set overload alarming threshold

We can set the overload warning threshold for web server. When a web server finds its load is over its threshold, it sends warning message to all LBA, so all LBA will stop assign new request to this web server. We combine this strategy with algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3 to develop the algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) and LBA-IV-3 (Tc), respectively.

Figure 6-15 shows the average response time of algorithm LBA-IV-1 (E), LBA-IV-2 (E) and LBA-IV-3 (E) when the report period is 10 seconds. Before the first report comes, we use algorithm LBA-IV-1 (3), LBA-IV-2 (3) and LBA-IV-3 (3), respectively. Table 6-27 lists the statistic data of algorithm LBA-IV-1 (E), LBA-IV-2 (E) and LBA-IV-3 (E). Table 6-28 lists the overhead of algorithm LBA-IV-1 (E), LBA-IV-2 (E) and lBA-IV-3 (E) when the number of requests varies from 800 to 10000.

Figure 6-15 Average Response Time of Algorithm

Table 6-27 Statistics of Algorithm LBA-IV-1 (E), LBA-IV-2 (E) And LBA-IV-3 (E)

|  | LBA-IV-1(E) | LBA-IV-2(E) | LBA-IV-3(E) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.017276 | 0.016729 | 0.016728 |
| Average Web Queuing Delay (s) | 0.001288 | 0.000944 | 0.000944 |
| Average Router Queuing Delay (s) | 0.000045 | 0.000042 | 0.000042 |
| Average Transmission Delay (s) | 0.014422 | 0.014235 | 0.014235 |
| Average Propagation Delay (s) | 0.000257 | 0.000258 | 0.000258 |
| Average Processing Delay (s) | 0.001265 | 0.001249 | 0.001249 |

Table 6-28 Overhead of Algorithm LBA-IV-1 (E), LBA-IV-2 (E) and LBA-IV-3 (E)

| Number of Requests | Number of Extra Events | Number of Extra Events/Number of Requests |
| --- | --- | --- |
| 800 | 10 | 0.99% |
| 1000 | 10 | 0.99% |
| 2000 | 20 | 1.248% |
| 3000 | 45 | 1.499% |
| 4000 | 65 | 1.624% |
| 5000 | 85 | 1.699% |
| 7000 | 120 | 1.714% |
| 9000 | 150 | 1.725% |

From Tables 6-22,6-24, 6-25, and 6-28, we can see that the average response times the algorithm LBA-IV-1 (E), LBA-IV-2 (E) and LBA-IV-3 (E) is reduced. Comparing Table 6-28 with Table 6-23, it is clear that the overhead of algorithm LBA-IV-1 (E), LBA-IV-2 (E) and LBA-IV-3 (E) are significantly decreased.

Now we test algorithm LBA-IV-1 (Tc), LBA-IV-2 (TC) and LBA-IV-3 (Tc). We set the overload and underload alarm threshold as 10 and 2, respectively. Therefore, when the number of requests of a web is over 10, it sends an overload message to LBA. On the other hand, when the number of requests of a web is under 2, it send a message to the LBA and the LBA will start to allocate new requests to this web site. Figure 6-16 shows the average response time of algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) and LBA-IV-3 (Tc). Table 6-29 summarizes their statistic characterizations. Table 6-30 gives the overhead information of algorithm LBA-IV-1 (Tc).

Figure 6-16 Average Response Time

Table 6-29 Statistics of Algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) And LBA-IV-3 (Tc)

|  | LBA-IV-1(Tc) | LBA-IV-2(Tc) | LBA-IV-3(Tc) |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.015913 | 0.015913 | 0.015913 |
| Average Web Queuing Delay (s) | 0.000335 | 0.000335 | 0.000335 |
| Average Router Queuing Delay (s) | 0.000015 | 0.000015 | 0.000015 |
| Average Transmission Delay (s) | 0.014454 | 0.014454 | 0.014454 |
| Average Propagation Delay (s) | 0.000256 | 0.000256 | 0.000256 |
| Average Processing Delay (s) | 0.000853 | 0.000853 | 0.000853 |

Table 6-30 Overhead of Algorithm LBA-IV-1 (Tc)

| Number of Requests | Number of Extra Events | Number of Extra Events/Number of Requests |
| --- | --- | --- |
| 800 | 10 | 0.47% |
| 1000 | 10 | 0.47% |
| 2000 | 10 | 0.47% |
| 3000 | 10 | 0.47% |
| 4000 | 10 | 0.47% |
| 5000 | 10 | 0.47% |
| 7000 | 10 | 0.47% |
| 9000 | 10 | 0.47% |

From Tables 6-28 and 6-30, we can see that algorithm LBA-IV-1 (Tc) and LBA-IV-2 (Tc), LBA-IV-3 (Tc) has the lowest overhead and their balancing effect is better than other algorithms.

Tc (Threshold) is an important factor of the algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) and LBA-IV-3 (Tc). Figure 6-17 shows the average response time of the algorithm LBA-IV-1(Tc) when the overload alarm threshold changes from 5 to 20. Table 6-31 lists the corresponding overhead data.

# Figure 6-17 Average Response Time of Algorithm LBA-IV-1 (Tc)

Table 6-31 Overhead of Algorithm LBA-IV-1 (Tc)

| Threshold | Number of Extra Events | Number of Extra Events/Number of Requests |
| --- | --- | --- |
| 5 | 30 | 2.997% |
| 6 | 30 | 2.997% |
| 7 | 20 | 1.998% |
| 8 | 10 | 0.999% |
| 9 | 10 | 0.999% |
| 10 | 10 | 0.999% |
| 11 | 10 | 0.999% |
| 12 | 10 | 0.999% |
| 13 | 10 | 0.999% |
| 14 | 10 | 0.999% |
| 15 | 10 | 0.999% |

From Figure 6-17 and Table 6-31, we can see that the small threshold will generate big overhead and has poor balancing effect. Therefore we can not set the threshold too small.

6.5 SUMMARY

In this Chapter, we simulation algorithm LBA-I, LBA-I-1, LBA-I-2, LBA-II (I), LBA-II (I-1), LBA-II (I-2), LBA-II-1 (I), LBA-II-1 (I-1), LBA-II-1 (I-2), LBA-II-2 (I), LBA-II-2 (I-1), LBA-II-2 (I-2), LBA-III (I), LBA-III (I-1), LBA-III (I-2), LBA-IV-1, LBA-IV-2, LBA-IV-3, LBA-IV-1 (2), LBA-IV-2 (2), LBA-IV-3 (2), LBA-IV-1 (3), LBA-IV-2 (3), LBA-IV-3 (3), LBA-IV-1 (E), LBA-IV-2 (E), LBA-IV-3 (E), LBA-IV-1 (Tc), LBA-IV-2 (Tc), LBA-IV-3 (Tc).

In order to improve the load balancing performance, the algorithm should makes the allocating decision based on the actual load of servers. However this needs extra computation and generates communication overheads due to the additional messages used between the web server and LBA. The overhead degrades the performance of this kind of algorithms. Algorithm LBA-I and LBA-I-1 that use only the static information and has zero overhead have the best balancing effect.