# CHAPTER 7

## NWTWORK DESIGN SIMULATION

In Chapter 6, we simulated and analyzed the developed load balancing algorithms. In this chapter, we will simulate and analyze the some network design issues. Such as how many web servers at a network can let the load-balancing algorithm have the best balancing effect, how many clients at a network can let the load-balancing algorithm have the best balancing effect, In next chapter, we will summarize the statistic characterization of the load-balancing algorithms.

In this chapter, we will use algorithm LBA-I, LBA-I-1, LBA-I-2 and network r50 for the simulation. Appendix A gives its topology, bandwidth, link distance, and node degree.

7.1 SIZE AND FREQUENCY OF REQUEST

In Chapter 6, we use the distribution of document size shown in Figure 6-1, which is based on the statistic analysis results in Chapter 4. For the following simulation we use the distribution of the request size shown in Figure 7-1 and the distribution of the request interval shown in Figure 6-2:

Figure 7-1 Distribution of Request Size

In Figure 7-1, the size of 80% of requests is from 1 to 5 K, and 20 % of requests are of size over 5 K. Figure 7-2 shows the average response time of algorithm LBA-I, LBA-I-1, LBA-I-2, RR, and Random. Table 7-1 lists their statistic data.

Figure 7-2 Average Response Time

Table 7-1 Algorithm Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.023615 | 0.022086 | 0.024234 | 0.024219 | 0.024863 |
| Average Web Queuing Delay (s) | 0.000058 | 0.000067 | 0.000007 | 0.000006 | 0.000014 |
| Average Router Queuing Delay (s) | 0.000015 | 0.000014 | 0.000004 | 0.000002 | 0.000003 |
| Average Transmission Delay (s) | 0.020020 | 0.019042 | 0.020106 | 0.020047 | 0.020676 |
| Average Propagation Delay (s) | 0.002257 | 0.002249 | 0.003416 | 0.003430 | 0.003428 |
| Average Processing Delay (s) | 0.000355 | 0.000364 | 0.000356 | 0.000366 | 0.000374 |

From Table 7-1 and Figure 7-2, we can see that the load-balancing algorithm LBA-I and LBA-I-1 still have better balancing effect than algorithm RR. Comparing to algorithm RR, algorithm LBA-I and LBA-I-1 reduces 2.5% and 8.8% of response time, respectively.  Comparing to the Random algorithm, algorithm LBA-I and LBA-I-1 reduces 5.0% and 1.16% of response time, respectively. Comparing to algorithm LBA-I-2, the algorithm LBA-I and LBA-I-1 reduces 2.55 % and 8.86% of response time, respectively. Comparing Table 7-1 to Table 6-7, we can see that the transmission time is significantly reduced in this case. 11% for algorithm LBA-I and 12.7% for algorithm LBA-I-1 reduces the transmission delay. The average response time is also significantly reduced, 8.17% for algorithm LBA-I and 8.1735% for algorithm LBA-I-1. Therefore we can draw the conclusion that both the transmission delay and the average response time will be reduced if the document size is designed smaller.

Next we use the distribution of request size shown in Figure 7-3. Which has longer trailer and bigger request size than that shown in Figure 7-1.

Figure 7- 3 Distribution of Request Size

Figure 7-4 shows the average response time in this case, where we still use the distribution of the request interval shown in Figure 6-1. Table 7-2 lists the corresponding statistic characterization.

Figure 7-4 Average Response Time

Table 7-2 Algorithm Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.055493 | 0.051805 | 0.056958 | 0.056004 | 0.055689 |
| Average Web Queuing Delay (s) | 0.000365 | 0.000494 | 0.000449 | 0.000457 | 0.000372 |
| Average Router Queuing Delay (s) | 0.000041 | 0.000053 | 0.000047 | 0.000048 | 0.000040 |
| Average Transmission Delay (s) | 0.051086 | 0.047467 | 0.051729 | 0.051697 | 0.051120 |
| Average Propagation Delay (s) | 0.002271 | 0.002273 | 0.003385 | 0.003429 | 0.003463 |
| Average Processing Delay (s) | 0.000905 | 0.000902 | 0.000906 | 0.000901 | 0.000888 |

In this case, comparing to the Random algorithm, algorithm LBA-I and LBA-I-1 reduces 0.35% and 6.97% of average response time, respectively. Comparing to algorithm RR, algorithm LBA-I and LBA-I-1 reduces 0.91% and 7.5% of average response time, respectively. Comparing to algorithm LBA-I-2, algorithm LBA-I and LBA-I-1 reduces 2.57% and 9.04% of average response time, respectively. Comparing Table 7-2 to Table 6-7, we can see that the transmission delay has significantly increased. The transmission delay has increased by 99.42% for algorithm LBA-I and 117.5% for algorithm LBA-I-1, respectively. The average response time has increased by 115.7% and 107.4% for algorithm LBA-I and LBA-I-1, respectively. Therefore at same request interval, larger document size will cause longer response time.

Now we change the distribution of the request interval and use the distribution shown in Figure 7-5. The request interval shown in Figure 7-5 is faster than that in Figure 6-2.

Figure 7-5 Distribution of Request Frequency.

Figure 7-6 shows the balancing effect of different algorithms for the distribution of request size shown in Figure 7-3. Table 7-3 lists their statistic characterization.

Figure 7-6 Algorithm Average Response Time

Table 7-3 Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.054979 | 0.052330 | 0.056194 | 0.056012 | 0.057457 |
| Average Web Queuing Delay (s) | 0.000227 | 0.000243 | 0.000031 | 0.000028 | 0.000045 |
| Average Router Queuing Delay (s) | 0.000040 | 0.000053 | 0.000047 | 0.000049 | 0.000040 |
| Average Transmission Delay (s) | 0.050521 | 0.047984 | 0.050948 | 0.050728 | 0.052048 |
| Average Propagation Delay (s) | 0.002267 | 0.002237 | 0.003412 | 0.003406 | 0.003467 |
| Average Processing Delay (s) | 0.001838 | 0.001932 | 0.001788 | 0.001838 | 0.001883 |

Figure 7-7 shows the average response time of algorithm LBA-I, LBA-I-1 and LBA-I-2 for the distribution of request frequency shown in Figure 7-5 and the distribution of request size shown in Figure 7-1. Table 7-4 lists the statistic data of these algorithms.

Figure 7-7 Average Response Time

Table 7-4 Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.022080 | 0.021217 | 0.023360 |
| Average Web Queuing Delay (s) | 0.000054 | 0.000060 | 0.000007 |
| Average Router Queuing Delay (s) | 0.000017 | 0.000021 | 0.000004 |
| Average Transmission Delay (s) | 0.019065 | 0.018198 | 0.019218 |
| Average Propagation Delay (s) | 0.002221 | 0.002263 | 0.003462 |
| Average Processing Delay (s) | 0.000723 | 0.000675 | 0.000669 |

Comparing Table 7-3 and 7-4, we can see that for the same distribution of request frequency, the smaller document size will significantly reduce the transmission time and average response time.

7.3 NUMBER OF WEB SERVERS

Figures 7-8, 7-9, and 7-10 show the average response time of algorithm LBA-I, LBA-I-1, and LBS-I-2 when the number of web servers changes from 1 to 10, respectively.

Figure 7-8 Average Response Time of Algorithm LBA-I

Figure 7-9 Average Response Time of Algorithm LBA-I-1

Figure 7-10 Average Response Time of Algorithm LBA-I-2

From Figures 7-8, 7-9, and 7-10, we can see that there is an optimal value for the number of web servers. Too few or too many web servers do not have good balancing effect. We should optimize network structure to enhance the balancing efficiency.

Tables 7-5 to 7-9 lists the transmission delay, propagation delay, web queuing delay, router queuing delay, and total processing delay when the number of web servers changes from 1 to 10, respectively.

Table 7-5 Transmission Delay

| Number of Webs | Number of Webs/Number of LBAs | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- | --- |
| 1 | 2.5% | 0.019671 | 0.019671 | 0.019671 |
| 2 | 5.0% | 0.019954 | 0.019585 | 0.020220 |
| 3 | 7.3% | 0.020531 | 0.018992 | 0.020240 |
| 4 | 10.0% | 0.023017 | 0.019927 | 0.022152 |
| 5 | 12.5% | 0.020440 | 0.019805 | 0.020432 |
| 6 | 15.0% | 0.019987 | 0.019224 | 0.019715 |
| 7 | 17.5% | 0.023523 | 0.020362 | 0.021259 |
| 8 | 20.0% | 0.022733 | 0.020873 | 0.022326 |
| 9 | 22.5% | 0.022321 | 0.021554 | 0.021962 |
| 10 | 25.00% | 0.022749 | 0.021321 | 0.022532 |

Table 7-6 Propagation Delay

| Number of Webs | Number of Webs/Number of LBAS | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- | --- |
| 1 | 2.5% | 0.004169 | 0.004169 | 0.004169 |
| 2 | 5.0% | 0.003652 | 0.003586 | 0.003930 |
| 3 | 7.3% | 0.003289 | 0.003290 | 0.003777 |
| 4 | 10.0% | 0.003090 | 0.003009 | 0.004021 |
| 5 | 12.5% | 0.002340 | 0.002310 | 0.003483 |
| 6 | 15.0% | 0.002263 | 0.002376 | 0.003472 |
| 7 | 17.5% | 0.002348 | 0.002336 | 0.003667 |
| 8 | 20.0% | 0.002337 | 0.002239 | 0.003524 |
| 9 | 22.5% | 0.002257 | 0.002149 | 0.003481 |
| 10 | 25.00% | 0.002272 | 0.002262 | 0.003390 |

Table 7-7 Web Queuing Delay

| Number of Webs | Number of Webs/Number of LBAs | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- | --- |
| 1 | 2.5% | 0.000029 | 0.000029 | 0.000029 |
| 2 | 5.0% | 0.000035 | 0.000032 | 0.000006 |
| 3 | 7.3% | 0.000063 | 0.000063 | 0.000005 |
| 4 | 10.0% | 0.000046 | 0.000052 | 0.000004 |
| 5 | 12.5% | 0.000054 | 0.000050 | 0.000002 |
| 6 | 15.0% | 0.000066 | 0.000060 | 0.000005 |
| 7 | 17.5% | 0.000072 | 0.000062 | 0.000004 |
| 8 | 20.0% | 0.000069 | 0.000077 | 0.000005 |
| 9 | 22.5% | 0.000085 | 0.000072 | 0.000006 |
| 10 | 25.00% | 0.000071 | 0.000077 | 0.000009 |

Table 7-8 Router Queuing Delay

| Number of Webs | Number of Webs/Number of LBAs | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- | --- |
| 1 | 2.5% | 0.000030 | 0.000030 | 0.000030 |
| 2 | 5.0% | 0.000035 | 0.000031 | 0.000010 |
| 3 | 7.3% | 0.000018 | 0.000020 | 0.000003 |
| 4 | 10.0% | 0.000027 | 0.000021 | 0.000006 |
| 5 | 12.5% | 0.000018 | 0.000021 | 0.000003 |
| 6 | 15.0% | 0.000022 | 0.000020 | 0.000003 |
| 7 | 17.5% | 0.000015 | 0.000019 | 0.000003 |
| 8 | 20.0% | 0.000019 | 0.000019 | 0.000002 |
| 9 | 22.5% | 0.000015 | 0.000016 | 0.000004 |
| 10 | 25.00% | 0.000018 | 0.000020 | 0.000003 |

Table 7-9 Processing Delay

| Number of Webs | Number of Webs/Number of LBAs | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- | --- |
| 1 | 2.5% | 0.000609 | 0.000609 | 0.000609 |
| 2 | 5.0% | 0.000637 | 0.000628 | 0.000627 |
| 3 | 7.3% | 0.000716 | 0.000701 | 0.000660 |
| 4 | 10.0% | 0.000667 | 0.000699 | 0.000673 |
| 5 | 12.5% | 0.000696 | 0.000691 | 0.000678 |
| 6 | 15.0% | 0.000739 | 0.000730 | 0.000728 |
| 7 | 17.5% | 0.000837 | 0.000736 | 0.000761 |
| 8 | 20.0% | 0.000866 | 0.000786 | 0.000803 |
| 9 | 22.5% | 0.000859 | 0.000811 | 0.000755 |
| 10 | 25.00% | 0.000851 | 0.000801 | 0.000784 |

From the above discussion, we can see that a network with too few or too many web servers does not have good balancing effect and waste the resource. Therefore we must reasonably choose the number of web servers. From Figures 7-6, 7-7, and 7-8, we can see that when the ratio of the number of webs to the number of LBAs is around 10 % to 15 %, the algorithms have the best performance.

7.4 NUMBER OF CLIENTS

In this section, we will analyze the effect of the ration of the number of clients to the number of web servers on the load balancing performance. Figure 7-11 shows the average response time of algorithm LBA-I-1, LBA-I-1 and LBA-I-2 when the number of clients changes from 1 to 25 and the number of requests is 5000.

Figure 7-11 Average Response Time

From Figure 7-11, we can see that as the number of client’s increases, the average response time of the algorithm increases. Figure 7-12 shows the average transmission delay of the algorithm LBA-I, LBA-I-1 and LBA-I-2 when the number of clients changes from 1 to 25.

Figure 7-12 Average Transmission Delay

Figures 7-13, 7-14, and 7-15 show the propagation delay, web queuing delay, and router queuing delay of algorithm LBA-I, LBA-I-1 and LBA-I-2 when the number of clients changes from 1 to 25, respectively.

Figure 7-13 Propagation Delay

Figure 7-14 Web Queuing Delay

Figure 7-15 Router Queuing Delay

From Figures 7-13,7-14, and 7-15, we can see that as the number of clients increases the web queuing delay and the average response time will increase.

7.5 WEB SERVER RESOURCE AND BANDWIDTH

In this section we analyze the effect of the ration of the web server processing power to the bandwidth on the load balancing performance so that we can fully use the network resource.

Figure 7-16 shows the average response time of the algorithm LBA-I, LBA-I-1 and LBA-I-2 when the processing power of each web servers is increased by 5 times. Table 7-10 lists the statistic data of the algorithms.

Figure 7-16 Average Response Time

Table 7-10 Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.025418 | 0.024363 | 0.026140 |
| Average Web Queuing Delay (s) | 0.000008 | 0.000008 | 0.000001 |
| Average Router Queuing Delay (s) | 0.000024 | 0.000030 | 0.000007 |
| Average Transmission Delay (s) | 0.022603 | 0.021510 | 0.022208 |
| Average Propagation Delay (s) | 0.002246 | 0.002282 | 0.003401 |
| Ave Processing Delay (sec) | 0.000536 | 0.000533 | 0.000524 |

Comparing Table 7-10 to Table 6-7, we can see that the average response time of the algorithm LBA-I, LBA-I-1, and LBA-I-2 is reduced by 1.16%, 2.5%, and 2.39%, respectively.

Figure 7-17 shows the average response time of the algorithm LBA-I, LBA-I-1 and LBA-I-2 when 5 times and the processing power of the web server does not increase the bandwidth changed. Table 7-11 lists the statistic characterization of the algorithm LBA-I, LBA-I-1 and LBA-I-2.

Figure 7-17 Average Response Time

Table 7-11 Statistic Data

|  | LBA-I | LBA-I-1 | LBA-I-2 |
| --- | --- | --- | --- |
| Average Response Time(s) | 0.013598 | 0.013117 | 0.014401 |
| Average Web Queuing Delay (s) | 0.000081 | 0.000078 | 0.000009 |
| Average Router Queuing Delay (s) | 0.000020 | 0.000019 | 0.000006 |
| Average Transmission Delay (s) | 0.010069 | 0.009904 | 0.010192 |
| Average Propagation Delay (s) | 0.002573 | 0.002307 | 0.003401 |
| Average Processing Delay (s) | 0.000855 | 0.000809 | 0.000792 |

Comparing Table 7-11 to Table 6-7, the average response time of the algorithm LBA-I and LBA-I-1 is reduced by 47.12% and 47.5%, respectively. Comparing Table 7-11 to Table 6-10, we can see that increasing bandwidth can more significantly reduce the average response time than increasing process power of the web server.

Figures 7-18, 7-19, and 7-20 show the average response time of the algorithm LBA-I, LBA-I-1, and LBA-I-2 when the processing power of the web server changes from 1 MB to 25 MB, respectively.

Figure 7-18 Average Response Time

Figure 7-19 Average Response Time

Figure 7-20 Average Response Time

From Figures 7-18, 7-19 and 7-20, we can see that when the processing power of the web server increases from 1 MB to 10 MB, the average response time is decreased by 2.1245%. However when the processing power of the web server continually increases from 10 MB to 25 MB, the curve of the average response time is almost flat, which means that increasing the process power of the web server does not reduce the average response time much. We can conclude that when the process power of the web server is increased to a range, the average response time does not be reducing significantly. In order to fully use the network resource, the ratio of the bandwidth to the processing power of the web server should be is about 6.26%.

Figures 7-21 to 5-25 show the transmission delay, propagation delay, web queuing delay, router queuing delay, and processing delay of the algorithm LBA-I, LBA-I-1 and LBA-I-2, respectively, when the processing power of the web server increases from 1 MB to 25 MB.

Figure 5-21 Transmission Delay

Figure 5-22 Propagation Delay

Figure 5-23 Web Queuing Delay

Figure 5-24 Router Queuing Delay

Figure 5-25 Processing Delay

From Figures 5-21 to 5-25, we can see that increasing the process power of the web servers can reduce the web queuing delay and processing delay. As we have mentioned, when the processing power of the web servers is increased from 1 MB to 10 MB, the web queuing delay and processing delay are significantly reduced. However when the process power of the web servers are increased from 10 MB to 25 MB the web queuing delay and processing delay are not reduced much.

7.6 WEB SERVER LOCATION

In this section, we will analyze the effect of the web server location on the average response time of the algorithm. We randomly choose five sets of the web location given in Table 7-12.

Table 7-12 Web Location Set

| Set ID | Web Server ID |
| --- | --- |
| 1 | N01, N09, N13, N15, N18, N20, N25, N29, N35,N42 |
| 2 | N04, N05, N19, N22, N27, N32, N44, N45, N48, N49 |
| 3 | N05, N08, N18, N28, N32, N38, N39, N40, N42, N45 |
| 4 | N07, N11, N14, N20, N26, N35, N36, N37, N42, N47 |

Figure 7-26 shows the average response time of the algorithm LBA-I for these different web server locations. Table 7-13 lists their average response time.

Figure 7-26 Average Response Time

Table 7-13 Average Response Time for Different Web Locations

|  | Set 1 | Set 2 | Set 3 | Set 4 |
| --- | --- | --- | --- | --- |
| Average Response Time (s) | 0.025881 | 0.025824 | 0.02518 | 0.025778 |

From Table 7-13, we can see that the difference between the best case whose average response time is 0.025180 second and the worst case whose average response time is 0.025881 second is 0.0007 second, about 2.7%. Therefore the web server location does affect the average response time of the algorithm.

Figures 7-27 to 7-31 show the transmission delay, propagation delay, web queuing delay, router queuing delay, and process delay.

Figure 7-27 Transmission Delay

Figure 7-28 Propagation Delay

Figure 7-29 Web Queuing Delay

Figure 7-30 Router Queuing Delay

Figure 7-31 Processing Delay

From Figures 7-27 to 7-31, we can see that the key factor that dominants the balancing performance is the transmission delay. We can reduce the transmission delay by locating the web server at proper position.

Figure 7-32 shows the average response time of algorithm LBA-I-1. Table 7-13 lists the average response time for different web sets.

Figure 7-32 Average Response Time of LBA-I-1

Table 7-13 Average Response Time of Algorithm LBA-I-1

| Web Server Location | Set 1 | Set 2 | Set 3 | Set 4 |
| --- | --- | --- | --- | --- |
| Average Response Time (s) | 0.024466 | 0.024784 | 0.024921 | 0.025095 |

From Table 7-13, we can see that the best case can reduce the average response time by 2.5% relative to the worst case.

Figures 7-33 to 7-37 show the transmission delay, propagation delay, web queuing delay, router queuing delay, and process delay, respectively.

Figure 7-33 Transmission Delay of LBA-I-1

Figure 7-34 Propagation Delay of LBA-I-1

Figure 7-35 Web Queuing Delay of LBA-I-1

Figure 7-36 Router Queuing Delay of LBA-I-1

Figure 7-37 Processing Delay of LBA-I-1

Figure 7-38 shows the average response time of the algorithm LBA-I-2 for the different web server location. Table 7-14 lists the average response time.

Figure 7-38 Average Response Time of LBA-I-2

Table 14 Average Response Time of LBA-I-2 for Different Web Location4

| Set ID | Set 1 | Set 2 | Set 3 | Set 4 |
| --- | --- | --- | --- | --- |
| Average Response Time (s) | 0.026578 | 0.028933 | 0.030683 | 0.029750 |

From Table 7-14, we can see that the best case can reduce the average response time by 1.33% relative to the worst case.

Figures 7-39 to 7-43 show the transmission delay, propagation delay, web queuing delay, router queuing delay, process delay, respectively.

Figure 7-39 Transmission Delay of LBA-I-2

Figure 7-40 Propagation Delay of LBA-I-2

Figure 7-41 Web Queuing Delay

Figure 7-42 Router Queuing Delay of LBA-I-2

Figure 7-43 Processing Delay of LBA-I-2

From the above discussion, we can see that web server location does affect the average response time of the algorithms.

7.7 SUMMARY

In this chapter, we discuss some network design issues by simulation experimental. We have the following suggestions for network design.

- Design small document size. We can not control the frequency of the request, but we have the control of the document size. By using small the document size, we can reduce the response time of request.

- Choose proper ration of the web server. By selecting proper ratio, we can fully use the resource of the network and also reduce the response time of clients.

- Choose proper process power of web server.

- Set web servers at proper locations.

- Increasing the bandwidth will get better efficiency than increasing the process power of web server.