CHAPTER 8

ALGORITHM CHARACTER ANALYSIS

In this chapter, we will analyze the following characters of the load-balancing algorithms.

- Stability and Reliability

- Scalability

- Complexity

- Feasibility

We will discuss each character at following section.

8.1 Stability

From the simulation results documented in Chapter 6, we know that algorithm LBA-I and LBA-I-2 have the best load balancing performance. However algorithms LBA-I and LBA-I-1 are based on some information, such as distance, bandwidth, web server processing power. If we can precisely know that information, the algorithms can give the best performance. But if we can not know that information precisely, do algorithm LBA-I and LBA-I-1 still give the best performance?

Figure 8-1 shows the average response time of algorithm LBA-I when the error in distance/bandwidth varies from 1% to 20%. Table 8-1 lists the statistic characters.

Figure 8-1 Average Response Time of Algorithm LBA-I

Table 8-1 Statistic Data of Algorithm LBA-I

| Data Error | 0 % | 1 % | 5 % | 10 % | 20 % |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.025881 | 0.025881 | 0.025881 | 0.025881 | 0.025881 |
| Average Web Queuing Delay (s) | 0.000071 | 0.000071 | 0.000071 | 0.000071 | 0.000071 |
| Average Router Queuing Delay (s) | 0.000016 | 0.000016 | 0.000016 | 0.000016 | 0.000016 |
| Average Transmission Delay (s) | 0.022675 | 0.022675 | 0.022675 | 0.022675 | 0.022675 |
| Average Propagation Delay (s) | 0.002268 | 0.002268 | 0.002268 | 0.002268 | 0.002268 |
| Average Processing Delay (s) | 0.000851 | 0.000851 | 0.000851 | 0.000851 | 0.000851 |

From Table 8-1 and Figure 8-1, we can see that the data error does not affect the performance of the algorithm LBA-I much. Therefore algorithm LBA-I has very good stability.

Figure 8-2 shows the average response time of the algorithm LBA-I-1 when the error in Distance/Bandwidth + number of hops varies from 1% to 20%. Table 8-2 lists the statistic characters.

Figure 8-2 Average Response Time of Algorithm LBA-I-1

Table 8-2 Statistic Data of Algorithm LBA-I-1

| Data Error | 0 % | 1 % | 5 % | 10 % | 20 % |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.024466 | 0.024466 | 0.024466 | 0.024466 | 0.024466 |
| Average Web Queuing Delay (s) | 0.000079 | 0.000079 | 0.000079 | 0.000079 | 0.000079 |
| Average Router Queuing Delay (s) | 0.000022 | 0.000022 | 0.000022 | 0.000022 | 0.000022 |
| Average Transmission Delay (s) | 0.021298 | 0.021298 | 0.021298 | 0.021298 | 0.021298 |
| Average Propagation Delay (s) | 0.002260 | 0.002260 | 0.002260 | 0.002260 | 0.002260 |
| Average Processing Delay (s) | 0.000806 | 0.000806 | 0.000806 | 0.000806 | 0.000806 |

From Table 8-2 and Figure 8-2, we can see that the data error does not affect the effect of algorithm LBA-I-1 much so this algorithm has very good stability.

Next we will analyze the effect of errors in distance, bandwidth, processing power and number of hops on algorithm LBA-I. Figure 8-3 shows the average response time of algorithm LBA-I when the errors in distance, bandwidth, processing power of the web server are respectively 20%. Table 8-3 lists the statistic characterization of algorithm LBA-I.

Figure 8-3 Average Response Time of Algorithm LBA-I

Table 8-3 Statistic Data of Algorithm LBA-I

|  | No Error | 20% Bandwidth Error | 20% Distance Error | 20% Processing Power Error |
| --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.025881 | 0.026440 | 0.026041 | 0.025884 |
| Average Web Queuing Delay (s) | 0.000071 | 0.000065 | 0.000074 | 0.000072 |
| Average Router Queuing Delay (s) | 0.000016 | 0.000010 | 0.000017 | 0.000016 |
| Average Transmission Delay (s) | 0.022675 | 0.023319 | 0.022530 | 0.022676 |
| Average Propagation Delay (s) | 0.002268 | 0.002180 | 0.002564 | 0.002266 |
| Average Processing Delay (s) | 0.000851 | 0.000865 | 0.000855 | 0.000854 |

From Table 8-3 and Figure 8-3, we can see that the bandwidth error has the biggest effect on the balancing performance. The distance error has the second biggest effect on the balancing performance.

Next we analyze the effect of errors in distance, bandwidth, processing power, and number of hops on the performance of the algorithm LBA-I-1. Figure 8-4 shows the average response time of algorithm LBA-I-1 when the errors in distance, bandwidth, processing power of the web server and number of hops are respectively 20%. Table 8-4 lists the statistic characterization of the algorithm LBA-I-1.

Figure 8-4 Average Response Time of LBA-I-1

Table 8-4 Statistic Data of LBA-I-1

|  | No Error | 20% Distance Error | 20% Bandwidth Error | 20% Processing Power Error | 20% Hop Number Error |
| --- | --- | --- | --- | --- | --- |
| Average Response Time(s) | 0.024466 | 0.024818 | 0.024474 | 0.024429 | 0.024466 |
| Average Web Queuing Delay (s) | 0.000079 | 0.000074 | 0.000079 | 0.000078 | 0.000079 |
| Average Router Queuing Delay (s) | 0.000022 | 0.000018 | 0.000022 | 0.000022 | 0.000022 |
| Average Transmission Delay (s) | 0.021298 | 0.021621 | 0.021282 | 0.021265 | 0.02129 |
| Average Propagation Delay (s) | 0.002260 | 0.002294 | 0.002255 | 0.002258 | 0.00226 |
| Average Processing Delay (s) | 0.000806 | 0.000811 | 0.000806 | 0.000806 | 0.000806 |

From Figure 8-4, we can see that the primary factor that affects of algorithm LBA-I-1 performance is the distance error. Based on the above discussion we can conclude that the potential factors that may affect the performance of algorithm LBA-I and LBA-I-1 are the distance precision and bandwidth precision.

Table 8-5 is a summary of algorithm characters.

Table 8-5 Summary of Algorithm Characters

| Algorithm | Parameters | Computing Error | Period | Overhead |
| --- | --- | --- | --- | --- |
| LBA-I, LBA-I-1, LBA-I-2 | Distance, Bandwidth, Number of Hops, Processing Power, Number of Web Servers | Very Small | No | No |
| LBA-II, LBA-II(I), LBA-II(I-1), LBA-II(I-2), LBA-II-1, LBA-II-1(I), LBA-II-1(I-1), LBA-II-1(I-2), LBA-II-2, LBA-II-2(I), LBA-II-2(I-1), LBA-II-2(I-2) | Distance, Bandwidth, Number of Hops, Processing Power, Number of Webs, Number of LBAs | Small | Yes | Heavy |
| LBA-III | Processing Power, Number of Webs | Large | Yes | Heavy |
| LBA-IV-1, LBA-IV-1(2), LBA-IV-1(3), LBA-IV-1(E) LBA-IV-2, LBA-IV-2(2), LBA-IV-2(3), LBA-IV-2(E), LBA-IV-3, LBA-IV-3(2), LBA-IV-3(3), LBA-IV-3(E) | Processing Power, Distance, Bandwidth, | Large | Yes | Heavy |
| LBA-IV-1(Tc), LBA-IV-2(Tc), LBA-IV-3(Tc) | Processing Power, Distance, Bandwidth | Small | Yes | Small |

8.2 SCALABILITY

Following we will discuss the scalability characterization. Except above two network, we test another network, one has totally 400 Nodes, maximum distance is 600 km, for network topology seeing Append B. Table 8-6 summaries the average response time for different network when the Nodes get more and the distance get longer. Table 8-7 summaries the statistic characterization those three network.

# Table 8-6 Average Response Time for Different Networks

|  | LBA-I | LBA-I-1 | LBA-I-2 | RR | Random |
| --- | --- | --- | --- | --- | --- |
| New-J | 0.013440 | 0.014754 | 0.013725 | 0.013750 | 0.013760 |
| R30 | 0.025577 | 0.022668 | 0.026455 | 0.027111 | 0.026373 |
| R50 | 0.025717 | 0.024988 | 0.026782 | 0.026648 | 0.027160 |

Table 8-7 Parameters of Network

|  | Nodes | Ave Distance | Bandwidth | Web Server | Number of Clients |
| --- | --- | --- | --- | --- | --- |
| New-J | 116 | 20 km | 5 Mb | 3 | 20 |
| R30 | 450 | 400 km | 5 Mb | 10 | 20 |
| R50 | 890 | 800 km | 5 Mb | 10 | 20 |

From above analysis, we can see that the algorithm LBA-I has better scalability and better balancing effect. The algorithm LBA-I-1 has the better balancing effect for larger network.

8.3 COMPLEXITY

Table 8-8 lists the computing condition that the algorithms depend on and computing time cost of the algorithms.

Table 8-8 Summary of Algorithm Complexity

| Algorithm | Parameters | Computing Error | Complexity | Overhead |
| --- | --- | --- | --- | --- |
| LBA-I LBA-I-1 LBA-I-2 | Distance, Bandwidth, Hops, Processing Power, Number of Web Servers | Very Small | Simple | No |
| LBA-II, LBA-II(I), LBA-II(I-1), LBA-II(I-2), LBA-II-1, LBA-II-1(I), LBA-II-1(I-1), LBA-II-1(I-2), LBA-II-2, LBA-II-2(I), LBA-II-2(I-1), LBA-II-2(I-2) | Distance, Bandwidth, Hops, Processing Power, Number of Webs, Number of LBAs | Small | Complex | Heavy |
| LBA-III | Processing Power Number of Webs | Large | Yes | Heavy |
| LBA-IV-1, LBA-IV-1(2), LBA-IV-1(3), LBA-IV-1(E), LBA-IV-2, LBA-IV-2(2), LBA-IV-2(3), LBA-IV-2(E), LBA-IV-3, LBA-IV-3(2), LBA-IV-3(3), LBA-IV-3(E) | Processing Power, Distance, Bandwidth, | Large | Complex | Heavy |
| LBA-IV-1(Tc) LBA-IV-2(Tc) LBA-IV-3(Tc) | Processing Power, Distance, Bandwidth | Small | Simple | Small |

We can conclude:

- Algorithm LBA-I and LBA-I-1 are simpler and cost less computing time, but the algorithms depend on the some static information.

- Algorithm LBA-II and LBA-II-1 and LBA-II-2 are more complex than the algorithm LBA-I and LBA-I-1, cost more computing time and those algorithms have more overheads.

- Algorithm LBA-III is simpler algorithm, but because the heavy overhead, this algorithm has the worse response time.

- Algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3 is simpler, but there are too much overhead, therefore there are the worse response time.

- Algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) and LBA-IV-3 (Tc) are the simpler algorithm and cost less computing time and fewer overheads.

8.4 FEASIBILTY

We have following conclusions for all developed load-balancing algorithms.

- The algorithm LBA-I, LBA-I-1 and LBA-I-2 depend on static information, such as distance, bandwidth, and number of hops, and processing power. If we do not know that information, we can not use those algorithms. But according to Chapter 8.1, we know that the algorithm LBA-I and LBA-I-1 have better stability, so we can estimate that information, the algorithm LBA-I and LBA-I-1 still have better balancing effect. Therefore the algorithms LBA-I, LBA-I-1 still are the feasible algorithms.

- Algorithm LBA-II is a feasible algorithm, but this algorithm has heavy overhead that significantly affects the balancing effect of the algorithms, so the algorithm LBA-II is not a feasible algorithm. Its two variation algorithms LBA-II-1 and LBA-II-2 greatly decrease the overhead and improve the balancing effect of the algorithm. But the algorithms still have the worse balancing effect.

- Algorithm LBA-III is not a feasible algorithm because is has too many overheads that slow down the transmission and increase the response time.

- Algorithm LBA-IV-1, LBA-IV-2 and LBA-IV-3 are not feasible algorithms because they have too much overhead that slows down the transmission and increase the response time.

- Algorithm LBA-IV-1 (Tc), LBA-IV-2 (Tc) and LBA-IV-3 (Tc) are feasible algorithms, they have less overhead and better balancing performance.