NAME

fitness—simulator for a link restoration algorithm called Failure Immunization Technology for NEtwork Service Survivability

SYNTAX

fitness    <net_file_name>.net    /b=nodeX–nodeY    [ /options ]

Simulation Options Section (below) explains available options.  As an example, to simulate link restoration between nodes N03 and N08,  with repeat limit of 14 and network restoration signaling channels  operated at 192 kbps, in a network described in file ‘my_network.net’, the command is:

fitness     my_network.net    /b=N03–N08    /r=14    /x=192

DESCRIPTION

fitness  is a distributed network restoration simulator which implements an  enhanced version of Yang and Hasegawa’s algorithm called Failure Immunization  Technology for NEtwork Service Survivability.  fitness follows the Sender-Chooser paradigm and the Sender sends an aggregated bandwidth request along each  outgoing active span that contains spares.  The Chooser collects the incoming requests and waits for a pre-determined time-out period,  which depends on the diameter of the networks and typically set at 250 mseconds for 2 second restoration time limit. When time-out occurs, the Chooser selects the request with the largest bandwidth, sends an ack back to the  Sender, and starts the timer. Our enhancement includes the adjustment of  the next time-out period according to the hopcounts in the incoming requests, the efficient data structure that permit the simulation of large networks,  and the support of simulation parameters such as node processing time,  link delay as derived from node coordinates or actual span distances,  and various DCS operating modes.  The simulator operates on a network description file.   The user specifies a network link  break as well as desired options, and the simulator provides a step-by-step profile of the recovery process including the restored bandwidth,  percentage of the restoration level, and associated time at which that level of  restoration was achieved.

The NETRESTORE family of tools includes: network restoration simulators,  such as,  fitness, rreact, twoprong, and shn, a relaxation method based optimal spare algorithm called  rx_mnet, and network file conversion utilities to facilitate the creation of network description files, such as nps2net, np2net, ns2net, nps2dat, np2dat,  and ns2dat.

SIMULATION SCENARIO

In order to analyze a network using the  fitness simulator, a four step sequence will generally be followed.  Each of the steps below is explained in more detail in later sections by the same name.

1)  Generate Network Description File

2)  Select Simulation Options

3)  Assemble Simulation Command with Options, Run Simulation

4)  Interpret Simulation Output.

NETWORK FILE GENERATION

A set of companion tools is available to facilitate the conversion of existing network files into a NETRESTORE file format shared  by  fitness and other NETRESTORE simulators.  They provide the basic statistics of the generated network file and  generate the script file for the simulation of each link restoration in the  network.  A required input parameter for node processing delay is shared by all these file conversion utilities. nps2net takes the node, path, and spare files as input parameters.  np2net takes the node and path files as input parameters, and allows users to specify the spare to working ratio for every span as an additional input parameter. The node file contains a list of node specification lines with four fields:  sequence number, node ID, V and H coordinates. The path file contains the current traffic pattern with a node list of each of working path followed by ‘45’, DS3 bandwidth, in each line.

These two programs correlate the working  and spare channels in each span, and the internal ports of each node from the path file. ns2net takes the node and span files as input parameters.  The span file contains the span specification lines, which specify the working and span channels in each span, and the span distance in kilo meters.

The ns2net correlates the number of input ports in each node from the span  files. Check the ‘man page’ for  nps2net,   np2net, and ns2net.

The nps2net file is located in   $NETRES/bin.  As an example, the command for creating mci.net is:

nps2net    mcinodes.txt    mcipaths.txt    mcispares.txt    mci.net    0.01

Three files are required as input (nodes, paths, and spares)  followed by the name of the target .net file and the default message processing delay (in seconds).

To change the message processing time of a specific node, the node specific repeat limit, or the span distance of a span, users are referred to the ‘man page’ for the  NETRESTORE file format. The current version of simulators is case sensitive on the .net filename. Please use all lower cases for the .net filenames.

SIMULATION OPTIONS

Options and parameters available with fitness are outlined below.  Each  option is invoked using the first character (lower case) of the option  in question.

1TSTIME —  This option relates to the transmission time of each individual signature.  For those wishing a more fine grained analysis, the node signature transmission time can be set to something other than the default 0.0 seconds.  For example, a delay of 2 msec would be set using:     /1=0.002

2INDEX —  Refractive index of the optical fiber can be specified with this option, which defaults to 1.5, corresponding to a 5 microsecond delay per Km.  It may be changed to 1.4 using:     /2=1.4

BREAK —  Break is the means by which link failures are specified.   The format is /b=<node1>(<node2>.   This is a required parameter.  The user specifies the end nodes using  the same names as are contained in the companion ‘.net’ network file.         Note that the name of a node, N07, is different from N7 and node 00 is  interpreted different from node 0.  For the break between N02 and N00, use: 	 /b=N02(N01

CROSS_CONNECT_TIME —  This is the time delay for a node to effect DCS cross connect.  A default time of  0.01 seconds is assumed.  An 8 msec time would be specified as:     /c=0.008

DEBUG —  The DEBUG option is not interactive, but simply provides more detail on the restoration process.  Specifically, it includes the output of additional simulation information to a log file (default NETSIM.OUT), a complete copy of the path listing as found in the .net file, as well as a list of specific path IDs which were disrupted.  Details of the broadcast phase are also included.  To invoke this option, add the  ‘/d’ qualifier to the simulation command.

INTERACTIVE —  More extensive diagnosis information on fault recovery progress is  possible using the interactive mode.  Details of events within each node are reported, for example.  The user is given the option to continue examining events, abort, or skip ‘n’ events before stopping for another visual check.  Interactive operation is invoked using:     /i

MSG_LENGTH —  Restoration time depends on the average length (bytes)  of restoration messages exchanged by distributed nodes.  The default message length is 8 bytes.  Restoration message length could be changed to 12 bytes using:     /m=12

OUT —  Simulation results are stored in a default log file called  NETSIM.OUT.  An alternative file name can be specified using:	/out=<file_name>

PPTOVERRIDE —  The default node processing time for each signature (distinct from 1STSTIME) used in ".net" files created with NETRESTORE translation utilities is ten msec. This overrides the node processing time of individual nodes, read in as the third parameter of the first line of each node description in the .net file.  To override the node processing time  to 8 msec, use:     /p=0.008

REPEATS —  This parameter represents the maximum repeat limit or hop count limit (13 is default) for restoration requests in the broadcast phase.   It is observed that increasing repeat limit does not guarantee the increase in restoration level with a real-time constrain. The increase message volume  may cause network congestion and results in slower restoration time and lower restoration level. Specify 9 hop limit as:     /r=9

STOPTIME —  Upper limit on simulation runtime (sec).  Default value  is ten (10.0) seconds.  A five second runtime limit is  specified as:     /s=5.0

TIMEOUT —  In the event that the Sender and Chooser are unable to achieve full restoration, the Sender will time-out and cancel the restoration request, releasing reserved bandwidth.  A default timeout value of ten (10.0) seconds is assumed.  To get a timeout of 5 seconds, use:     /t=5.0

WRITE_LINK —  The default is to use the link distance field  from the .net file.  Specifying  /w  as an option will cause the  simulator to calculate the link distance  (and hence link delay) according to V&H or pseudo latitude  and longitude coordinates as appropriate.

X_SPEED —  Transmission speed (kbps) for restoration messages on all links can be set with this option.  A default value of  8 kbps  is assumed.  A transmission speed of 384 kbps is specified as:     /x=384

Y_PARALLEL_DCS_MODE —   The default is batch processing mode where the DCS connections of all the  found bandwidth in a message processing can be done in one CROSS_CONNECT_TIME. /y=1 specifies the sequential DCS processing mode where each  channel connection is done in one CROSS_CONNECT_TIME. /y=k, where k is an integer greater than 1, specifies the parallel DCS processing mode where the found bandwidth are connected in k channels as a batch and each k channels are connected in CROSS_CONNECT_TIME. Note that all the simulators implement this option except shnnew which finds and connects individual spare paths one at a time.A parallel DCS processing of connecting 4 channels in a batch is specified as:     /y=4

SIMULATION OUTPUT INTERPRETATION

Simulation output starts with the statement "FITNESS algorithm results...with <net_file_name>".   The first portion of the simulation output documents the principal options selected for this specific run.  Next, fitness reads in the .net file and  checks its integrity. For example, the total  number of working ports of a node matches that implies by the working channels  in the node’s spans. The end nodes of the user specified link failure are listed, followed by the bandwidth needed for full restoration.

Restoration progress is reported by way of one record types.  An example of the progress report with the simulation of the following command,

fitness   /b=N07-N04   /y=1

is as follows:

wave number in the new internal timeout=001
Path  1 (27 bw) 33.33% rstrd at 606.48 msec ( (N04 N05 N07)
wave number in the new internal timeout=002
Path  2 (20 bw) 58.02% rstrd at 938.88 msec ( (N04 N10 N08 N03 N07)
wave number in the new internal timeout=003
Path  3 (16 bw) 77.78% rstrd at 1204.30 msec ( (N04 N06 N07)
wave number in the new internal timeout=004
Path  4 (14 bw) 95.06% rstrd at 1510.40 msec ( (N04 N10 N07)
wave number in the new internal timeout=005
Path  5 ( 3 bw) 98.77% rstrd at 1879.15 msec ( (N04 N02 N00 N03 N08 N10 N07)
Path  6 ( 1 bw)100.00% rstrd at 2220.80 msec ( (N04 N02 N00 N05 N07)
access file nj.dat.ls/N04_N07cut.l
optimal bandwidth that can be restored=81
optimal spare used =204
N07-N04 81/81=100.00% @2.220800 msgs=199/200 PNE=81/81 PLE=204/216

In this instance, the DCS’ are operated at the sequential processing mode, as it is indicated  by the option /y=1. Each channel is connected with the default CROSS_CONNECT_TIME=0.01 seconds  by the DCS’.  Path 1 is reported as being restored after an  elapsed time of 606.48 msec.  It restored 27 channels and the accumulated  percentage of restoration level is indicated as 33.33%.   Specifically, a restoration path is found that originates from node N04,  passes through node N05, and terminates at node N07.  In fact, this is what is reported in the last part of the record pointed by an arrow. Note that here the Sender, N04, received the the ack message of 27 channels as early as 336.48 msec. But since its DCS is operated at the sequential  processing mode with each channel connected at 0.01 seconds interval,  Path 1 does not restore the last of 27 channels until 336.48+27*10=606.48 msec.

The last line of output again summarizes the end nodes connected to the failed link, restored bandwidth, the lost bandwidth,  (also expressed as a percent).  The time at which this level of restoration  was achieved is reported.  The two numbers after "msgs=" represent  respectively the number of messages needed to restore bandwidth, and the  total number of messages required by the algorithm (including cleanup). PNE stands for Path Number Efficiency. It is a measure for evaluating the restoration level achieved by a network restoration method.  It contains two numbers. The first number represents the number of paths restored by the network restoration method being evaluated. The second number represents the maximum number of paths that can be restored. It was typically computed by  an optimal algorithm called rx_mnet and read in by fitness.    PLE stands for Path Length Efficiency. It is a measure for evaluating the  efficiency of a network restoration method in terms of the spare usage. It contains two numbers. The first number is the total number of spares in  the paths found by the optimal spare usage algorithm.  The second number is the total number of spares in the paths found by the network restoration method being evaluated.  Note that the PLE ratio is only meaningful when the PNE=1. The higher the PLE ratio the better.

Here fitness restores 81 channels the same as that found by the optimal algorithm. But fitness found paths that use 216 spares,  while rx_mnet found paths that use 204 spares.  fitness also appends this summary information line to the file  netres.fit.res in the working directory.  This allows a script with all the span breaks to accumulate the summarized network restoration results.

BUG REPORT

Please send bug report with the platform where fitness is executed and  the specific scenario where the bug occurred to chow@quandary.uccs.edu.  We will try to reply as early as possible.