## Slide 1
Content Web Switch
Weihong Wang

## Slide 2
What is a Content Switch?
A network device which routes the user requests based on their
contents and headers to a set of real servers.
A Content Switch can route the incoming request based on:
- url - email address
- http meta header - IMAP/POP login
- cookie value - UDP/NFS file path,block
- ssl session ID - telnet
- XML tags - ftp
It can be configured as:
- firewall.
- load balancing device or load distribution device.
- fail-over clustering device.

## Slide 3
Content Switch Load Balancing Web Server
Content Switch is a network component load balancing web server.
The performance of a web server farm can be improved by distributing
incoming request to a set of web servers.
The request distribution can be based on
- IP address and port# , Layer4 switching.
- Session Layer, Application Layer information, L5,L7 switching.

## Slide 4
ArrowPoint Network Services
(Support url and cookie-based switching)
. Who the customer is based on user cookie located within HTTP header.
. What information or transaction the customer is requesting.
. Where best to service the customers.

## Slide 5: Content Switch Architecture
From Apostolopoulos2000.
Port controller matches incoming packets
Forward packets to content switch processor or route them directly.
Rule matching results download to port controller
Content switch processor

## Slide 6: Content Switch Operations
Content Switching Rule Matching Algorithm
Header
Content Extraction
Packet Classification
Content
Switch
Rules
Packet Routing (Load Balancing)
CS Rule Editor
Incoming
Packets
Forward
Packet
To
Servers
Network Path Info
Server Load Status

## Slide 7
The Main Tasks of Content Switch
Packet Classification.
- Rule Configuration.
- Rule Matching Process.
TCP Traffic Forwarding Method.
- NAT, IP/Tunnel, IP/Direct Routing.
- Delayed Binding.

## Slide 8
Two design approaches of Content Switch
Process content switching on application level.
For example: Apache, Jserve, Java Servlet.
Process content switching on tcp/ip level.
Need to modify operating system kernel.
For example: using NAT to develop a content switch.

## Slide 9
Cisco Content Engine 2.20(CE)
Cisco CE supports HTTP and HTTPS proxy server.
CE examines web request and makes the action decision such as block,cache, or proxy.
The syntax of Rule is:
Rule action pattern-type patterns
rule no-cache url-regex\. *cgi-bin.*
rule block domain \.foo.com bar.com
rule no-cache dst-ip 172.77.120.0 255.255.192.0
The first rule configures that the incoming packets with the url matching the pattern “*cgi-bin” will not be forward to the proxy servers.

## Slide 10
Intel Action/Classification Engines(ACEs)
.ACE classifies incoming packets according to the predefined rule files.
ACE then triggers action in the associated action files.
ACE use Network Classification Language(NCL) to configure rules.
ACE is developed in tcp/ip level.
Example of NCL,
Rule check_http{tcp&&(tcp.sport==80)}{action_scan()}
- check_http is the name of the rule, {tcp&&(tcp.sport==80)} is class
matching condition, and {action_scan()} is action function of this condition.
- This rule means that incoming request with protocol=tcp and port=80 will
go to action “action_scan()”.
- NCL is simple for configuration.

## Slide 11
More Examples of Content Switch Rules
Cisco Network Based Application Recognition
Router(config)#class-map match-all http_secure
Router(config)#match protocol secure-http
Router(config)#class-map match any audio_video
Router(config)#match protocol http mime “audio/*”
Router(config)#match protocol http mime “video/*”
Router(config)#policy-map e-express
Router(config-pmap-c)#class http_secure
Router(config-pmap-c)#bandwidth 32
Router(config-pmap-c)#class audio_video
Router(config-pmap-c)#bandwidth 10
First define classes for secure http request and
audio/video request, and then distribute the
outbound bandwidth for each class.

## Slide 12
More Examples of Content Switch Rules
Foundry ServerIron
ServerIron(config)#url-map gifPolicy
ServerIron(config-url-gifPolicy)#method suffix
ServerIron(config-url-gifPolicy)#match “gif”1
ServerIron(config-gifPolicy)#default 2
ServerIron(config-gifPolicy)#exit
If the suffix of url in the incoming packets is gif, route to server
group 1, else route to server group 2.
Intel IX-API SDK
Rule check_src {ip.src==10.10.10.30} {action_A()}
Rule check_http{tcp&&(tcp.sport==80)}{action_scan()}
The meaning of rule check_src is: if source ip address
is 10.10.10.30, then execute the action function “action_A()”.

## Slide 13
Content Switching Rule Matching Algorithm
Brute Forced Sequential Execution – Early rules
have higher priority.
Easy to solve conflict problem.
Ways to speed up the process of rule matching:
- Set flags based on the headers and content
by-passed rules not related.
- Use compiler-optimization techniques to speed
up the set of rule.

## Slide 14
Content Switch Rule Syntax
if (condition) then (action)
Examples,
If( (iph->saddr==128.198.192.194)&&(tcph->dport==80)&&(iph->protocol==TCP))
then route_1(NONSTICKY, schedule)
- ( (iph->==128.198.192.194)…) is the combined condition,
- route_1() is the action subroutine. It will do:
> NONSTICKY means the connection is configured as not sticky connection,
> schedule is the schedule algorithm assigned for the connection .
> for the nonsticky connection scheduler should reschedule the real server
every time when Content Switch gets the http request.
> add the new scheduled real serve to the connection list.

## Slide 15
Content Switch Rule Syntax
If (iph->protocol==UDP)
then route_2(NONSTICKY, schedule)
- if coming packet is a UDP packet.
- route_2() will do:
> non-sticky connection. Next request will go through rule
matching again.
> Use “schedule” algorithm

## Slide 16
Content Switch Rule Syntax
If (http->cookie==VALUE)
then route_3(STICKY, schedule)
The current request will be forwarded according to the “schedule” algorithm to a real server, say real server 1.
The following requests from the same session will be forwarded to
same real server1.

## Slide 17: Packet Processing in Content Switch
Phase 1:
Phase 2:
Phase 3:

## Slide 18: Packet Processing in Content Switch
Phase1: Client establishes a TCP connection with
Content Switch.
Phase2: Content Switch examines the content of the
request and choose a real server to establish
a TCP connection with the real server.
Phase3: - NAT approach.
    Content Switch forward data in between
client and server.
- IP Tunnel/IP Direct Routing.
Client and server communicate directly
without going through Content Switch.

## Slide 19
Flow Chart of Content Switch (NAT)
packet from client
input to ip_input
connection established?
TCP/SYN?
create ACK back msg
send back ACK
to client
masquerade ip addr
port,seq.
forward ib packet
return
return
choose server
masq SYN msg
forward to server
choose server
masq UDP packet
forward to server
deliver to
upper layer
TCP/data/ack
UDP?
y
n
y
y
y
n
n
n

## Slide 20
Flow Chart of Content Switch(NAT)
packet from back server
Connection established?
msaq packet
forward it
return
SYN/ACK?
create connection hash table
masq ip addr,
port,seq.
forward saved
ip packet
forward as normal
input to ip_forward