Computer Science 522

Computer Communication

IEEE 802.11:

The Wireless LAN Standard

by

Brian Roberts

December 10, 2000

- Introduction

A wireless LAN (WLAN) is a data transmission system designed to provide location-independent network access between computing devices by using radio waves rather than a cable infrastructure. In the corporate enterprise, wireless LANs are usually implemented as the final link between the existing wired network and a group of client computers, giving these users wireless access to the full resources and services of the corporate network across a building or campus setting.

WLANs are on the verge of becoming a mainstream connectivity solution for a broad range of business customers. The wireless market is expanding rapidly as businesses discover the productivity benefits of going wire-free. According to Frost and Sullivan, the wireless LAN industry exceeded $300 million in 1998 and will grow to $1.6 billion in 2005. To date, wireless LANs have been primarily implemented in vertical applications such as manufacturing facilities, warehouses, and retail stores. The majority of future wireless LAN growth is expected in healthcare facilities, educational institutions, and corporate enterprise office spaces. In the corporation, conference rooms, public areas, and branch offices are likely venues for WLANs.

The widespread acceptance of WLANs depends on industry standardization to ensure product compatibility and reliability among the various manufacturers. The Institute of Electrical and Electronics Engineers (IEEE) ratified the original 802.11 specification in 1997 as the standard for wireless LANs. That version of 802.11 provides for 1 Mbps and 2 Mbps data rates and a set of fundamental signaling methods and other services.

The most critical issue affecting WLAN demand has been limited throughput. The data rates supported by the original 802.11 standard are too slow to support most general business requirements and have slowed adoption of WLANs. Recognizing the critical need to support higher data-transmission rates, the IEEE recently ratified the 802.11b standard (also known as 802.11 High Rate) for transmissions of up to 11 Mbps. Global regulatory bodies and vendor alliances have endorsed this new high-rate standard, which promises to open new markets for WLANs in large enterprise, small office, and home environments. With 802.11b, WLANs will be able to achieve wireless performance and throughput comparable to wired Ethernet.

Outside of the standards bodies, wireless industry leaders have united to form the Wireless Ethernet Compatibility Alliance (WECA). WECA's mission is to certify cross-vendor interoperability and compatibility of IEEE 802.11b wireless networking products and to promote that standard for the enterprise, the small business, and the home. Members include WLAN semiconductor manufacturers, WLAN providers, computer system vendors, and software makers—such as 3Com, Aironet, Apple, Breezecom, Cabletron, Compaq, Dell, Fujitsu, IBM, Intersil, Lucent Technologies, No Wires Needed, Nokia, Samsung, Symbol Technologies, Wayport, and Zoom.

- IEEE 802.11 and 802.11b Technology

As the globally recognized LAN authority, the IEEE 802 committee has established the standards that have driven the LAN industry for the past two decades, including 802.3 Ethernet, 802.5 Token Ring, and 802.3z 100BASE-T Fast Ethernet. In 1997, after seven years of work, the IEEE published 802.11, the first internationally sanctioned standard for wireless LANs. In September 1999 they ratified the 802.11b “High Rate” amendment to the standard, which added two higher speeds, 5.5 Mbps and 11 Mbps, to 802.11.

With 802.11b WLANs, mobile users can get Ethernet levels of performance, throughput, and availability. The standards-based technology allows administrators to build networks that seamlessly combine more than one LAN technology to best fit their business and user needs.

Like all IEEE 802 standards, the 802.11 standards focus on the bottom two levels of the ISO model, the physical layer and data link layer (Figure 1). Any LAN application, network operating system, or protocol, including TCP/IP and Novell NetWare, will run on an 802.11-compliant WLAN as easily as they run over Ethernet.

Figure 1. 802.11 and the ISO Model

The basic architecture, features, and services of 802.11b are defined by the original 802.11 standard. The 802.11b specification affects only the physical layer, adding higher data rates and more robust connectivity.

- The 802.11 Physical Layer

The three physical layers originally defined in 802.11 included two spread-spectrum radio techniques and a diffuse infrared specification. The infrared standard supported operates in the 850-to-950nM band with peak power of 2 W. The modulation for infrared is accomplished using either 4 or 16-level pulse-positioning modulation. The physical layer supports two data rates, 1 and 2Mbps. The radio-based standards operate within the 2.4 GHz ISM band. These frequency bands are recognized by international regulatory agencies, such as the FCC (USA), ETSI (Europe), and the MKK (Japan) for unlicensed radio operations. As such, 802.11-based products do not require user licensing or special training. Spread-spectrum techniques, in addition to satisfying regulatory requirements, increase reliability, boost throughput, and allow many unrelated products to share the spectrum without explicit cooperation and with minimal interference.

The original 802.11 wireless standard defines data rates of 1 Mbps and 2 Mbps via radio waves using frequency hopping spread spectrum (FHSS) or direct sequence spread spectrum (DSSS). It is important to note that FHSS and DSSS are fundamentally different signaling mechanisms and will not interoperate with one another. Using the frequency hopping technique, the 2.4 GHz band is divided into 75 one-MHz subchannels. The sender and receiver agree on a hopping pattern, and data is sent over a sequence of the subchannels. Each conversation within the 802.11 network occurs over a different hopping pattern, and the patterns are designed to minimize the chance of two senders using the same subchannel simultaneously. FHSS techniques allow for a relatively simple radio design, but are limited to speeds of no higher than 2 Mbps. This limitation is driven primarily by FCC regulations that restrict subchannel bandwidth to 1 MHz. These regulations force FHSS systems to spread their usage across the entire 2.4 GHz band, meaning they must hop often, which leads to a high amount of hopping overhead.

In contrast, the direct sequence signaling technique divides the 2.4 GHz band into 14 twenty-two MHz channels. Adjacent channels overlap one another partially, with 3 of the 14 being completely nonoverlapped. Data is sent across one of these 22 MHz channels without hopping to other channels. To compensate for noise on a given channel, a technique called “chipping” is used. Each bit of user data is converted into a series of redundant bit patterns called “chips.” The inherent redundancy of each chip combined with spreading the signal across the 22 MHz channel provides for a form of error checking and correction; even if part of the signal is damaged, it can still be recovered in many cases, minimizing the need for retransmissions.

- 802.11b Enhancements to the PHY Layer

The key contribution of the 802.11b addition to the wireless LAN standard was to standardize the physical layer support of two new speeds, 5.5 Mbps and 11 Mbps. To accomplish this, DSSS had to be selected as the sole physical layer technique for the standard since, as noted above, frequency hopping cannot support the higher speeds without violating current FCC regulations. The implication is that 802.11b systems will interoperate with 1 Mbps and 2 Mbps 802.11 DSSS systems, but will not work with 1 Mbps and 2 Mbps 802.11 FHSS systems.

The original 802.11 DSSS standard specifies an 11-bit chipping—called a Barker sequence—to encode all data sent over the air. Each 11-chip sequence represents a single data bit (1 or 0), and is converted to a waveform, called a symbol, that can be sent over the air. These symbols are transmitted at a 1 MSps (1 million symbols per second) symbol rate using a technique called Binary Phase Shift Keying (BPSK). In the case of 2 Mbps, a more sophisticated implementation called Quadrature Phase Shift Keying (QPSK) is used; it doubles the data rate available in BPSK, via improved efficiency in the use of the radio bandwidth. To increase the data rate in the 802.11b standard, advanced coding techniques are employed. Rather than the two 11-bit Barker sequences, 802.11b specifies Complementary Code Keying (CCK), which consists of a set of 64 eight-bit code words. As a set, these code words have unique mathematical properties that allow them to be correctly distinguished from one another by a receiver even in the presence of substantial noise and multipath interference (e.g., interference caused by receiving multiple radio reflections within a building). The 5.5 Mbps rate uses CCK to encode 4 bits per carrier, while the 11 Mbps rate encodes 8 bits per carrier. Both speeds use QPSK as the modulation technique and signal at 1.375 MSps. This is how the higher data rates are obtained. Table 1 shows the differences. To support very noisy environments as well as extended range, 802.11b WLANs use dynamic rate shifting, allowing data rates to be automatically adjusted to compensate for the changing nature of the radio channel. Ideally, users connect at the full 11 Mbps rate. However when devices move beyond the optimal range for 11 Mbps operation, or if substantial interference is present, 802.11b devices will transmit at lower speeds, falling back to 5.5, 2, and 1 Mbps. Likewise, if the device moves back within the range of a higher-speed transmission, the connection will automatically speed up again. Rate shifting is a physical-layer mechanism transparent to the user and the upper layers of the protocol stack.

| Table 1. 802.11b Data Rate Specifications |
| --- |
| Data Rate | Code Length | Modulation | Symbol Rate | Bits/Symbol |
| 1 Mbps | 11 (Barker Sequence) | BPSK | 1 MSps | 1 |
| 2 Mbps | 11 (Barker Sequence) | QPSK | 1 MSps | 2 |
| 5.5 Mbps | 8 (CCK) | QPSK | 1.375 MSps | 4 |
| 11 Mbps | 8 (CCK) | QPSK | 1.375 MSps | 8 |

- Compliance Tables

Table 2 lists the power levels permitted in each of the regions.

Table 2, Transmit Power Levels for Different Regions

| Maximum Output Power | Geographic Location | Compliance Document |
| --- | --- | --- |
| 1000 mW | USA | FCC 15.247 |
| 100 mW (EIRP) | EUROPE | ETS 300-328 |
| 10 mW/MHz | JAPAN | MPT ordinance 79 |

Table 3 lists the allowed center frequencies and the corresponding channel number for the three major markets areas for the operation of direct sequence spread spectrum physical layer implementations.

Table 3 DSSS Frequencies for Operating in Different Regions

| Channel Number | North American Frequencies | European Frequencies | Japanese Frequency |
| --- | --- | --- | --- |
| 1 | 2412 MHz | N/A | N/A |
| 2 | 2417 MHz | N/A | N/A |
| 3 | 2422 MHz | 2422 MHz | N/A |
| 4 | 2427 MHz | 2427 MHz | N/A |
| 5 | 2432 MHz | 2432 MHz | N/A |
| 6 | 2437 MHz | 2437 MHz | N/A |
| 7 | 2442 MHz | 2442 MHz | N/A |
| 8 | 2447 MHz | 2447 MHz | N/A |
| 9 | 2452 MHz | 2452 MHz | N/A |
| 10 | 2457 MHz | 2457 MHz | N/A |
| 11 | 2462 MHz | 2462 MHz | N/A |
| 12 | N/A | N/A | 2484 MHz |

Table 4 lists the range of center frequencies to be used for FH physical layer implementations. Within these ranges there are sets of hopping frequencies defined for operation of FH networks. Depending upon the country that the WLAN is used in there is a defined number of channels to be used in each hop set.

Table 4, Operating Frequency Range

| Lower Limit | Upper Limit | Regulatory Range | Geography |
| --- | --- | --- | --- |
| 2.402 GHz | 2.480 GHz | 2.400-2.4835 GHz | North America* |
| 2.402 GHz | 2.480 GHz | 2.400-2.4835 GHz | Europe* |
| 2.473 GHz | 2.495 GHz | 2.471-2.497 GHz | Japan* |
| 2.447 GHz | 2.473 GHz | 2.445-2.475 GHz | Spain* |
| 2.448 GHz | 2.482 GHz | 2.4465-2.4835 GHz | France* |

* The frequency ranges in this table are subject to the geographic specific regulatory authorities

Table 5 lists the minimum required for each country and the number defined for 802.11 operation.

Table 5, Number of Operating Channels

| Minimum* | Hopping Set | Geography |
| --- | --- | --- |
| 75 | 79 | North America* |
| 20 | 79 | Europe* |
| Not Applicable | 23 | Japan* |
| 20 | 27 | Spain* |
| 20 | 35 | France* |

* The number of required hopping channels is subject to the geographic specific Regulatory Authorities

The next set of tables defines the center frequencies for the channel numbers for the different regulatory regions.

Table 6, North American and European Requirements (Values specified in GHz)

| Channel # | Value | Channel # | Value | Channel # | Value |
| --- | --- | --- | --- | --- | --- |
| 2 | 2.402 | 28 | 2.428 | 54 | 2.454 |
| 3 | 2.403 | 29 | 2.429 | 55 | 2.455 |
| 4 | 2.404 | 30 | 2.430 | 56 | 2.456 |
| 5 | 2.405 | 31 | 2.431 | 57 | 2.457 |
| 6 | 2.406 | 32 | 2.432 | 58 | 2.458 |
| 7 | 2.407 | 33 | 2.433 | 59 | 2.459 |
| 8 | 2.408 | 34 | 2.434 | 60 | 2.460 |
| 9 | 2.409 | 35 | 2.435 | 61 | 2.461 |
| 10 | 2.410 | 36 | 2.436 | 62 | 2.462 |
| 11 | 2.411 | 37 | 2.437 | 63 | 2.463 |
| 12 | 2.412 | 38 | 2.438 | 64 | 2.464 |
| 13 | 2.413 | 39 | 2.439 | 65 | 2.465 |
| 14 | 2.414 | 40 | 2.440 | 66 | 2.466 |
| 15 | 2.415 | 41 | 2.441 | 67 | 2.467 |
| 16 | 2.416 | 42 | 2.442 | 68 | 2.468 |
| 17 | 2.417 | 43 | 2.443 | 69 | 2.469 |
| 18 | 2.418 | 44 | 2.444 | 70 | 2.470 |
| 19 | 2.419 | 45 | 2.445 | 71 | 2.471 |
| 20 | 2.420 | 46 | 2.446 | 72 | 2.472 |
| 21 | 2.421 | 47 | 2.447 | 73 | 2.473 |
| 22 | 2.422 | 48 | 2.448 | 74 | 2.474 |
| 23 | 2.423 | 49 | 2.449 | 75 | 2.475 |
| 24 | 2.424 | 50 | 2.450 | 76 | 2.476 |
| 25 | 2.425 | 51 | 2.451 | 77 | 2.477 |
| 26 | 2.426 | 52 | 2.452 | 78 | 2.478 |
| 27 | 2.427 | 53 | 2.453 | 79 | 2.479 |
|  |  |  |  | 80 | 2.480 |

Table 7, Japanese Requirements (Values specified in GHz)

| Channel # | Value | Channel # | Value | Channel # | Value |
| --- | --- | --- | --- | --- | --- |
| 73 | 2.473 | 81 | 2.481 | 89 | 2.489 |
| 74 | 2.474 | 82 | 2.482 | 90 | 2.490 |
| 75 | 2.475 | 83 | 2.483 | 91 | 2.491 |
| 76 | 2.476 | 84 | 2.484 | 92 | 2.492 |
| 77 | 2.477 | 85 | 2.485 | 93 | 2.493 |
| 78 | 2.478 | 86 | 2.486 | 94 | 2.494 |
| 79 | 2.479 | 87 | 2.487 | 95 | 2.495 |
| 80 | 2.480 | 88 | 2.488 | - | - |

Table 8, Spanish Requirements (Values specified in GHz)

| Channel # | Value | Channel # | Value | Channel # | Value |
| --- | --- | --- | --- | --- | --- |
| 47 | 2.447 | 56 | 2.456 | 65 | 2.465 |
| 48 | 2.448 | 57 | 2.457 | 66 | 2.466 |
| 49 | 2.449 | 58 | 2.458 | 67 | 2.467 |
| 50 | 2.450 | 59 | 2.459 | 68 | 2.468 |
| 51 | 2.451 | 60 | 2.460 | 69 | 2.469 |
| 52 | 2.452 | 61 | 2.461 | 70 | 2.470 |
| 53 | 2.453 | 62 | 2.462 | 71 | 2.471 |
| 54 | 2.454 | 63 | 2.463 | 72 | 2.472 |
| 55 | 2.455 | 64 | 2.464 | 73 | 2.473 |

Table 9, French Requirements (Values specified in GHz)

| Channel # | Value | Channel # | Value | Channel # | Value |
| --- | --- | --- | --- | --- | --- |
| 48 | 2.448 | 60 | 2.460 | 72 | 2.472 |
| 49 | 2.449 | 61 | 2.461 | 73 | 2.473 |
| 50 | 2.450 | 62 | 2.462 | 74 | 2.474 |
| 51 | 2.451 | 63 | 2.463 | 75 | 2.475 |
| 52 | 2.452 | 64 | 2.464 | 76 | 2.476 |
| 53 | 2.453 | 65 | 2.465 | 77 | 2.477 |
| 54 | 2.454 | 66 | 2.466 | 78 | 2.478 |
| 55 | 2.455 | 67 | 2.467 | 79 | 2.479 |
| 56 | 2.456 | 68 | 2.468 | 80 | 2.480 |
| 57 | 2.457 | 69 | 2.469 | 81 | 2.481 |
| 58 | 2.458 | 70 | 2.470 | 82 | 2.482 |
| 59 | 2.459 | 71 | 2.471 | - | - |

- The 802.11 Data Link Layer

The data link layer within 802.11 consists of two sublayers: Logical Link Control (LLC) and Media Access Control (MAC). 802.11 uses the same 802.2 LLC and 48-bit addressing as other 802 LANs, allowing for very simple bridging from wireless to IEEE wired networks, but the MAC is unique to WLANs. The 802.11 MAC is very similar in concept to 802.3, in that it is designed to support multiple users on a shared medium by having the sender sense the medium before accessing it. For 802.3 Ethernet LANs, the Carrier Sense Multiple Access with Collision Detection (CSMA/CD) protocol regulates how Ethernet stations establish access to the wire and how they detect and handle collisions that occur when two or more devices try to simultaneously communicate over the LAN. In an 802.11 WLAN, collision detection is not possible due to what is known as the “near/far” problem: to detect a collision, a station must be able to transmit and listen at the same time, but in radio systems the transmission drowns out the ability of the station to “hear” a collision. To account for this difference, 802.11 uses a slightly modified protocol known as Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA) or the Distributed Coordination Function (DCF). CSMA/CA attempts to avoid collisions by using explicit packet acknowledgment (ACK), which means an ACK packet is sent by the receiving station to confirm that the data packet arrived intact.

CSMA/CA works as follows. A station wishing to transmit senses the air, and, if no activity is detected, the station waits an additional, randomly selected period of time and then transmits if the medium is still free. If the packet is received intact, the receiving station issues an ACK frame that, once successfully received by the sender, completes the process. If the ACK frame is not detected by the sending station, either because the original data packet was not received intact or the ACK was not received intact, a collision is assumed to have occurred and the data packet is transmitted again after waiting another random amount of time. CSMA/CA thus provides a way of sharing access over the air. This explicit ACK mechanism also handles interference and other radio-related problems very effectively. However, it does add some overhead to 802.11 that 802.3 does not have, so that an 802.11 LAN will always have slower performance than an equivalent Ethernet LAN.

Another MAC-layer problem specific to wireless is the “hidden node” issue, in which two stations on opposite sides of an access point can both “hear” activity from an access point, but not from each other, usually due to distance or an obstruction. To solve this problem, 802.11 specifies an optional Request to Send/Clear to Send (RTS/CTS) protocol at the MAC layer. When this feature is in use, a sending station transmits an RTS and waits for the access point to reply with a CTS. Since all stations in the network can hear the access point, the CTS causes them to delay any intended transmissions, allowing the sending station to transmit and receive a packet acknowledgment without any chance of collision. Since RTS/CTS adds additional overhead to the network by temporarily reserving the medium, it is typically used only on the largest-sized packets, for which retransmission would be expensive from a bandwidth standpoint.

Finally, the 802.11 MAC layer provides for two other robustness features: CRC checksum and packet fragmentation. Each packet has a CRC checksum calculated and attached to ensure that the data was not corrupted in transit. This is different from Ethernet, where higher-level protocols such as TCP handle error checking. Packet fragmentation allows large packets to be broken into smaller units when sent over the air, which is useful in very congested environments or when interference is a factor, since larger packets have a better chance of being corrupted. This technique reduces the need for retransmission in many cases and thus improves overall wireless network performance. The MAC layer is responsible for reassembling fragments received, rendering the process transparent to higher-level protocols.

- Association

The 802.11 MAC layer is responsible for how a client associates with an access point. When an 802.11 client enters the range of one or more APs, it chooses an access point to associate with (also called joining a Basic Service Set), based on signal strength and observed packet error rates. Once accepted by the access point, the client tunes to the radio channel to which the access point is set. Periodically it surveys all 802.11 channels in order to assess whether a different access point would provide it with better performance characteristics. If it determines that this is the case, it reassociates with the new access point, tuning to the radio channel to which that access point is set (Figure 4).

Figure 4. Access Point Roaming

Reassociation usually occurs because the wireless station has physically moved away from the original access point, causing the signal to weaken. In other cases, reassociation occurs due to a change in radio characteristics in the building, or due simply to high network traffic on the original access point. In the latter case this function is known as “load balancing,” since its primary function is to distribute the total WLAN load most efficiently across the available wireless infrastructure. This process of dynamically associating and reassociating with APs allows network managers to set up WLANs with very broad coverage by creating a series of overlapping 802.11b cells throughout a building or across a campus. To be successful, the IT manager ideally will employ “channel reuse,” taking care to set up each access point on an 802.11 DSSS channel that does not overlap with a channel used by a neighboring access point (Figure 5). As noted above, while there are 14 partially overlapping channels specified in 802.11 DSSS, there are only three channels that do not overlap at all, and these are the best to use for multicell coverage. If two APs are in range of one another and are set to the same or partially overlapping channels, they may cause some interference for one another, thus lowering the total available bandwidth in the area of overlap.

Figure 5. Unlimited Roaming

- Security

802.11 provides for both MAC layer (OSI Layer 2) access control and encryption mechanisms, which are known as Wired Equivalent Privacy (WEP), with the objective of providing wireless LANs with security equivalent to their wired counterparts. For the access control, the ESSID (also known as a WLAN Service Area ID) is programmed into each access point and is required knowledge in order for a wireless client to associate with an access point. In addition, there is provision for a table of MAC addresses called an Access Control List to be included in the access point, restricting access to clients whose MAC addresses are on the list.

For data encryption, the standard provides for optional encryption using a 40-bit shared-key RC4 PRNG algorithm from RSA Data Security. All data sent and received while the end station and access point are associated can be encrypted using this key. In addition, when encryption is in use, the access point will issue an encrypted challenge packet to any client attempting to associate with it. The client must use its key to encrypt the correct response in order to authenticate itself and gain network access. Beyond Layer 2, 802.11 HR WLANs support the same security standards supported by other 802 LANs for access control (such as network operating system logins) and encryption (such as IPSec or application-level encryption). These higher-layer technologies can be used to create end-to-end secure networks encompassing both wired LAN and WLAN components, with the wireless piece of the network gaining unique additional security from the 802.11 feature set.

- Conclusion

802.11 WLANs are already commonly used in several large vertical markets. The 802.11b standard is the first standard to make WLANs usable in the general workplace by providing robust and reliable 11 Mbps performance, five times faster than the original standard. The new standard will also give WLAN customers the freedom to choose flexible, interoperable solutions from multiple vendors, since most major networking and personal computer vendors have endorsed it. Broad manufacturer acceptance and certifiable interoperability means users can expect to see affordable, high-speed wireless solutions proliferate throughout the large enterprise, small business, and home markets. This global wireless LAN standard opens exciting new opportunities to expand the potential of network computing.

- References

http://www.wlana.com

http://www.zdnet.com

http://www.proxim.com

http://www.nwfusion.com

http://www.slac.stanford.edu

http://www.ecompany.com

http://standards.ieee.org