## Slide 1: Decoding Human Movement Using Wireless Sensors
  Michael Baswell
  CS525 Semester Project
  Spring 2006

## Slide 2: Introduction & Background
Goal: to measure human body
  movement and, ultimately, to
  create a formal language
  describing this motion.
Not a new idea, but new tech-
  nologies may allow better/more accurate results
Wireless sensors are small enough to be wearable; can they be useful in this research?
This presentation focuses on ideas for an experiment in using cricket motes to measure movement

## Slide 3: Similar Technologies
Camera/Marker systems – LotR/Gollum
Markers can be
  Visual (cameras track movement)
  Electromagnetic
  Inertial sensors
Drawbacks:
  Line-of-sight
  Surrounding environment can cause interference & errors
  COST! Proprietary Systems can run $30-40 thousand or more.

## Slide 4: Cricket Indoor Location System
accuracy 1-3 cm
Based on Mica2 platform, but adds ultrasound
Beacons broadcast an RF indentifier signal, and at the same time emit an ultrasonic “chirp”
Passive listeners measure the time lapse between the two, and compute distance to that beacon
  RF propagates at speed of light
  Ultrasound propagates at speed of sound

## Slide 5: Cricket Limitations
Up to 15 beacons supported
Default config is too slow – up to 1.34 sec per broadcast/chirp.
  Assuming 6 beacons, we need to be about 100x faster!
Due to limited range from beacons, large movements may not be capturable (think about a ballet leap)
Due to these limitations, additional sensors such as flex sensors or inertial sensors, may need to be integrated into the system as well

## Slide 6: Additional Sensors
Flex Sensors can detect up to 90-degree bend
Interface with Mica2Dot, which can broadcast measurements at intervals
Mica2Dot sensors also include 2-dimension accelerometer and tilt sensors

## Slide 7: Experimental Design & Integration
Note: this has NOT been tested or simulated!
Requirements:
  At least 4 beacons, preferably more – up to 15! - distributed around test area. These should be spread out both above and below the subject, depending on the movement being monitored.
  1 listener attached to each key joint being monitored – i.e. Wrist, elbow, shoulder
  Flex sensors / Mica2Dots if appropriate (i.e., for an arm motion involving bend at the elbow)

## Slide 8: Experimental Design & Integration (continued)
Beacons should be synchronized to avoid collision. This will increase the number of useful broadcasts per second.
Listeners (and Dot motes, if applicable) should also be sync'ed to broadcast their readings at intervals; this should be fairly trivial, as the RF broadcast is much faster than the ultrasound chirp
We want ~10 readings per second per beacon, plus time for each listener to report results twice per second.

## Slide 9: Cricket Config Screen

## Slide 10: Cricket Beacon Readings
Assuming up to 10 meters distance from beacon, 10 bits per distance reading (in cm), 50 bits total plus ID for beacon (can be encoded to 4 bits).
~50 microseconds per bit * 54 bits = 2700 microseconds, or 2.7 ms.
We could encode by change, similar to Jpeg / VLI encoding, but why?
Depending on the movement, there might be a small gain.

## Slide 11: Cricket In Action
Videos online at Cricket web site
http://cricket.csail.mit.edu/
Tracking a moving train
Auto-configuring robots (Roomba video)

## Slide 12: Summary
For the goal of this project, we need highly accurate, quick measurements
Cricket is good, but there is room for improvement still
May need to use a hybrid system:
  cricket sensors plus cameras/markers?
  Flex sensors?
May need to focus on smaller movements or individual body parts
Further development of this platform may remove some of the limitations

## Slide 13: References
http://cricket.csail.mit.edu/
http://www.cs.berkeley.edu/%7Ekamin/localization.html
Yifei Wang, “Human movement tracking using a wearable wireless sensor network,” Masters Thesis, Iowa State University, 2005
Cricket v2 User Manual, Cricket Project, MIT Computer Science and Artificial Intelligence Lab, January 2005
Hari Balakishnan, Roshan Baliga, Dorothy Curtis, Michel Goraczko, Allen Miu, Bodhi Priyantha, Adam Smith, Ken Steele, Seth Teller, Kevin Wang, “ Lessons from Developing and Deploying the Cricket Indoor Location System,” MIT Computer Science and Artificial Intelligence Laboratory (CSAIL), November 2003