## Slide 1: Voice Over IP and Security
By Thao L. Pham
CS 525

## Slide 2: What is VoIP?
Inexpensive phone service using the internet which transforms analog signals into digital signals for transmission over the internet.

## Slide 3: VoIP call Flow
Analog to Digital
Converter
Data Compression
RTP Packets
UDP Packets
internet

## Slide 4: VoIP Components
The IP networks: supports VoIP technology, ensures smooth transmission and prioritize packets accordingly.
The call processor or controllers: setup calls, authorize users, calling plans and other basic telephone features (holding, transferring,etc.)
The media or signaling gateways: call initiation, detection, analog to digital conversion.
The subscriber terminals: provide real time communication, can be desk phone or soft phone.

## Slide 5: H.323
H.323 (includes H.325 & H.245):
specifies a standardized infrastructure consists of four major components:
Terminals: provides real time communication
Gateways: placed between circuit-switch network and IP network.
Gatekeepers: provides call management functions, address resolution and bandwidth control.
Multipoint Control Units: conferencing multiple connections.

## Slide 6: H.323 Architecture

## Slide 7: Session Initiation Protocol
Discussed in another project on Wednesday

## Slide 8: Security Issues
VoIP network be separated from data network: using logical address and subnet division, virtual LAN zoning.
ACL, IP filtering and VLAN be implemented where there need to be a link between data segment and IP segment.
Implement stateful firewalls: remembers traffic information in the header when filtering packets (for dynamic ports application). IP Soft phone be placed behind stateful firewalls.
Use IPsec tunneling mode : encryption at header and datagram.

## Slide 9: Security Issues (cont)
IPsec AH is incompatible with NAT : address behind NAT are masked -> Encapsulating IPsec packet in a new UDP packet.
Use SRTP: offers encryption, authentication and periodic refreshment of session keys.
Implement strict ACL at gateways.
Implement NAT behind firewalls: issues with incoming call.
  Application Level Gateway on firewalls -> associate with overhead.
  Middle boxes-> have the same risks as a traditional box.

## Slide 10: Conclusion
While VoIP is still maturing, companies are concerned about quality, latency and interoperability, many overlook security issues
If not implemented properly, VoIP could lead to serious privacy violation and unwanted solicitation over IP telephones.