## Slide 1: Multimedia Communications and Firewall/NAT
CS525
By
Saroj Patil

## Slide 2: Objective
H.323 - Packet-Based Multimedia Communications Systems
Problems penetrating firewall and establishing connection with endpoint behind firewall
H.460.17/18/19

## Slide 3
H.323 Family of protocols –

## Slide 4: H.323 Call Setup

## Slide 5: Problems Posed by Firewall / NAT
Problem 1 : Q.931 SETUP message blocked by Firewall

## Slide 6: Problems Posed by Firewall / NAT
Problem 2 : NAT hides internal endpoint address by replacing it with public address of firewall.

## Slide 7: Solution
Three approved standards –
H.460.17,
H.460.18,
H.460.19

## Slide 8: H.460.17
RAS over H.225
A single TCP connection between endpoint and a gatekeeper
Addresses of RAS, Q931 and H.245 need not pass through – The messages are tunneled over the single TCP connection

## Slide 9: H.460.18
Instead of tunneling, use of separate pinholes and extra signaling

## Slide 10: H.460.19
Modified RTP/RTCP versions
Outgoing keep-alive messages (RTP packets with empty payload) open pinhole for incoming RTP
Outgoing RTCP packets open pinhole for incoming RTCP packets (RTCP is bi-directional)

## Slide 11: Vendors
Tandberg
  Border Controller = GK + H.460.18/19 Server
  MXP endpoints include H.460.18/19 Client
Polycom
  V2IU servers and VSX endpoints will support H.460.18/19 in Q2/2006
Radvision
  PathFinder solution will support H.460.18/19 (Client/Server)

## Slide 12: Conclusion
H.460.18/19 is the accepted standard for H.323 FW/NAT traversal

## Slide 13: References :
http://en.wikipedia.org/wiki/H.323
http://en.wikipedia.org/wiki/Q.931
http://www.chebucto.ns.ca/~rakerman/articles/ig-h323_firewalls.html
http://www.h323forum.org/papers/301005_Firewall_NAT_Traversal_White_Paper.pdf
http://vide.net/conferences/spr2006/slides/schlatter_h460.pdf