## Slide 1: Mobile Ad hoc Network: Secure Issues In Multi-Hop Routing Protocols
Presented By PHILIP HUYNH
CS591-F2009

## Slide 2: Mobile Ad hoc Network: Architecture
An autonomous, self-configuring system of mobile devices (laptops, smart phones, sensors, etc.) connected by wireless links
Each node operates as both an end-system and a router
MANET characteristics:
  Mobility and dynamic topology
  Bandwidth-constrained
  Energy-constrained
  Prone to security threats

## Slide 3: Mobile Ad hoc Network: Applications
Notes: Mobile ad hoc networks were initially designed for military applications, but with the increase of portable devices as well as progress in wireless communication, MANET is gaining importance with increasing number of applications. It can be used for emergency and rescue operation, conferences and campus settings, airport and car networks and other more.

## Slide 4: Multi hop Routing Protocols
Topology-based protocols
  Proactive
    distance vector based (e.g., DSDV)
    link-state (e.g., OLSR)
  Reactive (on-demand)
    distance vector based (e.g., AODV)
    source routing (e.g., DSR)
Position-based protocols
    Greedy forwarding (e.g., GPSR, GOAFR)
    Restricted directional flooding (e.g., DREAM, LAR)
Hybrid approaches
Notes: Classification of ad hoc network routing protocols. Topology-based protocols are based on traditional routing concepts, such as maintaining routing tables or distributing link-state information, but they are adapted to the special requirements of mobile ad hoc networks. Position-based protocols use information about the physical locations of the nodes to route data packets to their destinations. Topology-based protocols can be proactive or reactive. Proactive protocols try to maintain consistent, up-to-date routing information within the system. In contrast to this, reactive protocols establish a route between a source and a destination only when it is needed. For this reason, reactive protocols are also called on-demand protocols.

## Slide 5: Dynamic Source Routing (DSR)
Notes: Example: Dynamic Source Routing (DSR)
On-demand source routing protocol
Two components:
  Route discovery
    Use only when source S attempts to send a packet to destination D
    Based on flooding of Route Request (RREQ) and returning Route Replies (RREP)
  Route maintenance
    Makes S able to detect route errors (e.g., if a link along that route no longer works)

## Slide 6: Attack Mechanisms
Notes: Eavesdropping, Replaying, Modifying, and Deleting Control Packets
Fabricating control packets containing fake routing information (forgery)
Fabricating control packets under a fake identity (spoofing)
Dropping data packets (attack against the forwarding function)
Wormholes and tunneling
Rushing

## Slide 7: Attack Mechanisms(2)
Notes: Eavesdropping, Replaying, Modifying, and Deleting Control Packets
Fabricating control packets containing fake routing information (forgery)
Fabricating control packets under a fake identity (spoofing)
Dropping data packets (attack against the forwarding function)
Wormholes and tunneling
Rushing

## Slide 8: Route Disruption
wormhole
source
destination
ROUTE DISRPUTION IN DSR WITH RUSHING; THE ADVERSARY DROPS ALL ROUTE REPLIES (RREP) CONTROL PACKETS.
Notes: The adversary prevents a route from being discovered between two nodes that are otherwise connected
The primary objective of this attack is to degrade the quality of service provided by the network
  The two victims cannot communicate, and
  Other nodes can also suffer and be coerced to use suboptimal routes
Attack mechanisms that can be used to mount this attack:
  Dropping route request or route reply messages on a vertex cut
  Forging route error messages
  Combining wormhole/tunneling and control packet dropping
  Rushing

## Slide 9: Route Diversion
wormhole
source
destination
ROUTE DIVERSION IN DSR WITH RUSHING; THE ADVERSARY CAN EAVESDROP OR MODIFY DATA PACKETS.
Notes: Due to the presence of the adversary, the protocol establishes routes that are different from those that it would establish, if the adversary did not interfere with the execution of the protocol
The objective of route diversion can be
  To increase adversarial control over the communications between some victim nodes
    The adversary tries to achieve that the diverted routes contain one of the nodes that it controls or a link that it can observe
    The adversary can eavesdrop or modify data sent between the victim nodes easier
  To increase the resource consumption of some nodes
    Many routes are diverted towards a victim that becomes overloaded
  Degrade quality of service
    By increasing the length of the discovered routes, and thereby, increasing the end-to-end delay between some nodes
Route diversion can be achieved by
  Forging or manipulating routing control messages
  Dropping routing control messages
  Setting up a wormhole/tunnel

## Slide 10: Creation of Incorrect Routing State
CREATION OF INCORRECT ROUTING STATE IN DSR; THE ADVERSARY SENDS THE FAKE ROUTE REPLIES (RREP).
Notes: This attack aims at jeopardizing the routing state in some nodes so that the state appears to be correct but, in fact, it is not
  Data packets routed using that state will never reach their destinations
The objective of creating incorrect routing state is
  To increase the resource consumption of some nodes
    The victims will use their incorrect state to forward data packets, until they learn that something goes wrong
  To degrade the quality of service
Can be achieved by
  Spoofing, forging, modifying, or dropping control packets

## Slide 11: Generation of Extra Control Traffic
Injecting spoofed control packets into the network
Aiming at increasing resource consumption due to the fact that such control packets are often flooded in the entire network

## Slide 12: Setting Up a Gray Hole
wormhole
source
destination
ROUTE DIVERSION IN DSR WITH RUSHING; THE ADVERSARY SELECTIVELY DROPS DATA PACKETS.
Notes: An adversarial node selectively drops data packets that it should forward
The objective is
  To degrade the quality of service
    Packet delivery ratio between some nodes can decrease considerably
  To increase resource consumption
    Wasting the resources of those nodes that forward the data packets that are finally dropped by the adversary
Implementation is trivial
  Adversarial node participates in the route establishment
  When it receives data packets for forwarding, it drops them
  Even better if combined with wormhole/tunneling

## Slide 13: Countermeasures
Notes: Authentication of control packets
  Using MACs or digital signatures
Protection of mutable information in control packets
  Using MACs or digital signatures
  Often complemented with the use of one-way hash functions
Detecting wormholes and tunnels
Combating gray holes
  Using multi-path routing
  Using a “detect and react” approach

## Slide 14: Secure Routing Protocol (SRP)
A  * : [RREQ, A, H, id, sn, macAH, ()]
B  * : [RREQ, A, H, id, sn, macAH, (B)]
C  * : [RREQ, A, H, id, sn, macAH, (C)]
D  * : [RREQ, A, H, id, sn, macAH, (D)]
E  * : [RREQ, A, H, id, sn, macAH, (E)]
F  * : [RREQ, A, H, id, sn, macAH, (E, F)]
G  * : [RREQ, A, H, id, sn, macAH, (D, G)]
H  A : [RREP, A, H, id, sn, (E, F), macHA]
A
B
C
E
F
G
H
macAH: Message Authentication Code covering RREQ, A, H, id, and sn
Notes: SRP is a secure variant of DSR
Uses symmetric-key authentication (MACs)
  Due to mobility, it would be impractical to require that the source and the destination share keys with all intermediate nodes
  Hence there’s only a shared key between the source and the destination
  Only end-to-end authentication is possible
  No optimizations
SRP is simple but it does not prevent the manipulation of mutable information added by intermediate nodes
  This opens the door for some attacks
  Some of those attacks can be thwarted by secure neighbor discovery protocols

## Slide 15: Some Secure Ad hoc Network Routing Protocols
SRP (on-demand source routing)
Ariadne (on-demand source routing)
endairA (on-demand source routing)
S-AODV (on-demand distance vector routing)
ARAN (on-demand, routing metric is the propagation delay)
SEAD (proactive distance vector routing)
SMT (multi-path routing combined error correcting)
Watchdog and Pathrater (implementation of the “detect and react” approach to defend against gray holes)
ODSBR (source routing with gray hole detection)

## Slide 16: Simulation
Multi hop routing attack – Gray hole
Using TinyOS, TOSSIM, TinyViz

## Slide 17: Simulation