## Slide 1: IPV6 SECURITY
By Rod Lykins

## Slide 2: OVERVIEW
Background
Benefits
Security Advantages
  Address Space
  IPSec
Remaining Security Issues
Conclusion

## Slide 3: IPv6 BACKGROUND
Originally created due to foreseeable lack of Internet address space…
  1979: 32-bit IPv4 provided 4.3 billion IP addresses
  1990: 128-bit IPv6 development started by IETF
  1998: IPv6 (RFC 2460) standard initially published
Address Space: 3.4 x 1038 IP addresses
  Or 340,282,366,920,938,463,463,374,607,431,768,211,456
  Earth = 4.5 billion years old; 100 trillion/second = 0.00000417% of used address space
IPv4 Address Depletion Slowed By:
  Variable Length Subnet Masks (VLSMs)
  Classless Inter-Domain Routing (CIDR)
  Network Address Translation (NAT)

## Slide 4: IPv6 BENEFITS
Other than increased address space…
  New Header Format
    Designed to minimize header overhead, which provides more efficient processing
    Note: IPv4 headers and IPv6 headers are not interoperable and the IPv6 protocol is not backward compatible with the IPv4 protocol
  Efficient and Hierarchical Addresses
    Backbone routers have much smaller routing tables
  Stateless and Stateful Address Configuration
    Address configuration with or without a DHCP server
  Better Support for Quality of Service (QoS)
    “Flow Label” in IPv6 Header – even when packet payload is encrypted with IPSec
  Better Security…

## Slide 5: SECURITY ADVANTAGES
Large Address Space
  Default Subnet Size = 264 addresses
    Scan 1,000,000 addresses / sec = > 500,000 year to scan
  Other Avenues for Attackers…
    Advertised: Mail Servers, Web Servers, etc.
    DNS Zone Transfers
    Logfile Analysis
    Applications
    Multi-cast Group Addresses
    During Transition (6to4)
IPSec
  Provides these Layer 3+ security features…
    Confidentiality: IPSec traffic is encrypted…captured IPSec traffic cannot be deciphered without encryption key
    Authentication: IPSec traffic is digitally signed with the shared encryption key so receiver can verify it was sent by IPSec peer
    Integrity: IPSec traffic contains cryptographic checksum that incorporates the encryption key…the receiver can verify the packet was not modified in transit

## Slide 6: IPSec (cont’d)
Two Major Protocols
  Authentication Header (AH)
    Similar to a CRC or CheckSum
      Dependent on selected shared key, hash function, mode (tunnel or transport), and network (IPv4 or IPv6)
    Provides integrity and authentication, but not confidentiality
  Encapsulating Security Payload (ESP)
    Provides integrity, authentication, and confidentiality

## Slide 7: IPSec (cont’d)
Two Modes of Operation
  Transport
    Only the actual payload of the IP packet is encrypted (i.e., the destination and source IP addresses, port numbers, and other IP header information is still readable
  Tunnel
    The entire IP packet is encrypted and then placed into an IPSec endpoint where it is encapsulated inside another IP packet.
Wide Range of Crypto Choices
  MD5, SHA-1, DES, 3DES, AES…
Most, if not all, successful IPSec exploitation attacks are side-channel attacks
  Poor Key Management (i.e., IKE Aggressive Mode)
  Unsecure Passwords, etc.

## Slide 8: SECURITY ISSUES
Attack Vectors
  IPSec relies on key exchanges
  Neighbor Discovery Spoofing
  DoS and DDoS attacks
  Application Layer attacks

## Slide 9: IPv6 IMPLEMENTATION
Dual-Stack
    Simplest method
Tunnel IPv6 via IPv4
Translation IPv6 to IPv4

## Slide 10: SOURCES
www.ietf.org
www.IPv6.com
Microsoft TechNet
CompTIA Network+

## Slide 11: QUESTIONS?