## Slide 1
Network Monitoring as a Layer of Security
CS 691 Advanced System Security Design
University of Colorado – Colorado Springs
July 28th 2009
Jeff Miller

## Slide 2: Introduction
Overview
  “Your doctor is watching for danger signs as blood flows through vessels, valves and chambers of the heart, while your network monitoring systems are tracking data moving along cables and through servers, switches, connections and routers.”
    – CIO magazine
Basic Definition
  A vital activity where one or more computers monitor network traffic, infrastructure devices, and other computer systems. The system notifies administrators with alerts (email, pager, cell phone, etc.) when a problem exists.

## Slide 3: Introduction Continued
What it is
  A system that collects data and alerts the admin when other systems or services are unavailable, or when a predefined threshold is reached (system resources, bandwidth usage, etc.)
What it isn’t
  Network Monitoring is not an Intrusion Prevention System (IPS) or Intrusion Detection System (IDS)
Critical Availability
  Always On – dedicated power, ePower (generator) ideal at a minimum battery backup system

## Slide 4: Practical Application
  Smart Grid
Internet Service Providers (ISPs)
Large Corporations
Hospitals
Military Networks
Everyone!?! Why not?

## Slide 5: Monitoring Techniques
Passive
  SNMP – Protocol for communicating – most basic and most popular
    Device based
    Limited information gathered
    Management Information Base (MIB)
    Monitor and Agents(s)
  RMON – requires more expensive hardware (more cpu cycles, memory, etc.)
    Flow based
    Specific SNMP MIB
    Console and Probe(s)
  Netflow – developed by CISCO – Juniper Network has JFlow
    Collector and probe(s)
  Traffic Sniffers
Active
  Generate and injection of test packets into the network. Test data send to devices, servers, and or applications. Volume of traffic is fully adjustable.
  Good way to test Service Level Agreements (SLAs)

## Slide 6: SNMP
Management Information Base (MIB)
  Hierarchical collection of information that is accessed using SNMP
  Comprised of managed objects
  Follow Internet Engineering Taskforce (IEFT) and IEEE standards

## Slide 7: MIB Tree
Example: Oracle Database MIB

## Slide 8: MIB Tree
Example: 3Com Network
Device MIB

## Slide 9: Monitoring via SNMP

## Slide 10: Benefits
No IDS, IPS, or Firewall guaranteed to prevent or detect all attacks
The more information we have about our network the easier we can identify potential problems and get alerts when something bad happens
General Benefits
  Spot overloaded equipment before it can bring down a network
  Help determine employee productivity
  Identify weak wide-area-network links and other bottlenecks
  Measure latency or the delayed transfer of data
  Provides executives the ammo they need to justify network upgrades
  Prove SLA are being met
Security Considerations
  Detect anomalous internal traffic that might indicate a security threat such as a DDOS attack
  Detect overloaded systems, crashed servers, lost network connections, virus or malware infections, and power outages

## Slide 11: Network Monitoring Solutions
Commercial – hardware appliances, software solutions and even outsourced service solutions (range from thousands to hundreds of thousands of dollars).
  HP OpenView – $$$
  CISCOWorks - $$$
  SolarWinds Orion - $$
  OpManager - $
  WhatsUpGold - $
  PRTG - $
Open Source - innovative, inexpensive, and numerous – everyone likes free! – (limited support – more difficult to setup)
  Nagios – (free with optional support license)
  MRTG

## Slide 12: Test Bed
Nagios 3.1.2
  Open Source / GPL / Free
  Network services like smtp, http, dns, and ftp can be easily monitored without the use of client add-ons
3 Part Setup
  Core
  Plugins
    NSClient++
  Add-ons
    Perl scripts, MIB info, etc.

## Slide 13: NSClient++
NSClient++
  Easily monitor hosts, devices, services, protocols, and applications with Nagios

## Slide 14: Test Bed
Network Management System
  Ubuntu Desktop 9.04
  Apache 2
  PHP 5
  GCC Compiler and development libraries
  GD graphics library
  Nagios 3.1.2 source code - sourceforge
Sample Clients
  Linux Server, 2 XP Laptops, 1 Networked Printer, 1 Linux Router/Switch

## Slide 15: Test Bed Continued…

## Slide 19: Linksys WRT54GS – DD-WRT
CPU check
  define command{ command_name check_linksys_cpu command_line $USER1$/check_snmp -H $HOSTADDRESS$ -C public -o 1.3.6.1.4.1.2021.10.1.5.1 -u % - w 60 -c 70 }
RAM check
  define command{ command_name check_linksys_ram command_line $USER1$/check_snmp -H $HOSTADDRESS$ -C public -o 1.3.6.1.2.1.25.2.3.1.6.101 -u kb -w 27000 -c 28000 }

## Slide 20: Conclusion
Nagios as a monitoring solution
  Large company with a big budget - commercial product would be easy to configure and support
  Small to medium size company with a limited budget and enjoy the flexibility to completely customize your solution consider Nagios or another OpenSource/GPL product
    Requires Linux knowledge
    Requires more in-depth configuration and possibly custom coding to support specific devices
In general I would recommend a monitoring solution as an extra layer of security for any network
  ROI analysis – costs will drive the solution

## Slide 21: References
[1] CIO Magazine (5 Jun 2009) Network Monitoring Definition and Solutions. Retrieved Jul 13, 2009 from http://www.cio.com/article/133700/Network_Monitoring_Definition_and_Solutions
[2] Ipswitch (14 Nov 2007) White Paper: THE VALUE OF NETWORK MONITORING: Why It’s Essential to Know Your Network. Retrieved Jul 29, 2009 from http://www.whatsupgold.com/resources/whitepapers/Value_of_Network_Monitoring.pdf
[3] Landis +Gyr (2009) White Paper: Securing the Smart Grid: Gridstream Security Architecture. Retrieved June 6, 2009 from http://www.landisgyr.com/en/pub/home.cfm
[4] EMS Satcom (2008) Blue Force Tracking: System Nuances and EMS SATCOM’s Contributions. Retrieve Jul 20, 2009 from http://www.emssatcom.com/newsletters/2008/Nov/bus2.aspx
[5] Stanford SLAC (11 Mar 2001) Passive vs. Active Monitoring. Retrieved Jul 13, 2009 from http://www.slac.stanford.edu/comp/net/wan-mon/passive-vs-active.html
[6] TCPIP Guide (?) SNMP MIB Graphic. Retrieved Jul 29, 2009 from www.tcpipguide.com
[7] HP Website
[8] Wikipedia (27 Jul 2009) Comparison of network monitoring systems. Retrieved Jul 29, 2009 from http://en.wikipedia.org/wiki/Comparison_of_network_monitoring_systems
[9] Nagios (2009) Nagios. Retrieved July, 13 2009 from http://www.nagios.org/
[10] NSClient++ () Installing NSClient++. Retrieved July 23, 2009 from http://nsclient.org/nscp/
[11] Nagios () Nagios Quickstart Installation Guides. Retrieve July 23, 2009 from http://nagios.sourceforge.net/docs/3_0/quickstart.html