# Secure Collective Internet Defense (SCID)
A midterm report submitted to
Network Information and Space Security Center (NISSC) 
for Summer 2003

C. Edward Chow
Yu Cai

David Wilkinson

1. Project Goal

The objective of this project is to create a secure collective internet defense system (SCID) that utilizes new cyber security defense techniques. SCID will push back intrusion attacks using an enhanced Intrusion Detection System and Isolation Protocol (IDIP) among a set of routers, and tolerate Distributed Denial of Services (DDoS) attacks with secure Domain Name System (DNS) updates, and alternate routes via a set of proxy servers with intrusion detection.

2. Project Status

So far, we have reached two significant milestones in the SCID project:

a) Developed client side indirect routing by setting up IP tunnels.

We have investigated several alternatives for implementing indirect routing. The alternatives include Zebedee [1], SOCKS proxy server [2], and IP tunnel [3]. The advantage of using IP tunnel is that it is a layer three protocol; therefore all the upper layer protocols and applications can use it. Second, IP tunnel is installed with Redhat 8 and 9 by default, and setting up IP tunnel doesn’t require additional software installation or kernel compilation.

We have successfully set up IP tunnels among machines running either Linux (Redhat 8 or 9) or Windows (2000 server version). The configuration can be Linux to Linux, Windows to Windows, or between Linux and Windows. We almost finished implementing a demon process running on client machine / proxy server / alternate gateway, listening to a certain port, waiting for message from a SCID coordinator, and setting up IP tunnel automatically. We are working on enhancing the resolver library on Linux so that the setup of the IP tunnel will be automatically and transparent to client. All the communications between the client and the SCID coordinator will be based on SSL connections, encrypted and mutually authenticated.

b) Extended Bind9 DNS server software package to include indirect routing entries.

When a client queries the modified DNS server, the client will get a DNS record with multiple proxy server IP addresses in addition to ordinary domain name and IP address mapping information. An indirect route can then be setup on client machine through the selected proxy server. We are working on using SSL to authenticate and encrypt the communication between DNS server and the SCID coordinator.

Details of the IP tunnel setup and configuration, Bind9 software package modification and extension, and preliminary performance test and result analysis for SCID project are included in a full report at http://cs.uccs.edu/~scid/scid_midterm_report.doc.

3. References

1. Zebedee Secure IP tunnel, http://www.winton.org.uk/zebedee/

2. SOCKS proxy server, http://www.tldp.org/HOWTO/Firewall-HOWTO-11.html

3. IPIP tunnel, http://www.europe.redhat.com/documentation/HOWTO/Net-HOWTO/x1284.php3

4. IP tunnel kernel compilation, http://www.redhat.com/docs/manuals/linux/RHL-9-Manual/custom-guide/s1-custom-kernel-modularized.html

5. DNS BIND 9, http://www.isc.org/products/BIND/

6. VS FTP Server, http://www.siliconvalleyccie.com/linux-hn/ftp-server.htm

7. Edward. Chow, “Security Related Research Projects at UCCS network research lab”, http://cs.uccs.edu/~Echow/research/security/uccsSecurityResearch.ppt, 2002

8. DNS and BIND, http://www.oreilly.com/catalog/dns4/chapter/ch11.html

9. Linux IP tunnel, http://www.europe.redhat.com/documentation/HOWTO/Adv-Routing-HOWTO-5.php3

10. SCID proposal to NISSC, http://cs.uccs.edu/~scid/doc/SCID_Proposal_to_NISSC.doc

11. SCID mid term report to NISSC (full version), http://cs.uccs.edu/~scid/doc/scid_midterm_report.doc